| INPUT CONTRIBUTION |
| --- |
| Group Name:* | PRO # 11.9 |
| Title:* | notification procedure for subscription |
| Source:* | LG Electronics |
| Contact: | Heedong Choi, heedong.choi@lge.com |
| Date:* | 2014-07-16 |
| Abstract:* | notification procedure for subscription |
| Agenda Item:* | PRO |
| Work item(s): | WI 0009 |
| Document(s) Impacted* | oneM2M-TS-0004 Core Protocol TS |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the text into the TS. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

============================Start of 1st Change==============================

## 7.X.X.X Notification for Subscription

Originator: When an event is generated, the Originator shall execute the following steps in order:

Editor’s Note: The attribute name of this section needs to check the consistency with ARC TS.

Step 1.0	Check the eventNotificationCriteria attribute:

If the eventNotificationCriteria attribute is set, then the Originator shall check whether the corresponding event matches with the event criteria. In that case, go to the step 2.0. Otherwise, the Originator shall discard the corresponding event

If the eventNotificationCriteria attribute is not configured, then continue with the step 2.0

Step 2.0	The Originator shall check the notification policy as described in the below steps, but the notification policy may be checked in the different order. After checking the notification policy in the step 2.x (i.e., from the step 2.1to the step 2.6), then continue with the step 3.0

Step 2.1	The Originator shall determine the type of the notification per notificationContentType attribute.

Step 2.2	Check the notificationEventCat attribute:

If the notificationEventCat attribute is set, the notification shall have the ec set to the notificationEventCat attribute. Then continue with other step

If the notificationEventCat attribute is not configured, it shall be determined as a default value by the CMDH policy. Then continue with other step

Step 2.3	Check the rateLimit attribute:

Step 2.4	Check the batchNotify attribute:

Step 2.5	Check the latestNotify attribute:

Step 2.6	Check the preSubscriptionNotify attribute:

Step 3.0	The Originator shall check the notification and reachability schedules, but the notification schedules may be checked in the different order.

If the notificationSchedule resource is set, then the Originator shall check the time periods by using the scheduleElement attribute.

Also, the Originator shall check the reachability schedule associated with the Receiver by using the <schedule> resource. If reachability schedules are not present in a Node then that Node is considered to be always reachable

If the notificationSchedule and reachability schedule are allowed, then go to the step 4.0. Otherwise, go to the step 5.0

Step 4.0	Check the pendingNotification attribute:

If the pendingNotification attribute is set, then the Originator shall cache pending notifications according to the pendingNotification. The possible values are ‘sendLatest’ and ‘sendAllPending’. If the value of pendingNotification is set to ‘sendLatest’, the most recent notification is cached in the Originator. If it is set to ‘sendAllPending’, all notifications are cached in the Originator. Then end the notification procedure

If the pendingNotification attribute is not configured, the Originator shall discard the corresponding notification. Then end the notification procedure

The processed notification by the pendingNotification is sent to the Receiver after the reachability recovery (see the step 7.0)

Step 5.0	Check the expirationCounter attribute:

If the expirationCounter attribute is set, then the expirationCounter shall be decreased by one when the Originator successfully sends the notification request to Receiver(s). If the counter meets zero, the corresponding subscription resource is deleted. Then end the notification procedure

If the expirationCounter attribute is not configured, then end the notification procedure

Originator: After reachability recovery, the Originator shall execute the following steps in order:

Step 6.0	The Originator shall send the processed notification by the pendingNotification attribute, then continue with the step 7.0

Step 7.0	Check the expirationCounter attribute:

If the expirationCounter attribute is set, then the expirationCounter shall be decreased by one when the Originator successfully sends the notification request to Receiver(s). If the counter meets zero, the corresponding subscription resource is deleted. Then end the notification procedure

If the expirationCounter attribute is not configured, then end the notification procedure

=============================End of 1st Change==============================