| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG3 |
| Title:* | Correction of the parameters at the Device Triggering commands |
| Source:* | Qi Yu, Huawei, yuqi@huawei.com |
| Contact: | <name>, <company>, <contact info> (if different to the source) |
| Date:* | 2014-07-15 |
| Abstract:* | At the Device Triggering commands, some AVPs are optional, the others are mandatory according to 3GPP TS 23.368. Some parameters are missing at Device Action Answer, Device Notification Request and Device Notification Answer commands. This contribution intends to correct the above issues. |
| Agenda Item:* | Core Protocol TS |
| Work item(s): | WI-0009 |
| Document(s) Impacted* | TS-0004v0.5.3 Annex B |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Member should agree on proposed changes. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

This contribution intends to add a column to indicate the optionality.  The missing parameters are also been added.

----- Start of change 1----

Annex B (normative):
Device Triggering

B.1 Providing Device Triggering service by means of 3GPP networks

B.1.1 Introduction

3GPP Underlying Network has defined a dedicated interface for requesting device triggering. The normative references for applicable interfaces are as follows: 3GPP TS 23.682 [15]. The specification for the interface Tsp is described in 3GPP TS 29.368 [16]. Tsp interface uses Diameter Base Protocol as specified in IETF RFC 3588 [13], in order to use such an interface the CSE shall act as a Diameter client as described in IETF RFC 6733 [14].

B.1.2 Device Action Request command

When a CSE needs to issue a device triggering request from MTC-IWF, the CSE shall send a Device-Action-Request (DAR) command (see [16]). The following tables provide an overview of the parameters and the parameter values needed for the DAR command.

NOTE:	The values of the parameters indicated in the "Value" column need to be mapped to the specific 3GPP data type.

Table B.1.2-1: AVPs in Device Action Request (DAR) command

| Attribute Value Pair (AVP) name | AVP description | 3GPP Data Type | AVP Code | Optionality | Value |
| --- | --- | --- | --- | --- | --- |
| Session-Id | It is used to identify a specific session (see [13]) | UTF8String | 263 | M | CSE implementation specific |
| Auth-Application-Id | This parameter transport the Tsp application identifier as specified in [16], clause 6.1.3 | Enumerated | 274 | M | 16777309 |
| Auth-Session-State | The Tsp session is terminated after each request/answer pair and in accordance with [16] the parameter shall indicate that the session state shall not be maintained | Enumerated | 277 | M | NO_STATE_MAINTAINED (see [16]) |
| Origin-Host | It identifies the endpoint that originated the Diameter message (see [13]) | DiamIdent | 264 | M | CSE implementation specific |
| Origin-Realm | It identifies the Realm of the originator of theDiameter message (see [13]) | DiamIdent | 296 | M | CSE implementation specific |
| Destination-Realm | It identifies the realm the message is to be routed to. (see [13]) | DiamIdent | 283 | M | Domain Identifier part from M2M-Ext-ID |
| Destination-Host | The absence of the Destination-Host causes the message to be sent to any Diameter server supporting the application within the specified realm. (see [13]) | DiamIdent | 293 | O | NULL |
| Origin-State-Id | It is an increasing value that is advanced whenever a Diameter entity restarts with loss of previous state, for example upon reboot (see [13]) | Unsigned32 | 278 | O | CSE implementation specific |
| Device-Action | It contains the specific action for the device (see [16]) | Grouped | 3001 | O | Specific format described in table B.1.2-2 |
| Proxy-Info | It's a grouped AVP which provides the proxy state and host (see [13]) | Grouped | 284 | O | CSE implementation specific |
| Route-Record | The identity added in this AVP is be the same as the one received in the Origin-Host (see [13]) | DiamIdent | 282 | O | Not applicable |

Table B.1.2-2: AVPs in Device Action AVP (Grouped AVP)

| Attribute Value Pair (AVP) name | AVP description | 3GPP Data Type | AVP Code | Optionality | Value |
| --- | --- | --- | --- | --- | --- |
| External-Id | It is the identifier of the device as specified in [TS 29.336] | UTF8String | 3111 | O | M2M-Ext-ID (see clause 6.3.2.2) |
| MSISDN | It is the identifier of the device as specified in [TS 29.329] | OctetString | 701 | O | M2M-Ext-ID (see clause 6.3.2.2) |
| SCS-Identifier | It identifies the CSE issuing the request (see [16]) | OctetString | 3104 | O | CSE-ID (see clause 6.3.2.1 ) |
| Reference-number | It uniquely identifies a transaction (see [16]) | Unsigned32 | 3007 | M | CSE implementation specific Editor's note: possibility to maybe use M2M-Request-ID is FFS |
| Action-Type | It informs the MTC-IWF of the required action | Enumerated | 3005 | M | 1 (Device Trigger Request) |
| Trigger-Data | It is used by the CSE to supply all data required for a device trigger request. | Grouped | 3003 | O | See table B.1.2-3 |
| Validity-Time | The validity time in seconds for the specific action requested. (see [16]) | Unsigned32 | 448 | O | CSE implementation specific |
|  | NOTE: Either external-Id or MSISDN shall be used, not both. |

Table B.1.2-1: AVPs in Trigger Data AVP (Grouped AVP)

| Attribute Value Pair (AVP) name | AVP description | 3GPP Data Type | AVP Code | Optionality | Value |
| --- | --- | --- | --- | --- | --- |
| Payload | It contains the payload to be transferred to the addressed device. (see [16]) | OctetString | 3004 | M | NULL Furhter values can be defined (FFS) Editor's Note: in the current TS-0001 does not specify how to use payload. |
| Priority-Indication | It identifies priority of the device trigger. (see [16]) | Enumerated | 3006 | O | CSE implementation specific (possible values are 0 or 1) |
| Application-Port-Identifier | It uniquely identifies the triggering entity addressed in the device. (see [16]) | Unsigned32 | 3010 | O | Trigger-Recipient-ID |

Editor's Note: Removal of Editor's Note in the Value file for Payload should be considered.

B.1.3 Device Action Answer command

As a result of device triggering request to MTC-IWF, the CSE receives a Device-Action-Answer (DAA) command (see [16]). The relevant parameters for a CSE are  in the following tables. Table B.1.3-1: AVPs in Device Action Answer (DAA) command

| Attribute Value Pair (AVP) name | AVP description | 3GPP Data Type | AVP Code | Optionality | Value |
| --- | --- | --- | --- | --- | --- |
| Session-Id | It is used to identify a specific session (see [13]) | UTF8String | 263 | M | Same with Session-id in the DAR command |
| Auth-Application-Id | This parameter transport the Tsp application identifier as specified in [16], clause 6.1.3 | Enumerated | 274 | M | 16777309 |
| Auth-Session-State | The Tsp session is terminated after each request/answer pair and in accordance with [16] the parameter shall indicate that the session state shall not be maintained | Enumerated | 277 | M | NO_STATE_MAINTAINED (see [16]) |
| Origin-Host | It identifies the endpoint that originated the Diameter message (see [13]) | DiamIdent | 264 | M | MTC-IWF implementation specific |
| Origin-Realm | It identifies the Realm of the originator of the Diameter message (see [13]) | DiamIdent | 296 | M | MTC-IWF implementation specific |
| Result-Code | It indicates whether a particular request was completed successfully or an error occurred (see [13]). | Unsigned32 | 268 | O | see [13] for details |
| Experimental-Result | It indicates whether a particular vendor-specific request was completed successfully or whether an error occurred (see [13]). | Grouped | 297 | O | see [13] for details |
| Error-Message | It may accompany a Result-Code AVP as a human-readable error message (see [13]). | UTF8String | 281 | O | see [13] for details |
| Error-Reporting-Host | It contains the identity of the Diameter host that sent the Result-Code AVP to a value other than success, only if the host setting the Result-Code is different from the one encoded in the Origin-Host AVP (see [13]). | DiamIdent | 294 | O | see [13] for details |
| Failed-AVP | It provides debugging information in cases where a request is rejected or not fully processed due to erroneous information in a specific AVP (see [13]). | Grouped | 279 | O | MTC-IWF implementation specific |
| Origin-State-Id | It is an increasing value that is advanced whenever a Diameter entity restarts with loss of previous state, for example upon reboot (see [13]) | Unsigned32 | 278 | O | MTC-IWF implementation specific |
| Device-Notification | It is used by the MTC-IWF to report any action requested by the CSE. | Grouped | 3002 | M | See table B.1.3-2 |
| Redirect-Host | When present,the receiving Diameter node should forward the request directly to one of the hosts identified in these AVPs(see [13]). | DiameterURI | 292 | O | see [13] for details |
| Redirect-Host-Usage | When present, this AVP provides hints about how the routing entry resulting from the Redirect-Host is to be used (see [13]). | Enumerated | 261 | O | see [13] for details |
| Redirect-Max-Cache-Time | It contains the maximum number of seconds the peer and route table entries, created as a result of the Redirect-Host, should be cached (see [13]). | Unsigned32 | 262 | O | see [13] for details |
| Proxy-Info | It's a grouped AVP which provides the proxy state and host (see [13]) | Grouped | 284 | O | MTC-IWF implementation specific |

Table B.1.3-2: AVPs in Device Notification AVP (Grouped AVP)

| Attribute Value Pair (AVP) name | AVP description | 3GPP Data Type | AVP Code | Optionality | Value |
| --- | --- | --- | --- | --- | --- |
| External-Id | It is the identifier of the device as specified in [TS 29.336] | UTF8String | 3111 | O | The same value with DAR command. |
| MSISDN | It is the identifier of the device as specified in [TS 29.329] | OctetString | 701 | O | The same value with DAR command. |
| SCS-Identifier | It identifies the CSE issuing the request (see [16]) | OctetString | 3104 | O | The same value with DAR command. |
| Reference-number | It uniquely identifies a transaction (see [16]). | Unsigned32 | 3007 | M | The same value with DAR command. |
| Action-Type | It informs the MTC-IWF of the required action (see [16]) | Enumerated | 3005 | M | 1 (Device Trigger Request) |
| Result-Status | It informs the CSE of the status of s device action request (see [16]). | Enumerated | 3008 | O | See table B.1.3-3 |
| Delivery-Outcome | It informs the CSE of the outcome of the device action request (see [16]). | Enumerated | 3009 | O | See table B.1.3-4 |
|  | NOTE: Either external-Id or MSISDN shall be used, not both. |

Table B.1.3-3: Result Status

| Result-Status value | Name | Parameter description |
| --- | --- | --- |
| 0 | SUCCESS | This value indicates that device action requested is confirmed. |
| 201 | TEMPORARYERROR | See [16] for detail. |
| 101 | INVALIDPAYLOAD | See [16] for detail. |
| 102 | INVEXTID | See [16] for detail. |
| 103 | INVSCSID | See [16] for detail. |
| 104 | INVPERIOD | See [16] for detail. |
| 105 | NOTAUTHORIZED | See [16] for detail. |
| 106 | SERVICEUNAVAILABLE | See [16] for detail. |
| 107 | PERMANENTERROR | See [16] for detail. |
| 108 | QUOTAEXCEEDED | See [16] for detail. |
| 109 | RATEEXCEEDED | See [16] for detail. |

Table B.1.3-4: Delivery-Outcome

| Delivery-Outcome value | Name | Parameter description |
| --- | --- | --- |
| 0 | SUCCESS | This value indicates that the device action request was successfully completed. |
| 1 | EXPIRED | See [16] for detail. |
| 2 | TEMPORARYERROR | See [16] for detail. |
| 3 | UNDELIVERABLE | See [16] for detail. |
| 4 | UNCONFIRMED | See [16] for detail. |

B.1.4 Device Notification Request command

As a report of the result for device triggering delivery by 3GPP network, the CSE receives a Device-Notification-Request (DNR) command (see [16]). The relevant parameters for a CSE are in the following table.

Table B.1.4-1: AVPs in Device Notification Request (DNR) command

| Attribute Value Pair (AVP) name | AVP description | 3GPP Data Type | AVP Code | Optionality | Value |
| --- | --- | --- | --- | --- | --- |
| Session-Id | It is used to identify a specific session (see [13]) | UTF8String | 263 | M | MTC-IWF implementation specific (see [13] for details) |
| Auth-Application-Id | This parameter transport the Tsp application identifier as specified in [16], clause 6.1.3 | Enumerated | 274 | M | 16777309 |
| Auth-Session-State | The Tsp session is terminated after each request/answer pair and in accordance with [16] the parameter shall indicate that the session state shall not be maintained | Enumerated | 277 | M | NO_STATE_MAINTAINED (see [16]) |
| Origin-Host | It identifies the endpoint that originated the Diameter message (see [13]) | DiamIdent | 264 | M | MTC-IWF implementation specific |
| Origin-Realm | It identifies the Realm of the originator of theDiameter message (see [13]) | DiamIdent | 296 | M | MTC-IWF implementation specific |
| Destination-Realm | It identifies the realm the message is to be routed to. (see [13]) | DiamIdent | 283 | M | CSE implementation specific |
| Destination-Host | The absence of the Destination-Host causes the message to be sent to any Diameter server supporting the application within the specified realm. (see [13]) | DiamIdent | 293 | M | CSE implementation specific |
| Origin-State-Id | It is an increasing value that is advanced whenever a Diameter entity restarts with loss of previous state, for example upon reboot (see [13]) | Unsigned32 | 278 | O | MTC-IWF implementation specific |
| Device-Notification | It is used by the MTC-IWF to report any action requested by the CSE. | Grouped | 3002 | O | See table B.1.3-2 |
| Proxy-Info | It's a grouped AVP which provides the proxy state and host (see [13]) | Grouped | 284 | O | MTC-IWF implementation specific |
| Route-Record | The identity added in this AVP is the same as the one received in the Origin-Host (see [13]) | DiamIdent | 282 | O | Not applicable |

B.1.5 Device Notification Answer command

As a result of device notification request to MTC-IWF, the CSE sends a Device-Notification-Answer (DNA) command (see [16]). The relevant parameters for a CSE are in the following table.

Table B.1.2-1: AVPs in Device Notification Answer (DNR) command

| Attribute Value Pair (AVP) name | AVP description | 3GPP Data Type | AVP Code | Optionality | Value |
| --- | --- | --- | --- | --- | --- |
| Session-Id | It is used to identify a specific session (see [13]) | UTF8String | 263 | M | CSE implementation specific |
| Auth-Application-Id | This parameter transport the Tsp application identifier as specified in [16], clause 6.1.3 | Enumerated | 274 | M | 16777309 |
| Auth-Session-State | The Tsp session is terminated after each request/answer pair and in accordance with [16] the parameter shall indicate that the session state shall not be maintained | Enumerated | 277 | M | NO_STATE_MAINTAINED (see [16]) |
| Origin-Host | It identifies the endpoint that originated the Diameter message (see [13]) | DiamIdent | 264 | M | CSE implementation specific |
| Origin-Realm | It identifies the Realm of the originator of theDiameter message (see [13]) | DiamIdent | 296 | M | CSE implementation specific |
| Result-Code | It indicates whether a particular request was completed successfully or an error occurred (see [13]). | Unsigned32 | 268 | O | see [13] for details |
| Experimental-Result | It indicates whether a particular vendor-specific request was completed successfully or whether an error occurred (see [13]). | Grouped | 297 | O | see [13] for details |
| Origin-State-Id | It is an increasing value that is advanced whenever a Diameter entity restarts with loss of previous state, for example upon reboot (see [13]) | Unsigned32 | 278 | O | CSE implementation specific |
| Error-Message | It may accompany a Result-Code AVP as a human-readable error message (see [13]). | UTF8String | 281 | O | see [13] for details |
| Error-Reporting-Host | It contains the identity of the Diameter host that sent the Result-Code AVP to a value other than success, only if the host setting the Result-Code is different from the one encoded in the Origin-Host AVP (see [13]). | DiamIdent | 294 | O | see [13] for details |
| Failed-AVP | It provides debugging information in cases where a request is rejected or not fully processed due to erroneous information in a specific AVP (see [13]). | Grouped | 279 | O | CSE implementation specific |
| Redirect-Host | When present, the receiving Diameter node should forward the request directly to one of the hosts identified in these AVPs (see [13]). | DiameterURI | 292 | O | see [13] for details |
| Redirect-Host-Usage | When present, this AVP provides hints about how the routing entry resulting from the Redirect-Host is to be used (see [13]). | Enumerated | 261 | O | see [13] for details |
| Redirect-Max-Cache-Time | It contains the maximum number of seconds the peer and route table entries, created as a result of the Redirect-Host, should be cached (see [13]). | Unsigned32 | 262 | O | see [13] for details |
| Proxy-Info | It's a grouped AVP which provides the proxy state and host (see [13]) | Grouped | 284 | O | CSE implementation specific |

----- End of change 1----

# Comments

Is this reference, which is to an obsolete version of the RFC, correct?

Reference to be added in the reference clause.

Reference to be added in the reference clause.

Reference to be added in the reference clause.

Reference to be added in the reference clause.