| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG3 |
| Title:* | Correction of the parameters at the Device Triggering commands |
| Source:* | Qi Yu, Huawei, yuqi@huawei.com |
| Contact: | <name>, <company>, <contact info> (if different to the source) |
| Date:* | 2014-07-15 |
| Abstract:* | At the Device Triggering commands, some AVPs are optional, the others are mandatory according to 3GPP TS 23.368. Some parameters are missing at Device Action Answer, Device Notification Request and Device Notification Answer commands. This contribution intends to correct the above issues. R01: Only keep the parameters which are mapped to 3GPP. Others refers to 3GPP specification. Modify the references |
| Agenda Item:* | Core Protocol TS |
| Work item(s): | WI-0009 |
| Document(s) Impacted* | TS-0004v0.5.3 Annex B |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Member should agree on proposed changes. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

This contribution intends to add a column to indicate the optionality.  The missing parameters are also been added.

----- Start of change 1----

## Normative references

The following referenced documents are necessary for the application of the present document.

[1]	IETF RFC 5139: "Revised Civic Location Format for Presence Information Data Format Location Object (PIDF-LO)".

[2]	IETF RFC 3986: "Uniform Resource Identifier (URI): Generic Syntax".

[3]	W3C XMLSchemaP2: "W3C Recommendation (2004), XML Schema Part 2:Datatypes Second Edition.".

[4]	ISO 19136 (2007): "Geographic information -- Geography Markup Language (GML).".

[5]	W3C XMLPath: "W3C Recommendation (2010), XML Path Language (XPath) 2.0 (Second Edition)".

[6]	oneM2M TS-0001 "Functional Architecture". TBD.

[7]

[8]	IEEE 754-2008: IEEE. IEEE Standard for Floating-Point Arithmetic. 29 August 2008. http://ieeexplore.ieee.org/servlet/opac?punumber=4610933

[9]	IETF RFC 3548: "The Base16, Base32, and Base64 Data Encodings". 2003.

[10]	IETF RFC 2045: "Multipurpose Internet Mail Extensions (MIME) Part One: Format of Internet Message Bodies". 1996.

[11]	IETF RFC 3987:" Internationalized Resource Identifiers (IRIs)" . January 2005.

[12]	IETF BCP 47: "Best Current Practices 47". Concatenation of RFC 4646:" Tags for Identifying Languages"(2006) and RFC 4647: "Matching of Language Tags"( 2006).

[13]	IETF RFC 3588: "Diameter Base Protocol". September 2003.

[14]	IETF RFC 6733: "Diameter Base Protocol". October 2012.

[15]	3GPP TS 23.682: "Architecture enhancements to facilitate communications with packet data networks and applications" Release 11.

[16]	3GPP TS 29.368: "Tsp interface protocol between the MTC Interworking Function (MTC-IWF) and Service Capability Server (SCS)" Release 11.

----- End of change 1----

----- Start of change 2----

Annex B (normative):
Device Triggering

B.1 Providing Device Triggering service by means of 3GPP networks

B.1.1 Introduction

3GPP Underlying Network has defined a dedicated interface for requesting device triggering. The normative references for applicable interfaces are as follows: 3GPP TS 23.682 [15]. The specification for the interface Tsp is described in 3GPP TS 29.368 [16]. Tsp interface uses Diameter Base Protocol as specified in IETF RFC 3588 [13], in order to use such an interface the CSE shall act as a Diameter client as described in IETF RFC 6733 [14].

B.1.2 Device Action Request command

When a CSE needs to issue a device triggering request to  the MTC-IWF, the CSE shall send a Device-Action-Request (DAR) command (for details, see TS 29.368[16]). The following list provides \ the parameters mapping between the oneM2M and 3GPP.

Either External-Id or MSISDN:  the CSE maps it to the M2M-External-ID, see clause 6.3.2.3

SCS identifier: the CSE maps it to the CSE-ID, see clause 6.3.2.1

Application Port Identifier: the CSE maps it to Trigger-Recipient-ID, see clause 6.2

B.1.3 Device Action Answer command

| As a result of device triggering request to MTC-IWF, the CSE receives a Device-Action-Answer (DAA) command (for details, see TS29.368 [16]). |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| T |  |  |

B.1.4 Device Notification Request command

As a report of the result for device triggering delivery by 3GPP network, the CSE receives a Device-Notification-Request (DNR) command (for details, see TS 29.368 [16]).

B.1.5 Device Notification Answer command

As a result of device notification request to MTC-IWF, the CSE sends a Device-Notification-Answer (DNA) command (for details, see TS29.368 [16]).

----- End of change 2----

# Comments

These 2 references are NOT mentioned in the document. Move them to the Bibliography or delete them.

Empty reference. Mentioned in the document in table 6.3.2.1-1. Please update.

Is this reference, which is to an obsolete version of the RFC, correct?

Reference to be added in the reference clause.

Reference to be added in the reference clause.

Reference to be added in the reference clause.

Reference to be added in the reference clause.