| Change Request |
| --- |
| Group Name:* | WG3 (PRO) |
| Source:* | QUALCOMM Incorporated (TIA), InterDigital (TIA) |
| Format:* | PRO#12.5 (teleconference) |
| Date:* | 2014-09-09 |
| Contact:* | Wolfgang Granzow, wgranzow@qti.qualcomm.com Phil Brown, phil.brown@interdigital.com |
| Reason for Change/s:* | Changes to XSD design guidelines to reflect current practice |
| CR against: Release* | 1 |
| CR against: TS/TR* | TS-0004 - V-0.6.1 |
| Clauses/Sub Clauses* | Annex F |
| Type of change:* | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

---------------------------- Start of change 1 ---------------------------------

Annex F (informative):
Guidelines for one M2M resource type XSD

This Annex contains rules to be followed when creating XML Schema Definition (XSD) files to represent the oneM2M resources. The XSD files themselves form part of the oneM2M protocol specification, but the rules used to construct them do not, hence this Annex is informative.

The purpose of these rules is:

- To keep a consistent style between the schemas for different resources

- To keep the XSD simple

- To allow individual resource schemas to be authored and maintained separately, while minimising the risk of conflict when they are all used together

Each XSD file should include a schema element with following namespace declarations:

- <xs:schema xmlns:xs="http://www.w3.org/2001/XMLSchema" 	
                      targetNamespace="http://www.onem2m.org/xml/protocols" 
                      xmlns:m2m="http://www.onem2m.org/xml/protocols"
                      elementFormDefault="unqualified" attributeFormDefault="unqualified" >

This defines the prefix xs: for the XML Schema namespace, a target namespace http://www.onem2m.org/xml/protocols, and the prefix m2m: as equivalent for the target namespace. Locally declared elements and attributes shall be unqualified (elementFormDefault and attributeFormDefault declarations are not strictly required since “unqualified” is the default value setting).

Each Resource XSD file will contain a single Global Element Declaration whose name is the name of the Resource Type in accordance with [6]. This means that the root element of a Resource (when represented as an XML instance) contains an m2m: (or equivalent) namespace prefix. It shall not contribute anything to the m2m: namespace other than this root element.

The root element of each Resource XSD file shall have an attribute called “name” which gives an identifier for that particular resource instance. A URI to the resource instance can be constructed by taking the URI of its parent and appending /<name> where <name> is the value of the name attribute.

Each resource attribute of the Resource Type in accordance with [6] is represented as a child element of the top level element. It shall be declared as an element that is local to the resource that contains it, and so does not have a namespace prefix in any XML instance representation of the resource.

Each child resource of the Resource Type in accordance with [6] shall be represented as a child element of the top level element using the name ‘childResource’ of data type m2m:childResourceRef.

Each resource attribute shall be declared to use one of the following data types:

  - A data type listed in clause 6.3.1 or 6.3.2.

  - A list of one of the data types listed in clause 6.3.1 or 6.3.2. If the list type is not already included in 6.3.2 it may be defined inside the XSD file for the resource, but if so it must be defined as an anonymous type in the attribute declaration itself.

  - A data type derived by restriction from one of the types listed in clause 6.3.1 or 6.3.2. This may be defined inside the XSD file for the resource, but if so it must be defined as an anonymous type in the attribute declaration itself.

  - All complex types should be defined as part of the attribute declaration (inside the XSD file for the resource).

If a data type is used by more than one attribute (either in the same resource or in two different resources) it must be included in 6.3.2, and referenced by each attribute that uses it. Options 6b, 6c, 6d should only be used in cases where the type is only used by one attribute.

With the exception of CSEBase, all Resource types will extend one of the XML complex types regularResourceType, subordinateResourceType or announceableResourceType defined in the file CDT-commonTypes-v1_0_0<date>.xsd.

The resource-specific attributes and child resources shall appear as a sequence of elements in the XSD file, with their order being determined by the order shown in the tables in clause 9.6 of [6].

Each XSD file shall include an XML comment that contains a oneM2M Copyright Notification,  Notice of Disclaimer & Limitation of Liability, and a change history. The change history is to be filled in only after the initial release.

To enable distinction between element names used for resource attributes and their data types in the m2m: namespace, it shall be avoided to use identical names. It is recommended to use the text suffix ‘Type’ in data type names.

Example:

<xs:element name="status" type="m2m:statusType />

---------------------------- End of change 1 ---------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Comments

This is good, in particular the removing of the xmlns: default namespace declaration

I think we should use the same concept to define the mgmtLink attribute in XSD. This could be captured in an additional paragraph (after we have achieved agreement on the proposed text for the childResource).

Should the URI value include the name of the child resource as given in the @name attribute?

I think that a discussion of m2m:childResourceRef really belongs somewhere in clause 6.3 rather than in Annex F since it's something that gets filled in at runtime rather than instructions to the XSD creator. All we really need in Annex F is a directive to use m2m:childResourceRef.  Having said that, Wolfgang's comment and example raises a couple of  questions. i) Should we allow any URI, not just non-hierarchical ones?  ii) what is the xsd datatype and format of the type element? Is it a string, the QName of the Resource type GED, the NCName part of that Resource type GED or the m2m:resourceType (currently an integer enumeration)?

If we agree to include all resource attribute data types into clause 6.3, see comment GW4 below, we actually should mandate to not use anonymous data types at all.

Would you want to include list types and types defined by restriction of simple types in 6.3 as well?

What about subordinateResourceType, do we not need that any more?

I don’t think that this is strictly necessary as they are in separate namespaces. I’m undecided as to whether we should require a type suffix on everything. At the moment we have it on some types but not others, which looks a bit irregular