| CHANGE REQUEST |
| --- |
| Group Name:* | PRO#13 |
| Title: * | Cleanup for resource announcement |
| Source:* | ZTE, LG Electronics |
| Format:* | Plenary / Teleconference |
| Date:* | 2014-09-22 |
| Contact:* | Hao Wu, ZTE, wu.hao18@zte.com.cn Rajesh Bhalla, ZTE, rabhalla@ztetx.com Seungkyu Park, LG Electronics, seungk.park@lge.com |
| Reason for Change/s:* | This contribution corrects the procedures for the resource announcement. |
| CR against: Release* | Release 1 |
| CR against: TS/TR* | TS-0004, ver 0.6.0 |
| Clauses/Sub Clauses* | 7.2.2.3.9, 7.2.2.3.10 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution propose to clean up procedure for announce/de-announce the resource or attribute.

1. add the subject of actions to make this clause more readable.

2. change “marked with” to “specified as” according to agreement in the last meeting.

3. add the missing case of deletion or creation of the announceTo announcedAttribute attribute by UPDATE operation, which is excluded in clause 7.2.2.3.6 “Update the resource”.

4. other editorial error.

### -----------------------Start of Change 1-------------------------------------------

##### Announce the resource or attribute

If CREATE request that contains an announceTo attribute is received, the hosting CSE shall,

Compose a CREATE Request primitive as follows:

Link attribute is set to the URI of the original resource.

If accessControlPolicyIDs attribute of the original resource is not present, accessControlPolicyIDs attribute is set to the same value as the parent resource or from the local policy of the original resource.

Attributes specified as MA and attributes specified as OA that are included in the announcedAttribute attribute shall be included in the Request. Such attributes shall be present in the original resource and shall be set to same value as the original resource.

Send the CREATE Request to the the CSE(s) represented by exact URI(s) or CSE-ID(s) in the announceTo attribute of the request.

Wait for Response primitive

Add the URI of successfully announced resource to the announceTo attribute of the resource

Include updated announceTo attribute in the content parameter in the Response to the received CREATE Request.

If UPDATE request that adds the URI or CSE-ID into the announceTo attribute is received, the hosting CSE shall,

Compose a CREATE Request primitive as follows:

Link attribute is set to the URI of the original resource.

If accessControlPolicyIDs attribute of the original resource is not present, accessControlPolicyIDs attribute is set to the same value as the parent resource or from the local policy of the original resource.

Attributes speicified as MA and attributes specified as OA that are included in the announcedAttribute attribute shall be included in the Request. Such attributes shall be present in the original resource and shall be set to same value as the original resource.

Send the CREATE Request to the CSE(s) represented by exact URI(s) or CSE-ID(s) in the announceTo attribute of the request, which is not included in the announceTo attribute of the original resource.

Wait for Response primitive

If announceTo attribute is not present in the original resource, create announceTo attribute.

Add the URI of successfully announced resource to the announceTo attribute of the resource

Include updated announceTo attribute in the content parameter in the Response to the received UPDATE Request.

If UPDATE request that adds attribute name(s) into the announcedAttribute attribute is received, the hosting CSE shall,

Compose an UPDATE Request. The UPDATE Request shall provide the attribute name for the attribute to be announced, and the initial value for the attribute in the content parameter. The initial value shall be the same as the value from the original resource. The attribute that will be announced shall be specified as OA.

Send the UPDATE Requests to all announced resources listed in the announceTo attribute.

Wait for Response primitive.

If the announcedAttribute attribute is not present in the original resource, create announcedAttribute attribute.

Add the attribute name of the successfully announced attribute to the announcedAttribute attribute.

Include updated announcedAttribute attribute in the content parameter in the Response to the received UPDATE Request.

If an attribute(s) specified as MA (See [6]) or an attribute(s) included in the announcedAttribute attribute is updated, the hosting CSE shall,

Compose an UPDATE Request primitive by including the updated attribute(s) with its associated updated value.

Send the UPDATE Request to all CSE(s) represented by the URI(s) in the announceTo attribute of the original resource.

If an attribute(s) specified as MA (See [6]) or an attribute(s) included in the announcedAttribute attribute is deleted, the hosting CSE shall,

Compose an UPDATE Request primitive by including the updated attribute(s) with its value set to NULL.

Send the UPDATE Request to all CSE(s) represented by the URI(s) in the announceTo attribute of the original resource.

### -----------------------End of Change 1-------------------------------------------

### -----------------------Start of Change 2-------------------------------------------

##### De-announce the resource or attribute

If UPDATE Request that deletes the URI from the announceTo attribute is received, the hosting CSE shall,

Compose a DELETE Request primitive.

Send the DELETE Request to the CSE(s) represented by URI(s) in the announceTo attribute of the resource, which is not included in the announceTo of the request. The to parameter in the DELETE Request shall be set to the URI for the announced resource that will be deleted.

Wait for Response primitive.

If announceTo attribute is set to NULL in the UPDATE Request, delete announceTo attribute. Else, remove the URI of  successfully de-announced resource from the announceTo attribute of the resource, and include updated announceTo attribute in the content parameter in the Response to the UPDATE Request of the original resource.

If DELETE Request is received, the hosting CSE shall,

Compose a DELETE Request primitive.

Send the DELETE Requests to all announced resources addressed by the URI(s) in the announceTo attribute of the resource.

Wait for Response primitive.

If UPDATE request that deletes the attribute name from the announcedAttribute attribute is received, the hosting CSE shall,

Compose an UPDATE Request primitive. The to parameter in the UPDATE Request shall be set to the URI for the announced resource. The UPDATE Request shall set the attribute to NULL that will be de-announced (i.e. to be deleted) in the content parameter. The attribute that will be de-announced shall be specified as OA.

Send the UPDATE Requests to all announced resources listed in the announceTo attribute of the original resource.

Wait for Response primitive.

If announcedAttribute is set to NULL in the UPDATE Request, delete announcedAttribute attribute. Else, remove the attribute name of the successfully de-announced attribute from the announcedAttribute attribute, and include updated announcedAttribute attribute in the content parameter in the Response to the received UPDATE Request.

### -----------------------End of Change 2---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?