| CHANGE REQUEST |
| --- |
| Group Name:* | PRO |
| Source:* | FUJITSU |
| Format:* | ordinary meeting |
| Date:* | 2014-09-15 |
| Contact:* | Shingo Fujimoto,FUJITSU,shingo_fujimoto@jp.fujitsu.com |
| Reason for Change/s:* | The current specification does not provide enough information to perform CRUD operations in HTTP binding |
| CR against: Release* | 1.0 |
| CR against: TS/TR* | TS-0009 V0.4.3 |
| Clauses/Sub Clauses* | 5 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The current specification does not provide enough information to understand about the HTTP binding.

This contribution proposed to add more descriptive texts for better understadings.

### -----------------------Start of change 1-------------------------------------------

# 6	HTTP Message Mapping

## 6.1	Introduction

Mapping between HTTP message and oneM2M primitive shall be applied in the following cases:

- when the Originator sends a request primitive,

- when the Receiver receives a request primitive,

- when the Receiver sends a response primitive,

- when the Originator receives a response primitive.

The following sub-clauses specify how to map each oneM2M primitive parameter to a corresponding HTTP message field to compose a HTTP request/response message..

## 6.2	Parameter Mappings on Request-Line

### 6.2.1	Method

The HTTP ‘Method’ shall be specified according to the oneM2M operation parameter of the request primitive (clause 7.2.1.1.1 [6]):

Table 6.2.1-1: HTTP Method Mapping

| oneM2M Operation | HTTP Method |
| --- | --- |
| Create | POST |
| Retrieve | GET |
| Update | PUT or POST (for partial update) |
| Delete | DELETE |
| Notify | POST |

Editor’s Note: Update operation mapping is TBD until the attribute level manipulation scheme is resolved in TS-0001 and TS-0004.

At the Receiver, an HTTP request message with POST method shall be mapped to a oneM2M Create or Notify request primitive in accordance with the value of the operation parameter.

### 6.2.2	Request-Target

The HTTP Request-Target shall be prepared as absolute-form (see [1]).:

The to parameter shall be mapped to ‘absolute-path’ in Request-Target.Other request parameter shall be specified as pair of field-name and value in query-string as shown in Table.X

Table X: request parameters mapped as query-string field

| request parameter | field name | Note |
| --- | --- | --- |
| Original Timestamp | ot filed |  |
| Request Expiration Timestamp | ret field |  |
| Result Expiration Timestamp | rst field |  |
| Operation Execution Time | oet field |  |
| Response Type | rt field |  |
| Result Persistence | rp field |  |
| Result Content | rc field |  |
| Event Category | ec field |  |
| Delivery Aggregation | da field |  |
| Group Request Identifier | gid field |  |
| Filter Criteria | fc field |  |
| Discovery Result Type | drt field |  |

Editor’s Note: encoding structured information such as ec and fc is FFS.

### 6.2.3	HTTP-Version

This specification supports binding to HTTP 1.1 [1], so the version field shall be set to “HTTP/1.1”.

#### 6.2.4 Mapping on Request Headers

Following request parameters are mapped to HTTP Headers in present specification.

| request parameter | header name | Note |
| --- | --- | --- |
| From | From |  |
| Request Identifier | X-M2M-RI |  |
| Resource Type | Content-Type | ty parameter of application/vnd.onem2m-resource-data+xml |
| Name | Content-Location |  |

## 6.3	Status-Line

### 6.3.1	HTTP-Version

This specification supports binding to HTTP 1.1[1], so the version field shall be set to “HTTP/1.1”.

### 6.3.2	Status-Code

The oneM2M responseStatusCode shall be mapped to HTTP Status-Code. Since the responseStatusCode have been defined more specifically, one or more responseStatusCodes may be mapped to Status-Code. The original responseStatusCode parameter shall be carried in message-body (see clause 6.5).

N:1 status code mapping from the oneM2M request primitive to HTTP request message shall be:

Table 6.3.2-1: Status Code Mapping

| oneM2M Response Status Codes | HTTP Status Codes |
| --- | --- |
| Success | 200 (OK) |
| Accepted | 202 (Accepted) |
| Location info not authorized | 403 (Forbidden) |
| Unsupported resource | 404 (Not Found) |
| Unsupported attribute | 404 (Not Found) |
| Cannot forward, target not reachable | 404 (Not Found) |
| Cannot forward, other reason TBD | 404 (Not Found) |
| Create error - no privilege | 403 (Forbidden) |
| Create error - already exists | 403 (Forbidden) |
| Create error - missing mandatory parameter | 400 (Bad Request) |
| Retrieve error - no privilege | 403 (Forbidden) |
| Retrieve error - does not exist | 404 (Not Found) |
| Update error - no privilege | 403 (Forbidden) |
| Update error - does not exist | 404 (Not Found) |
| Update error - unacceptable contents | 415 (Unsupported Media Type) |
| Delete error - does not exist | 404 (Not Found) |
| Delete error - no privilege | 403 (Forbidden) |
| Create delivery - not able to take on responsibility | 403 (Forbidden) |
| Create fanoutpoint - group request identifier exists | 409 (Conflicts) |
| Retrieve fanoutpoint - group request identifier exists | 409 (Conflicts) |
| Update fanoutpoint - group request identifier exists | 409 (Conflicts) |
| Delete fanoutpoint - group request identifier exists | 409 (Conflicts) |
| Create mgmtObj - memory shortage | 403 (Forbidden) |
| External object not found | 404 (Not Found) |
| Cancel execInstance - not cancellable | 403 (Forbidden) |
| Cancel execInstance - already complete | 403 (Forbidden) |
| Delete execInstance - not cancellable | 403 (Forbidden) |
| Delete execInstance - already complete | 403 (Forbidden) |
| Retrieve CSEBase - format error | 400 (Bad Request) |
| CMDH rules -non compliant | 403 (Forbidden) |
| Target is not subscribable | 403 (Forbidden) |
| Cannot initiate subscription verification | 403 (Forbidden) |
| Subscription verification failed | 403 (Forbidden) |

Editor’s Note: This table needs to be updated aligning with TS-0004.

### 6.3.3	Reason-Phrase

Reason-Phrase shall be mapped to the description of the corresponding responseStatusCode of the response primitive (see clause 6.5.4 [3]).

## 6.4	Header Fields

### 6.4.1	Host

A Host header shall be included in an HTTP request message. Other headers may be included in an HTTP request/response message.

Host shall be derived from the to parameter of the request primitive. This shall consist of the host and optionally port number.

### 6.4.2	Accept

An Originator may use the Accept header to indicate which content-type is supported by the Originator.  The Accept header shall be set to “application/onem2m-resource+xml” or “application/onem2m-resource+json”.

Editor’s Note: Supported types are TBD.

### 6.4.3	Content-type

Any request or response containing message-body shall include the Content-type header set to “application/onem2m-resource+xml” or “application/onem2m-resource+json”.

Editor’s Note: Supported types are TBD.

### 6.4.4	Content-Location

The Content-Location header shall be set to the URI of:

- the created resource, when responding to a Create request primitive;

- the retrieved resource, when responding to a Retrieve request primitive if the retrieved resource location is different from the requested resource location;

- the updated resource, when responding to a Update request primitive

Editor’s Note: Usage of this header needs more investigation.

Editor’s Note: How to indicate the oneM2M URI scheme is TBD

### 6.4.5	Content-Length

If message-body is included, the Content-Length header shall be included indicating the length of the message-body in octets (8-bit bytes).

### 6.4.6	ETag

A retrieve response primitive corresponding to a resource retrieval request primitive should include an ETag header together with the resource representation [1].

ETag facilitates the use of conditional requests (i.e. using the if-match and if-none-match HTTP headers).

If a CSE supports the ETag header, then the CSE shall support conditional requests.

### 6.4.7	From

The From header shall be mapped to the from parameter of the request/response primitive, and shall contain the oneM2M specified ID of the Originator (e.g. CSE-ID or AE-ID).

### 6.4.8	Location

The Location header shall be mapped to the URI of the created resource. This header shall be present in the response primitive corresponding to a create request and shall not be present in any other request or response.

Editor’s Note: if Originator’s nm parameter can be modified and accepted by the Hosting CSE is TBD.

### 6.4.9	X-M2M-RI

All requests and responses shall include an oneM2M defined header field called X-M2M-RI that contains the requestID.

Editor’s Note: mapping request ID can be query or this extension header, this is TBD.

### 6.4.10	Other Header Fields

Other HTTP header fields shall be mapped with oneM2M primitive parameters.

Editor’s Note: The list of the fields and details are FFS.

## 6.5	Message-body

Depends on the operation type and the reference point, the combination of the primitive parameters may be different (see clause 7.2.1.1 [3]).

In HTTP request message, among the request parameters (see Table 7.2.1.1-1 [3]) Message-body shall include mandatory parameters except primitive type, to, from, request identifier parameter and may include conditional/optional parameters.

In HTTP response message, among the response parameters (see Table 7.2.1.1-2 and 7.2.1.1-3 [3]) Message-body shall include mandatory parameters except primitive type parameter and may include conditional/optional parameters.

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 6.7.1 application/vnd.onem2m-resource-data+xml

This data type is used for XML-based data to represent the oneM2M resource.

This MIME-Type also mandate to specify the parameter ‘ty’ with the resource type id of the resource.

The content of this MIME-Type shall be XML serialized formed M2M resource.

### -----------------------End of change 2---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?