| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TP#13 |
| Title:* | aggregate notifications |
| Source:* | Jiaxin Yin, Huawei Technologies Co., Ltd. |
| Contact: | Jiaxin Yin, Yinjiaxin@huawei.com |
| Date:* | 2014-9-11 |
| Abstract:* | The contribution provides procedure for group to aggregate notifications. |
| Agenda Item:* | TBD |
| Work item(s): | WI0009 |
| Document(s) Impacted* | TS0004 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the text into TS0004 if approved. |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

#### Introduction

The contribution provides detailed procedure for group to aggregate notifications to be supplements of the procedure in architecture TS.

******************start of change 1******************

#### 7.4.2.5	Notification for subscription via group

Whenever the subscribed to resources' modification causes a notification sending procedure indicated in clauses 7.4.2.1 and the subscription relationship is established through group resource, the following procedure shall be performed for the notification sending.

The Member hosting CSE shall perform the steps defined in 7.4.2.1.

The Group hosting CSE shall perform the following steps in order:

Validate if the notification is sent from its own member resources when it gets a notification at the notificationURI. The group hosting CSE shall respond a response with response status code “access denied” if the validation is not successful.

Upon successful validation, the group hosting CSE shall collect the notifications to the same subscriber according to the notificationForwardingURI of each notification. The group hosting CSE shall aggregate them into aggregatedNotification which shall be included in notification. The timing of aggregation is done as per the group hosting CSE’s local policy which is out of scope.

Send the aggregated notification to the notificationURI according to the notificationForwardingURI in the notification. In the case the group hosting CSE is the member of another group hosting CSE through which the subscription is created, the notification shall be sent according to the mapping of the notificationURI of the two group hosting CSEs. When aggregating the notifications, the group hosting CSE may utilize the rqet in the notification to determine the time the aggregated notifications to be sent.

"Wait for Response primitive".

Upon receiving the response, the group hosting CSE shall send the response separately to each individual member hosting CSEs to respond their corresponding notify request.

The group hosting CSE may also stop aggregating the notifications depending on its own policy. The group hosting CSE shall not stop aggregating the notifications before the expirationTime of the corresponding subscription expires.

The Subscriber shall perform the following steps in order:

- Extract each notification from the aggregated notification;

- Treat the notification as it is sent from the original subscribed-to resource;

- “Create a successful response”

- “Send the Response primitive”

******************end of change 1******************

******************start of change 2******************

#### Un-successful Response Codes

Table 6.6.3.2-1 specify the RSCs for un-successful responses for each release.

Table 6.6.3.2-1: RSCs for Un-successful Responses for Release 1

| Description | Numeric Code | StatusDescription | Applicability |
| --- | --- | --- | --- |
|  |  |  | Mca | Mcc | Mcn | Mcc' |
| Location info not authorized | 6001 |  |  |  | X |  |
| Unsupported resource | 5001 | Resource URI | X | X |  |  |
| Unsupported attribute | 5002 | Attribute URI | X | X |  |  |
| Target not reachable | 5003 | Resource URI | X | X |  |  |
| Cannot forward, other reason TBD | 5004 | Resource URI | X | X |  |  |
| No privilege | 5005 | Resource URI | X | X |  |  |
| Already exists | 5006 | Resource URI | X | X |  |  |
| Create error - missing mandatory parameter | 4007 | Missing parameter | X | X |  |  |
| Retrieve error - does not exist | 5009 | Target URI | X | X |  |  |
| Update error - unacceptable contents | 4012 | Attribute URI | X | X |  |  |
| Create delivery - not able to take on responsibility | 5015 |  | X | X |  |  |
| group request identifier exists | 6002 |  | X | X |  |  |
| access denied |  |  | X | X |  |  |
| External object not reachable | 6003 | mgmtObj URI | X | X |  |  |
| Create mgmtObj - memory shortage | 6004 | CSEBase URI | X | X |  |  |
| External object not found | 6005 | MgmtObj URI | X | X |  |  |
| Cancel execInstance - not cancellable | 6006 | execInstance URI | X | X |  |  |
| Cancel execInstance - already complete | 6007 | execInstance URI | X | X |  |  |
| Delete execInstance - not cancellable | 6008 | execInstance URI | X | X |  |  |
| Delete execInstance - already complete | 6009 | execInstance URI | X | X |  |  |
| Retrieve CSEBase - format error | 5035 | CSEBase URI | X | X |  |  |
| CMDH rules -non compliant | 5036 |  |  |  |  |  |
| Target is not subscribable | 5037 |  |  |  |  |  |
| Cannot initiate subscription verification | 5038 |  |  |  |  |  |
| Subscription verification failed – Originator ID | 5039 | Originator ID |  |  |  |  |
| Subscription verification failed - creator |  | creator |  |  |  |  |
| Max number of member exceeded | 6010 |  |  |  |  |  |
| Member type inconsistent | 6011 |  |  |  |  |  |
| Management session cannot be established | 6022 |  | X |  |  |  |
| Management session establishment timeout | 6003 |  | X |  |  |  |
| Create mgmtCmd – invalid cmdType | 6003 |  | X | X |  |  |
| Create mgmtCmd – invalid arguments | 6004 |  | X | X |  |  |
| Create mgmtCmd – insufficient arguments | 6005 |  | X | X |  |  |
| MgmtCmd – conversion error | 6006 |  | X | X |  |  |
| Delete mgmtCmd- execInstance cancellation error | 6007 |  | X | X |  |  |
| Cancel execInstance – cancellation error | 6008 |  | X |  |  |  |
| Delete execInstance – cancellation failed | 6009 |  | X |  |  |  |