| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TP#13 |
| Title:* | procedure for service layer managements |
| Source:* | Jiaxin Yin, Huawei Technologies Co., Ltd. |
| Contact: | Jiaxin Yin, Yinjiaxin@huawei.com |
| Date:* | 2014-9-11 |
| Abstract:* | The contribution provides procedure for service layer managements. |
| Agenda Item:* | TBD |
| Work item(s): | WI0009 |
| Document(s) Impacted* | TS0004 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the text into TS0004 if approved. |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

#### Introduction

The contribution provides service layer management procedures.

---------------------------------start of change 1-----------------------------------

#### Resource Specific Procedure on CRUD Operations

#### This clause describes <mgmtObj> resource specific procedure on resource Hosting CSE for CRUD operations. The procedures are defined for management when external management technologies are used. When service layer management are performed, generic procedures defined in 7.2.1.2 shall comply for resource creation, update, retrieval and deletion. Procedures additional to resource manipulations to perform the management are further defined in Annex D.

---------------------------------end of change 1-----------------------------------

---------------------------------start of change 2-----------------------------------

# Annex D (Normative): <mgmtObj> Resource Specializations

## D.1	Introduction

## The annex is to define the structure and procedure for each <mgmtObj> resource specializations. The defined following resource specializations shall be created on the IN-CSE when the management request is performed using external management protocols. The IN-CSE further interacts with the management server to perform management requests towards the managed entity. If the management request is performed solely over the M2M Service Layer, the following resources are created on the managed entity if the managed entity is equipped with a CSE. If the managed entities are non-oneM2M Nodes, the resources are created on the MN-CSE of the managed entity. The details can be referenced to TS0001[6].

## D.2	Resource [firmware]

D.2.1	Introduction

The detailed description can be found in clause D.2 of Architecture TS-0001 [6].

Table D.2-1: Data Type Definition of [firmware]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| firmwareType | CDT-firmware-v1_0_0-<<date of published>>.xsd |  |

Table D.2-2: Data Types for resource specific attributes

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | NP | NP | See clause 7.3.13 | Fixed string “firmware” |
| objectID | O | O | NP | NP | See clause 7.3.13 |  |
| objectPath | O | O | NP | NP | See clause 7.3.13 |  |
| description | O | O | O | NP | See clause 7.3.13 |  |
| version | M | O | O | NP | xs:string |  |
| name | M | O | O | NP | xs:string |  |
| URL | M | O | O | NP | xs:anyURI |  |
| update | M | NP | O | NP | xs:boolean |  |
| updateStatus | NP | O | O | NP | m2m:actionStatus |  |

D.2.2	Resource Specific Procedure on CRUD Operations

When management is performed using external management technologies, procedures defined in 7.3.14.2 <mgmtObj> specific procedures shall be used. The following clauses define additional procedures besides generic procedure defined in 7.2.1.2.

D.2.2.1 Create

Originator:

No change from the generic procedures in clause 7.2.1.2.1

Receiver:

Primitive specific step after generic procedure defined in 7.2.1.2.2:

May start to download the firmware image from the location indicated by attribute URL in the firmware resource.

#### D.2.2.2 Update

Originator:

No change from the generic procedures in clause 7.2.1.2.1

Receiver:

Primitive specific operation additional to Recv-6.5 “Create/Update/Retrieve/Delete/Notify operation is performed”:

When the attribute update of the firmware resource is updated to TRUE, use the downloaded firmware image to update the current using firmware. The Receiver may need to update the fwVersion attribute of the deviceInfo resource if needed.

#### D.2.2.3 Retrieve

Originator:

No change from the generic procedures in clause 7.2.1.2.1

Receiver:

#### No change from the generic procedures in clause 7.2.1.2.2

D.2.2.4 Delete

Originator:

No change from the generic procedures in clause 7.2.1.2.1

Receiver:

Primitive specific step after generic procedure defined in 7.2.1.2.2:

## Delete the downloaded firmware image locally.D.3	Resource [software]

D.3.1	IntroductionThe detailed description can be found in clause D.3 of Architecture TS-0001 [6].

Table D.3-1: Data Type Definition of [software]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| softwareType | CDT-software-v1_0_0-<<date of published>>.xsd |  |

Table D.3-2: Data Types for resource specific attributes

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | NP | NP | See clause 7.3.13 | Fixed string “software” |
| objectID | O | O | NP | NP | See clause 7.3.13 |  |
| objectPath | O | O | NP | NP | See clause 7.3.13 |  |
| description | O | O | O | NP | See clause 7.3.13 |  |
| version | M | O | O | NP | xs:string |  |
| name | M | O | O | NP | list of xs:anyURI |  |
| URL | M | O | O | NP | xs:anyURI |  |
| install | NP | NP | O | NP | xs:boolean |  |
| uninstall | NP | NP | O | NP | xs:boolean |  |
| installStatus | NP | O | NP | NP | m2m:actionStatus |  |
| activate | NP | NP | O | NP | xs:boolean |  |
| deactivate | NP | NP | O | NP | xs:boolean |  |
| activateStatus | NP | O | NP | NP | m2m:actionStatus |  |

### D.3.2	Resource Specific Procedure on CRUD Operations

### When management is performed using external management technologies, procedures defined in 7.3.14.2 <mgmtObj> specific procedures shall be used. The following clauses define additional procedures besides generic procedure defined in 7.2.1.2.

#### D.3.2.1 Create

Originator:

No change from the generic procedures in clause 7.2.1.2.1

Receiver:

Primitive specific step after generic procedure defined in 7.2.1.2.2:

May start to download the software package from the location indicated by attribute URL in the software resource.

#### D.3.2.2 Update

Originator:

No change from the generic procedures in clause 7.2.1.2.1

Receiver:

#### Primitive specific operation additional to Recv-6.5 “Create/Update/Retrieve/Delete/Notify operation is performed”:

#### When the attribute install of the software resource is updated to TRUE, install the software package downloaded from the address indicated by attribute URL of the software resource.

When the attribute uninstall of the software resource is updated to TRUE, uninstall the corresponding software of the software resource.

#### When the attribute activate of the software resource is updated to TRUE, activate the corresponding software of the software resource.

When the attribute deactivate of the software resource is updated to TRUE, deactivate the corresponding software of the software resource.

The Receiver may need to update the swVersion attribute of the deviceInfo resource if needed.

#### D.3.2.3 Retrieve

Originator:

No change from the generic procedures in clause 7.2.1.2.1

Receiver:

#### No change from the generic procedures in clause 7.2.1.2.2

#### D.3.2.4 Delete

Originator:

No change from the generic procedures in clause 7.2.1.2.1

Receiver:

Primitive specific step after generic procedure defined in 7.2.1.2.2:

Delete the downloaded software package locally.

## D.4	Resource [memory]

## D.4.1	Introduction

The detailed description can be found in clause D.4 of Architecture TS-0001 [6].

Table D.4-1: Data Type Definition of [memory]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| memoryType | CDT-memory-v1_0_0-<<date of published>>.xsd |  |

Table D.4-2: Data Types for resource specific attributes

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | NP | NP | See clause 7.3.13 | Fixed string “memory” |
| objectID | O | O | NP | NP | See clause 7.3.13 |  |
| objectPath | O | O | NP | NP | See clause 7.3.13 |  |
| description | O | O | O | NP | See clause 7.3.13 |  |
| memAvailable | M | O | O | NP | xs:unsignedLong | Unit: Byte. |
| memTotal | M | O | O | NP | xs:unsignedLong | Unit: Byte. |

### D.4.2	Resource Specific Procedure on CRUD Operations

### When management is performed using external management technologies, procedures defined in 7.3.14.2 <mgmtObj> specific procedures shall be used. The following clauses define additional procedures besides generic procedure defined in 7.2.1.2.

#### D.4.2.1 Create

Originator:

No change from the generic procedures in clause 7.2.1.2.1

Receiver:

#### No change from the generic procedures in clause 7.2.1.2.2

#### D.4.2.2 Update

Originator:

No change from the generic procedures in clause 7.2.1.2.1

Receiver:

#### No change from the generic procedures in clause 7.2.1.2.2

#### D.4.2.3 Retrieve

Originator:

No change from the generic procedures in clause 7.2.1.2.1

Receiver:

#### No change from the generic procedures in clause 7.2.1.2.2

#### D.4.2.4 Delete

Originator:

No change from the generic procedures in clause 7.2.1.2.1

Receiver:

No change from the generic procedures in clause 7.2.1.2.2

## D.5	Resource [areaNwkInfo]

D.5.1	IntroductionThe detailed description can be found in clause D.5 of Architecture TS-0001 [6].

Table D.5-1: Data Type Definition of [areaNwkInfo]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| areaNwkInfoType | CDT-areaNwkInfo-v1_0_0-<<date of published>>.xsd |  |

Table D.5-2: Data Types for resource specific attributes

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | NP | NP | xs:string | “areaNwkInfo” |
| objectID | O | O | NP | NP | xs:string (See clause 7.3.14) |  |
| objectPath | O | O | NP | NP | xs:string (See clause 7.3.14) |  |
| description | O | O | O | NP | xs:string (See clause 7.3.14) |  |
| areaNwkType | M | O | O | NP | xs:string |  |
| listOfDevices | M | O | O | NP | list of xs:anyURI |  |

### D.5.2	Resource Specific Procedure on CRUD Operations

### When management is performed using external management technologies, procedures defined in 7.3.14.2 <mgmtObj> specific procedures shall be used. The following clauses define additional procedures besides generic procedure defined in 7.2.1.2.

#### D.5.2.1 Create

Originator:

No change from the generic procedures in clause 7.2.1.2.1

Receiver:

#### No change from the generic procedures in clause 7.2.1.2.2

#### D.5.2.2 Update

Originator:

No change from the generic procedures in clause 7.2.1.2.1

Receiver:

#### No change from the generic procedures in clause 7.2.1.2.2

#### D.5.2.3 Retrieve

Originator:

No change from the generic procedures in clause 7.2.1.2.1

Receiver:

No change from the generic procedures in clause 7.2.1.2.2

#### D.5.2.4 Delete

Originator:

No change from the generic procedures in clause 7.2.1.2.1

Receiver:

No change from the generic procedures in clause 7.2.1.2.2

## D.6	Resource [areaNwkDeviceInfo]

D.6.1	Introduction

The detailed description can be found in clause D.6 of Architecture TS-0001 [6].

Table D.6-1: Data Type Definition of [areaNwkDeviceInfo]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| areaNwkDeviceInfoType | CDT-areaNwkDeviceInfo-v1_0_0-<<date of published>>.xsd |  |

Table D.6-2: Data Types for resource specific attributes

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | NP | NP | xs:string | “areaNwkDeviceInfo” |
| objectID | O | O | NP | NP | xs:string (See clause 7.3.14) |  |
| objectPath | O | O | NP | NP | xs:string (See clause 7.3.14) |  |
| description | O | O | O | NP | xs:string (See clause 7.3.14) |  |
| devID | M | O | O | NP | xs:string |  |
| devType | M | O | O | NP | xs:string |  |
| areaNwkId | M | O | O | NP | xs: anyURI |  |
| sleepInterval | O | O | O | NP | xs:NonNegativeInteger | Unit: second |
| sleepDuration | O | O | O | NP | xs:NonNegativeInteger | Unit: second |
| Status | O | O | O | NP | xs:string |  |
| listOfNeighbors | M | O | O | NP | list of xs:anyURI |  |

### D.6.2	Resource Specific Procedure on CRUD Operations

### When management is performed using external management technologies, procedures defined in 7.3.14.2 <mgmtObj> specific procedures shall be used. The following clauses define additional procedures besides generic procedure defined in 7.2.1.2.

#### D.6.2.1 Create

Originator:

No change from the generic procedures in clause 7.2.1.2.1

Receiver:

#### No change from the generic procedures in clause 7.2.1.2.2

#### D.6.2.2 Update

Originator:

No change from the generic procedures in clause 7.2.1.2.1

Receiver:

Primitive specific operation additional to Recv-6.5 “Create/Update/Retrieve/Delete/Notify operation is performed”:

#### When the attribute listOfNeighbors of the [areaNwkDeviceInfo] is updated, the receiver shall modify the corresponding connection relationship among devices in the M2M Area Network by sending signals to non-oneM2M Nodes which is out of scope of oneM2M. According to the response from the non-oneM2M nodes of the modify signal, the receiver shall corresponding update the [areaNwkDeviceInfo] resource which may include the update of the listOfNeighbors and the devType attribute. The modify may include change of the attach point of the device or removal from the area network.

#### D.6.2.3 Retrieve

Originator:

No change from the generic procedures in clause 7.2.1.2.1

Receiver:

#### No change from the generic procedures in clause 7.2.1.2.2

#### D.6.2.4 Delete

Originator:

No change from the generic procedures in clause 7.2.1.2.1

Receiver:

No change from the generic procedures in clause 7.2.1.2.2

## D.7	Resource [battery]

### D.7.1	Introduction

The detailed description can be found in clause D.7 of Architecture TS-0001 [6].

Table D.7-1: Data Type Definition of [battery]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| batteryType | CDT-battery-v1_0_0-<<date of published>>.xsd |  |

Table D.7-2: Data Types for resource specific attributes

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | NP | NP | See clause 7.3.13 | Fixed string “memory” |
| objectID | O | O | NP | NP | See clause 7.3.13 |  |
| objectPath | O | O | NP | NP | See clause 7.3.13 |  |
| description | O | O | O | NP | See clause 7.3.13 |  |
| batteryLevel | M | O | O | NP | Xs:unsignedInt | Range: 0-100 Unit: Percent |
| batteryStatus | M | O | O | NP | m2m:batteryStatus |  |

### D.7.2	Resource Specific Procedure on CRUD Operations

### When management is performed using external management technologies, procedures defined in 7.3.14.2 <mgmtObj> specific procedures shall be used. The following clauses define additional procedures besides generic procedure defined in 7.2.1.2.

#### D.7.2.1 Create

Originator:

No change from the generic procedures in clause 7.2.1.2.1

Receiver:

#### No change from the generic procedures in clause 7.2.1.2.2

#### D.7.2.2 Update

Originator:

No change from the generic procedures in clause 7.2.1.2.1

Receiver:

#### No change from the generic procedures in clause 7.2.1.2.2

#### D.7.2.3 Retrieve

Originator:

No change from the generic procedures in clause 7.2.1.2.1

Receiver:

#### No change from the generic procedures in clause 7.2.1.2.2

#### D.7.2.4 Delete

Originator:

No change from the generic procedures in clause 7.2.1.2.1

Receiver:

No change from the generic procedures in clause 7.2.1.2.2

## D.8	Resource [deviceInfo]

### D.8.1	Introduction

The Resource [deviceInfo] is used to provide information regarding the device.

The detailed description can be found in clause D.8 of Architecture TS-0001 [6].

Table D.8-1: Data Type Definition of [deviceInfo]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| deviceInfoType | CDT-deviceInfo-v1_0_0-<<date of published>>.xsd |  |

Table D.8-2: Data Types for resource specific attributes

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | NP | NP | See table 7.3.13.1-2 | Fixed string "deviceInfo" |
| objectID | O | O | NP | NP | See table 7.3.13.1-2 |  |
| objectPath | O | O | NP | NP | See table 7.3.13.1-2 |  |
| description | O | O | O | NP | See table 7.3.13.1-2 |  |
| deviceLabel | M | O | O | NP | xs:string |  |
| manufacturer | M | O | O | NP | xs:string |  |
| model | M | O | O | NP | xs:string |  |
| deviceType | M | O | O | NP | xs:string |  |
| fwVersion | M | O | O | NP | xs:string |  |
| swVersion | M | O | O | NP | xs:string |  |
| hwVersion | M | O | O | NP | xs:string |  |

### D.8.2	Resource Specific Procedure on CRUD Operations

### When management is performed using external management technologies, procedures defined in 7.3.14.2 <mgmtObj> specific procedures shall be used. The following clauses define additional procedures besides generic procedure defined in 7.2.1.2.

#### D.8.2.1 Create

Originator:

No change from the generic procedures in clause 7.2.1.2.1

Receiver:

No change from the generic procedures in clause 7.2.1.2.2

#### D.8.2.2 Update

Originator:

No change from the generic procedures in clause 7.2.1.2.1

Receiver:

No change from the generic procedures in clause 7.2.1.2.2

#### D.8.2.3 Retrieve

Originator:

No change from the generic procedures in clause 7.2.1.2.1

Receiver:

No change from the generic procedures in clause 7.2.1.2.2

#### D.8.2.4 Delete

Originator:

No change from the generic procedures in clause 7.2.1.2.1

Receiver:

No change from the generic procedures in clause 7.2.1.2.2

## D.9	Resource [deviceCapability]

### D.9.1	Introduction

The Resource [deviceCapability] is used to provide information regarding the device.

The detailed description can be found in clause D.9 of Architecture TS-0001 [6].

Table D.9-1: Data Type Definition of [deviceCapability]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| deviceCapabilityType | CDT-deviceCapability-v1_0_0-<<date of published>>.xsd |  |

Table D.9-2: Data Types for resource specific attributes

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | NP | NP | See table 7.3.13.1-2 | Fixed string "deviceCapability" |
| objectID | O | O | NP | NP | See table 7.3.13.1-2 |  |
| objectPath | O | O | NP | NP | See table 7.3.13.1-2 |  |
| description | O | O | O | NP | See table 7.3.13.1-2 |  |
| capabilityName | M | O | O | NP | xs:string |  |
| attached | M | O | O | NP | xs:boolean | true: currently attached to the device false: currently dettached to the device |
| capabilityActionStatus | M | O | O | NP | m2m: actionStatus | The action (i.e., enable, disable) and the related status. See the Table 6.3.2.3 1 |
| currentState | M | O | O | NP | xs:boolean | true: the device capability is enabled false: the device capability is disabled |
| enable | O | NP | O | NP | xs:boolean | this attribute shall not have any values |
| disable | O | NP | O | NP | xs:boolean | this attribute shall not have any values |

### D.9.2	Resource Specific Procedure on CRUD Operations

### When management is performed using external management technologies, procedures defined in 7.3.14.2 <mgmtObj> specific procedures shall be used. The following clauses define additional procedures besides generic procedure defined in 7.2.1.2.

#### D.9.2.1 Create

Originator:

No change from the generic procedures in clause 7.2.1.2.1

Receiver:

#### No change from the generic procedures in clause 7.2.1.2.2

#### D.9.2.2 Update

Originator:

No change from the generic procedures in clause 7.2.1.2.1

Receiver:

Primitive specific operation additional to Recv-6.5 “Create/Update/Retrieve/Delete/Notify operation is performed”:

When the attribute enable of the deviceCapability resource is updated to TRUE, enable the device capability of the deviceCapability resource.

#### When the attribute disable of the deviceCapability resource is updated to TRUE, disable the device capability of the deviceCapability resource.

#### D.9.2.3 Retrieve

Originator:

No change from the generic procedures in clause 7.2.1.2.1

Receiver:

No change from the generic procedures in clause 7.2.1.2.2

#### D.9.2.4 Delete

Originator:

No change from the generic procedures in clause 7.2.1.2.1

Receiver:

No change from the generic procedures in clause 7.2.1.2.2

## D.10	Resource [reboot]

### D.10.1	Introduction

The Resource [reboot] is used to provide information regarding the device.

The detailed description can be found in clause D.10 of Architecture TS-0001 [6].

Table D.10-1: Data Type Definition of [reboot]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| rebootType | CDT-reboot-v1_0_0-<<date of published>>.xsd |  |

Table D.10-2: Data Types for resource specific attributes

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | NP | NP | See table 7.3.13.1-2 | Fixed string "reboot" |
| objectID | O | O | NP | NP | See table 7.3.13.1-2 |  |
| objectPath | O | O | NP | NP | See table 7.3.13.1-2 |  |
| description | O | O | O | NP | See table 7.3.13.1-2 |  |
| reboot | M | NP | O | NP | xs:boolean | this attribute shall not have any values |
| factoryReset | M | NP | O | NP | xs:boolean | this attribute shall not have any values |

### D.10.2	Resource Specific Procedure on CRUD Operations

### When management is performed using external management technologies, procedures defined in 7.3.14.2 <mgmtObj> specific procedures shall be used. The following clauses define additional procedures besides generic procedure defined in 7.2.1.2.

#### D.10.2.1 Create

Originator:

No change from the generic procedures in clause 7.2.1.2.1

Receiver:

No change from the generic procedures in clause 7.2.1.2.2

#### D.10.2.2 Update

Originator:

No change from the generic procedures in clause 7.2.1.2.1

Receiver:

Primitive specific operation additional to Recv-6.5 “Create/Update/Retrieve/Delete/Notify operation is performed”:

When the attribute reboot of the [reboot] resource is updated to TRUE, reboot the corresponding node.

#### When the attribute factoryReset of the [reboot]resource is updated to TRUE, factoryReset the corresponding node.

#### D.10.2.3 Retrieve

Originator:

No change from the generic procedures in clause 7.2.1.2.1

Receiver:

No change from the generic procedures in clause 7.2.1.2.2

#### D.10.2.4 Delete

Originator:

No change from the generic procedures in clause 7.2.1.2.1

Receiver:

No change from the generic procedures in clause 7.2.1.2.2

## D.11	Resource [eventLog]

### D.11.1	Introduction

The Resource [eventLog] is used to provide information regarding the device.

The detailed description can be found in clause D.11 of Architecture TS-0001 [6].

Table D.11-1: Data Type Definition of [eventLog]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| eventLogType | CDT-eventLog-v1_0_0-<<date of published>>.xsd |  |

Table D.11-2: Data Types for resource specific attributes

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | NP | NP | See table 7.3.13.1-2 | Fixed string "eventLog" |
| objectID | O | O | NP | NP | See table 7.3.13.1-2 |  |
| objectPath | O | O | NP | NP | See table 7.3.13.1-2 |  |
| description | O | O | O | NP | See table 7.3.13.1-2 |  |
| logTypeId | M | O | O | NP | m2m:logTypeId | See Table 6.3.2.2.x-1 |
| logData | M | O | O | NP | xs:string | the content and format of this attribute is out of this specification. |
| logStatus | M | O | O | NP | m2m:logStatus | See Table 6.3.2.2.x-1 |
| logStart | M | NP | O | NP | xs:boolean | this attribute shall not have any values |
| logStop | M | NP | O | NP | xs:boolean | this attribute shall not have any values |

### D.11.2	Resource Specific Procedure on CRUD Operations

### When management is performed using external management technologies, procedures defined in 7.3.14.2 <mgmtObj> specific procedures shall be used. The following clauses define additional procedures besides generic procedure defined in 7.2.1.2.

#### D.11.2.1 Create

Originator:

No change from the generic procedures in clause 7.2.1.2.1

Receiver:

No change from the generic procedures in clause 7.2.1.2.2

#### D.11.2.2 Update

Originator:

No change from the generic procedures in clause 7.2.1.2.1

Receiver:

Primitive specific operation additional to Recv-6.5 “Create/Update/Retrieve/Delete/Notify operation is performed”:

When the attribute logStart of the [eventLog] resource is updated to TRUE, start the logging.

When the attribute logStop of the [eventLog]resource is updated to TRUE, stop the logging.

#### D.11.2.3 Retrieve

Originator:

No change from the generic procedures in clause 7.2.1.2.1

Receiver:

No change from the generic procedures in clause 7.2.1.2.2

#### D.11.2.4 Delete

Originator:

No change from the generic procedures in clause 7.2.1.2.1

Receiver:

No change from the generic procedures in clause 7.2.1.2.2

---------------------------------end of change 2-----------------------------------