| INPUT CONTRIBUTION |
| --- |
| Group Name:* | PRO WG |
| Title:* | MQTT protocol binding – primitive mapping |
| Source:* | MQTT protocol binding TS rapporteur |
| Contact: | Peter Niblett, peter_niblett@uk.ibm.com |
| Date:* | 2014-09-15 |
| Abstract:* | Pull the material that describes the mapping of the OneM2M primitives onto MQTT payloads into a clause 6.3, and provide more details on this mapping. |
| Agenda Item:* | TBD |
| Work item(s): | WI 0014 – MQTT Protocol Binding |
| Document(s) Impacted* | TS-0010 MQTT Protocol Binding Technical Specification |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree to include this material in the revised baseline for TS-0010 |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

======================== START 1ST CHANGE ===========================

### 6.2.1 	Request and Response Messages

An MQTT Control Packet consists of up to three parts: a fixed header, a variable header, a payload. The control packet format is depicted in Figure 6.2.1-1. MQTT does not have a data model to describe or constrain the content of its Application Message payloads (to that extent it is similar to a TCP socket).  Mca and Mcc request messages shall be serialized into XML or JSON following the serialization process defined in clause 6.3.

======================== END 1ST CHANGE ===========================

======================== START 2ND CHANGE ===========================

### 6.2.2 	Sending a Request

A request is transmitted by sending it as an MQTT PUBLISH protocol packet to the MQTT Server. It uses a Topic that identifies the Receiver of the request. The precise structure of this Topic is FFS, but an initial suggestion is:

/oneM2M/req/<to>

- “oneM2M” is a literal string identifying the topic as being used by oneM2M

- <to> is the URI of the target resource (it is assumed that this includes the AE or CSE id)

- “req” is a literal string identifying this as a request.

NOTE: It might be useful to include some other components in the topic name, such as the Operation type. In particular it might be useful to include a <fr> field for security purposes. This is FFS.

The payload of the MQTT publish packet is used to carry the request primitive, as described in clause 6.3.

### 6.2.3 	Listening for and responding to a Request

A Receiver listens for requests arriving via MQTT by subscribing to its Topic (as described in the previous clause). In the case or Read, Update or Delete this is straightforward, as there should be a resource already in existence. In the case of Create, the Originator will publish to a topic that hasn’t previously been used, so in order to see that (and thus be able to process the Create), the CSE will subscribe using the wildcarded topic filter /oneM2M/req/#.

When it receives a request, the receiver shall check the request expiration timestamp (if any) contained in the request, since it is possible that that time might have passed while the message was being stored by MQTT.

It then transmits a response by sending an MQTT PUBLISH packet to a response topic. This takes the form

/oneM2M/resp/<to>

- “oneM2M” is a literal string identifying the topic as being used by oneM2M

- <to> is the URI of the originator of the request (or the rd information from the request)

- “resp” is a literal string identifying this as a response.

The originator (or other interested party) must subscribe to this topic if it is to see the response.

The payload of the MQTT publish packet is used to carry the response primitive, as described in clause 6.3.

======================== END 2ND CHANGE ===========================

======================== START 3RD CHANGE ===========================

6.3	Primitive Mapping

### 6.3.1 	Request primitives

A oneM2M request primitive is made up of a number of control parameters and (optionally) a content part. All the parameters in these parts are serialized into the payload of an MQTT Publish Packet, using the rules given in clause 8 of [3].

All the parameters that are present in the primitive shall be serialized, in particular the request shall contain the Operation parameter to indicate whether it is a Create, Read, Update or Delete.

Figure 6.2.2-1 MQTT Request example

### 6.3.2 	Response primitives

A oneM2M response primitive is serialized using the rules given in clause 8 of [3].

In particular, each response primitive shall include the Response Code parameter to indicate success or failure of the operation.

======================== END 3RD CHANGE ===========================

# Comments

Text moved to new clause 6.3

Text moved from the previous clause 6.2.5

Text moved to new clause 6.3