| CHANGE REQUEST |
| --- |
| Group Name:* | WG3 (PRO) |
| Source:* | QUALCOMM Incorporated (TIA) |
| Format:* | PRO#13.4 |
| Date:* | 2014-10-28 |
| Contact:* | Nobu Uchida, nuchida@qti.qualcomm.com |
| Reason for Change/s:* | Correction to Request/Response message parameter data types |
| CR against: Release* | 1 |
| CR against: TS/TR* | TS-0004 - V-0.7.1 |
| Clauses/Sub Clauses* | 6.4 Message parameter data types |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Clause 6.4 defines data types for Request/Response message parameters. This CR proposes;

- Make the parameter names consistent with Architecture TS. Please note that it’s not consistent within Architecture TS, we should use the parameter names in the description part, not in the Table in Arc TS.

- Delete short name from the tables since it’s already covered by Section 8.2.

- Correction to wrong data types.

- Add reference to data types in Core Protocol TS.

- Delete filterCriteria table as it’s a duplication with Section 6.3.4.1.

- Update editor’s nores.

- Define m2m:primitiveType as an enumeration data type

### -----------------------Start of change 1-------------------------------------------

## Message parameter data types

This clause specifies the message parameter data types for messages, which cross the Mca and Mcc reference points.

Editor’s Note: This is per ARC TS, what about Mcc’?

### Request message parameter data types

The data Types of request message parameters are specified in this clause.

Detailed request message parameter descriptions and usage can be found in clause 8.1.2 of the Architecture TS [6].

Table 6.4.1-1:  Data Types for Request message parameters

| Request message parameter |  | Data Type |  | Comment |
| --- | --- | --- | --- | --- |
| Content |  | m2m:content |  | See 6.3.4.6 |
| Delivery Aggregation |  | xs:boolean |  |  |
| Discovery Result Type |  | m2m:discResType |  | See 6.3.3.2.8 |
| Event Category |  | m2m:eventCat |  | See 6.3.4.2 |
| Filter Criteria |  | m2m:filterCriteria |  | See 6.3.4.1 |
| From |  | m2m:ID |  | See 6.3.2 |
| Group Request Identifier |  | xs:string |  |  |
| Name |  | xs:string |  |  |
| Operation |  | m2m:operation |  | See 6.3.3.2.5 |
| Operational Execution Timestamp |  | m2m:timestamp |  |  |
| Originating Timestamp |  | m2m:timestamp |  |  |
| Primitive Type |  | m2m:primitiveType |  | This is an additional parameter defined only in this TS. See 6.3.3.2.33 |
| Request Message Expiration Timestamp |  | m2m:timestamp |  | “Result ExpirationTimestamp” shall be later than “Request Expiration Timestamp” |
| Request Identifier |  | m2m:requestID |  | See 6.3.2 |
| Resource Type |  | m2m:resourceType |  | See 6.3.3.2.1 |
| Response Message Type |  | m2m:responseType |  | See 6.3.3.2.6 |
| Result Content |  | m2m:resultContent |  | See 6.3.3.2.7 |
| Result Expiration Timestamp |  | m2m:timestamp |  |  |
| Response Persistence |  | xs:duration |  |  |
| Role |  | xs:string |  | Editor’s Note: Missing procedure in ARC TS |
| To |  | xs:anyURI |  |  |

Editor’s Note: This list is from ARC TS 1.2.0 and may need updating.

### Response message parameter data types

The data types of response message parameters are specified in this clause.

Detailed response message parameter descriptions and usage can be found in clause 8.1.3 of the Architecture TS [6].

Table 6.4.2-1: Data Types for Response primitive parameters

| Response primitive parameter |  | Data Type |  | Comment |
| --- | --- | --- | --- | --- |
| Content |  | m2m:content |  | See 6.3.4.6 |
| Event Category |  | m2m:eventCat |  | See 6.3.4.2 |
| From |  | m2m:ID |  | See 6.3.2 |
| Originating Timestamp |  | m2m:timestamp |  |  |
| Primitive Type |  | m2m:primitiveType |  | This is an additional parameter defined only in this TS. See 6.3.3.2.33 |
| Request Identifier |  | m2m:requestID |  | See 6.3.2 |
| Result Expiration Timestamp |  | m2m:timestamp |  |  |
| To |  | xs:anyURI |  |  |
| Response Status Code |  | m2m:responseStatus |  | See 6.3.4.15 |

Editor’s Note: This list is from ARC TS 1.2.0 (less status codes) and may need updating.

## -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

##### m2m:primitiveType

Used for primitiveType parameter in request/response messages.

Table 6.3.3.2.33-1: Interpretation of primitiveType

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | REQUEST |  |
| 2 | RESPONSE |  |
| See Cluase 6.3 “Message parameter data types” |

## -----------------------End of change 2---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?