| CHANGE REQUEST |
| --- |
| Group Name:* | PRO14.0 |
| Source:* | Gemalto N.V. (ETSI) |
| Format:* | Plenary Face-to-face |
| Date:* | 2014-11-09 |
| Contact:* | Francois Ennesser, Gemalto (francois.ennesser@gemalto.com) |
| Reason for Change/s:* | Some statements related to Security in PRO TS-0008 are not in line with the latest evolutions of SEC TS-0003. |
| CR against: Release* | Rel. 1 |
| CR against: TS/TR* | TS-0008 V-0.5.0 |
| Clauses/Sub Clauses* | 7 and sub-clauses |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Section 7 of TS-0008 needs to be aligned with current version of TS-0003.

### -----------------------Start of change 1-------------------------------------------

# 7	Security Consideration

CoAP itself does not provide protocol primitives for authentication or authorization; where this is required, it shall be provided by DTLS.

Just as HTTP is secured using Transport Layer Security (TLS) over TCP, CoAP shall be secured using Datagram TLS (DTLS) [5].

All CoAP messages shall be sent as DTLS “application data”. For matching an ACK or RST to a CON message or a RST to a NON message: The DTLS session shall be the same and the epoch shall be the same.

For matching a response to a request, the DTLS session shall be the same and the epoch shall be the same. The response to a DTLS secured request shall always be DTLS secured using the same security session and epoch.

OneM2M primitive parameters contained in CoAP messages may be protected by DTLS in a hop-by-hop manner. For the details, see the oneM2M Security solution specifications. [4].

NOTE: Though some provisioning schemes of TS-0003 enable the provisioning of end-to-end credentials, the usage of such credentials in the present release is M2M application specific, as protocols to establish security associations between non-adjacent nodes are not specified.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?