| INPUT CONTRIBUTION |
| --- |
| Group Name:* | PRO |
| Title:* | CoAP Option Cleanup |
| Source:* | LG Electronics |
| Contact: | Seongyoon Kim, LG Electronics, seongyoon.kim@lge.com |
| Date:* | 2014-10-31 |
| Abstract:* | CoAP Option Cleanup |
| Agenda Item:* | PRO |
| Work item(s): | WI 0009 |
| Document(s) Impacted* | Technical Specification – Core Protocol (Draft version 0.7.1) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Approve the proposed change and integrate it into the TS document |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Rationale

- Token

Endpoints of CoAP communication have 0 hop relationship, token is only valid between Registrar and Registree (not end-to-end manner). However request identifier is valid between Originator and Hosting CSE ( can’t map request identifier to token

- URI

ARC WG has had a consensus on how to forward a request/response.

pointOfAccess will be mapped to URI of host and port, and to will be mapped to URI of path.

========================Start of 1st Change==========================

## Configuration of Options and Query String

This clause describes which information needs configuring to which CoAP options or query string.

## 6.2.1	Content Format Negotiation Options

The CoAP Accept option can be used to indicate which Content-Format is acceptable to an Originator. If a Hosting CSE supports the Content-Format specified in Accept option of the request, the Hosting CSE shall respond with that Content-Format. If the Hosting CSE doesn’t support the Content-Format specified in Accept option of the request, 4.06 "Not Acceptable" MUST be sent as a response, unless another error code takes precedence for this response.

Editor’s note: which content format supported in oneM2M needs to be clarified.

## 6.2.2	Token

Token option is used to match between a request and a response(s) in hop-by-hop manner. If rt parameter is configured as nonBlockingRequestSynch or nonBlockingRequestAsynch, Token option shall be included in a request and a corresponding response.

## 6.2.3	URI Options

This clause describes how to configure CoAP Uri-Host, Uri-Port, Uri-Path, and Uri-Query.

Host and port part of the address specified in pointOfAccess attribute of <remoteCSE> resource shall be mapped to Uri-Host and Uri-Port respectively.

to parameter is mapped to Uri-Path, and query strings specified in clause 6.2.4 are serialized to Uri-Query.

## 6.2.4	Query String

da, dr, ec, fc, fr, gid, nm, oet, ort, ret, rqt, rst, rc, ret, rp, ri and ro (see core protocol specification [2]) shall be carried in query string.

========================End of 1st Change==========================