| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG3 Protocols |
| Title:* | PRO-2014-0550-6_3_Response_Code_Mapping_Cleanup |
| Source:* | Hitachi |
| Contact: | He Xuan, xhe@hitachi.cn |
| Date:* | 2014-11-01 |
| Abstract:* | This contribution proposes modification of response code mapping cleanup based on V0_5_0. |
| Agenda Item:* | Contributions |
| Work item(s): | WI 0012 |
| Document(s) Impacted* | oneM2M-TS-0008-CoAP Protocol Binding |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | <A concise statement of the decision required or the recommended action to be taken> |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution proposes CoAP protocol binding related part to TS-0008.

--------------------- Start of proposed modified text -------------------

## 6.3	Response Codes Mapping

## 6.3.1	Response Primitive to CoAP Response

The response primitive shall be correlated to the corresponding request primitive and the following rules shall be followed:

- The CoAP response shall be correlated to the CoAP request corresponding to the request primitive.

- If the response primitive has any resource representation, this shall be transported in the payload of the CoAP response.

- The status code of the response for successful and unsuccessful response shall be set according to the table below.

If the request is send from originator, Table 6.3.1-1 shall be used for mapping as successful cases, and Table 6.3.1-2 shall be used for unsuccessful cases:

# Table 6.3.2-1 Successful Cases

| Status Code | Status Code of CoAP |
| --- | --- |
| STATUS_CREATED | 2.01 Created |
| STATUS_ DELETED | 2.02 Deleted |
| STATUS_CHANGED | 2.04 Changed |
| STATUS_CONTENT | 2.05 Content |
| STATUS_ACCEPTED | ACK |

# Table 6.3.2-2 Unsuccessful Cases

| Status Code | Status Code of CoAP |
| --- | --- |
| 2000 Location info not authorized | 4.01 Unauthorized |
| 2001 Unsupported resource | 5.01 Not Implemented |
| 2002 Unsupported attribute | 5.01 Not Implemented |
| 2003 Target not reachable | 5.05 Proxying Not Supported |
| 2004 Cannot forward, other reason | 5.00 Internal Server Error |
| 2005 No privilege | 4.01 Unauthorized |
| 2006 Already exists | 4.12 Precondition Failed |
| 2007 Create error - missing mandatory parameter | 4.02 Bad Option |
| 2009 Does not exist | 4.04 Not Found |
| 2012 Update error - unacceptable contents | 4.06 Not Acceptable |
| 2015 Create delivery - not able to take on responsibility | 4.01 Unauthorized |
| 2016 Group request identifier exists | 4.12 Precondition Failed |
| 2022 External Object not reachable | 5.02 Bad Gateway |
| 2023 Create mgmtObj - memory shortage | 4.13 Request Entity Too Large |
| 2028 External Object not found | 4.04 Not Found |
| 2031 Cancel execInstance - not cancellable | 4.03 Forbidden |
| 2032 Cancel execInstance - already complete | 4.00 Bad Request |
| 2033 Delete execInstance - not cancellable | 4.03 Forbidden |
| 2034 Delete execInstance - already complete | 4.00 Bad Request |
| 2035 Retrieve CSEBase - format error | 4.15 Unsupported Content-Format |
| 2036 CMDH rules -non compliant | 4.00 Bad Request |
| 2037 Target is not subscribable | 4.05 Method Not Allowed |
| 2038 Cannot initiate subscription verification | 5.03 Service Unavailable |
| 2039 Subscription verification failed - Originator | 5.03 Service Unavailable |
| 4040 Subscription verification failed - Creator | 4.00 Bad Request |
| 2040 Max number of member exceeded | 4.00 Bad Request |
| 2041 Member type inconsistent | 4.00 Bad Request |
| 2042 Management session cannot be established | 5.03 Service Unavailable |
| 2043 Management session establishment timeout | 5.04 Gateway Timeout |

Add OneM2M response code numbering

## 6.3.2	CoAP Response Code to oneM2M Response Code

If the CoAP response code is in the range 2.01 to 2.05, then the response shall be considered as a successful case. Table 6.3.2-1 shall be used for successful cases mapping.

Table 6.3.2-1 Successful Cases

| CoAP Response Code | oneM2M Response Code | Note |
| --- | --- | --- |
| Success 2.xx | 2.01 Created | STATUS_CREATED |  |
|  | 2.02 Deleted | STATUS_ DELETED |  |
|  | 2.03 Valid | - | Same as HTTP304 Not Modified |
|  | Changed | STATUS_CHANGED |  |
|  | 2.05 Content | STATUS_CONTENT |  |

If the CoAP response code is in the range of 4.00 to 4.15 or 5.00 to 5.05, then the response shall be considered as unsuccessful. Table 6.3.2-2 shall be used for unsuccessful cases mapping. Additional information about the error should be included.

Table 6.3.2-2 Successful Cases

| CoAP Response Code | oneM2M Response Code | Note |
| --- | --- | --- |
| Client error | 4.00 | 2032 Cancel execInstance - already complete 2034 Delete execInstance - already complete 2036 CMDH rules -non compliant 4040 Subscription verification failed – Creator 2040 Max number of member exceeded 2041Member type inconsistent | 4.00 shall be used for multiple response, depends on parameters in additional information |
|  | 4.01 | 2000 Location info not authorized 2005 No privilege 2015 Create delivery - not able to take on responsibility | 4.01 shall be used for multiple response, depends on parameters in additional information |
|  | 4.02 | 2007 Create error - missing mandatory parameter |  |
|  | 4.03 | 2031 Cancel execInstance - not cancellable 2033 Delete execInstance - not cancellable | 4.03 shall be used for multiple response, depends on parameters in additional information |
|  | 4.04 | 2009 Does not exist 2028 External Object not found | 4.04 shall be used for multiple response, depends on parameters in additional information |
|  | 4.05 | 2037 Target is not subscribable |  |
|  | 4.06 | 2012 Update error - unacceptable contents |  |
|  | 4.12 | 2006 Already exists 2016 Group request identifier exists | 4.12 shall be used for multiple response, depends on parameters in additional information |
|  | 4.13 | 2023 Create mgmtObj - memory shortage |  |
|  | 4.15 | 2035 Retrieve CSEBase - format error |  |
| Server error | 5.00 | 2004 Cannot forward, other reason |  |
|  | 5.01 | 2001 Unsupported resource 2002 Unsupported attribute | 5.01 shall be used for multiple response, depends on parameters in additional information |
|  | 5.02 | 2022 External Object not reachable |  |
|  | 5.03 | 2038 Cannot initiate subscription verification 2039 Subscription verification failed – Originator 2042 Management session cannot be established | 5.03 shall be used for multiple response, depends on parameters in additional information |
|  | 5.04 | 2043 Management session establishment timeout |  |
|  | 5.05 | 2003 Target not reachable |  |

Add OneM2M response code numbering

## 6.3.3	Additional Information

CoAP message includes the 8-bit Code.  In case of a request, the Code field shall indicate the Request Method; in case of a response, the Code field shall indicate a Response Code.

The Code field is limited to indicate all oneM2M response code, so additional information shall be carried via the CoAP payload field.

--------------------- End of proposed modified text ---------------------