| CHANGE REQUEST |
| --- |
| Group Name:* | PRO |
| Source:* | FUJITSU |
| Format:* | Face-to-Face Meeting |
| Date:* | 2014-11-03 |
| Contact:* | Shingo Fujimoto, FUJITSU, shingo_fujimoto@jp.fujitus.com |
| Reason for Change/s:* | Structured Filter Criteria definition should be changed. |
| CR against: Release* | v.0.7.2 |
| CR against: TS/TR* | TS-0004 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The ‘Filter Criteria’ cannot be applied on RETEIVE operation in HTTP and CoAP operation with current sepecification since GET operation won’t take body content with structured data.

This contribution proposed to change the definition of Fileter Criteria as concept instead of structured data.

Following definition texts of fc(filter criteria) are cited from “clause 8.1.2 Request” in architecture TS.

- fc: optional filter criteria: conditions for filtered retrieve operation are described in table 8.1.2-1. This is used for resource discovery (clause 10.2.6) and general retrieve, update, delete requests (clause 10.1.2, 10.1.3 and 10.1.4).

Example usage of retrieve requests with filter criteria using modifiedSince condition tag: if a target resource is modified since 12:00 then the Hosting CSE will send a resource representation.

Disrestype: Optional Discovery result format. This parameter applies to discovery related requests (see clause 10.2.6) to indicate the preference of the Originator for the format of returned information in the result of the operation. This parameter shall take on one of the following values reflecting the options in clause 9.3.1:

Hierarchical URI option.

Non-hierarchical URI option.

CSE-ID, and resource identifier option.

For example if Disrestype is set to Non-hierarchical URI option, then the request Originator indicates that the discovered resources should be in the form of Non-hierarchical URI.

The absence of the parameter implies that the result shall be in Hierarchical URI format.

Table 8.1.2-1: filterCriteria conditions

| Condition tag | Multiplicity | Matching condition |
| --- | --- | --- |
| createdBefore | 0..1 | The creationTime attribute of the resource is chronologically before the specified value. |
| createdAfter | 0..1 | The creationTime attribute of the resource is chronologically after the specified value. |
| modifiedSince | 0..1 | The lastModifiedTime attribute of the resource is chronologically after the specified value. |
| unmodifiedSince | 0..1 | The lastModifiedTime attribute of the resource is chronologically before the specified value. |
| stateTagSmaller | 0..1 | The stateTag attribute of the resource is smaller than the specified value. |
| stateTagBigger | 0..1 | The stateTag attribute of the resource is bigger than the specified value. |
| expireBefore | 0..1 | The expirationTime attribute of the resource is chronologically before the specified value. |
| expireAfter | 0..1 | The expirationTime attribute of the resource is chronologically after the specified value. |
| labels | 0..n | The labels attributes of the resource matches the specified value. |
| resourceType | 0..n | The resourceType attribute of the resource is the same as the specified value. It also allows differentiating between normal and announced resources. |
| sizeAbove | 0..1 | The contentSize attribute of the <contentInstance> resource is equal to or greater than the specified value. |
| sizeBelow | 0..1 | The contentSize attribute of the <contentInstance> resource is smaller than the specified value. |
| contentType | 0..n | The typeOfContent attribute of the <contentInstance> resource matches the specified value. |
| limit | 0..1 | Limitation the number of matching resources to the specified value. |
| attribute | 0..n | This is an attribute of resource types (clause 9.6). Therefore, a real tag name is variable and depends on its usage. E.g. creator of container resource type can be used as a filter criteria tag as “creator=Sam”. |
| filterUsage | 0..1 | Indicates how the filter criteria is used. E.g. if this parameter is not provided, the Retrieve operation is for generic retrieve operation. If filterUsage is provided, the Retrieve operation is for resource <discovery> (clause 10.2.6). |

The rules when multiple conditions are used together shall be as follows:

different conditions shall use the "AND" logical operation

same conditions shall use the "OR" logical operation

Below is an example usage of filter criteria conditions in a HTTP query: an HTTP GET operation can be requested applying also a filter in the query part of the request itself:

GET /root?label=one&label=two&createdBefore=2014-01-01T00:00:00&limit=128&filterUsage=discovery

The example discovers a maximum of 128 resources matching the following logical condition: createdBefore < 2014-01-01T00:00:00 AND (label = one OR label = two).

Once the Request is delivered, the Receiver shall analyze the Request to determine the target resource.

If the target resource is addressing another M2M Node, the Receiver shall route the request appropriately.

If the target resource is addressing the Receiver, it shall:

Check the existence of to addressed resource.

Identify the resource type by ty.

Check the privileges for fr Originator to perform the requested operation.

Perform the requested operation (using cn content when provided) according to the provided request parameters as described above.

Depending on the request result content, respond to the Originator with indication of successful or unsuccessful operation results. In some specific cases (e.g. limitation in the binding protocol or based on application indications), the Response could be avoided.

### -----------------------Start of change 1-------------------------------------------

### 6.3.6	Filter Criteria

The request message parameter Filter Criteria shall be specified as combination of following sub-parameters.

#### 6.3.6.1 Created Time condition

The condition matches with the resources which the createdTime attribute is chronologically in specified range.

Table 6.3.6.1-1: Defition of Create Time condition

| Format Variants | Definition | Note |
| --- | --- | --- |
| createdBefore | -YYYYMMDDhhmmss |  |
| created After | YYYYMMDDhhmmss- |  |
| createdBetween | YYYYMMDDhhmmss-YYYYMMDDhhmmss |  |
| NOTE: YYYY represents year, MM represents month, DD represents day of month, hh represets hour, mm represents minute, and ss represents second. The timezone is interpreted as UTC. |

Example) cr=-20140401150020

#### 6.3.6.2 LastModified Time condition

The condition matches with the resources which the lastModifiedTime attribute is chronologically in specified range.

Table 6.3.6.2-1: Defition of LastModified Time condition

| Format Variants | Definition | Note |
| --- | --- | --- |
| modifiedSince | YYYYMMDDhhmmss- |  |
| unmodifiedSince | -YYYYMMDDhhmmss |  |
| modifiedBetween | YYYYMMDDhhmmss-YYYYMMDDhhmmss |  |
| NOTE: YYYY represents year, MM represents month, DD represents day of month, hh represets hour, mm represents minute, and ss represents second. The timezone is interpreted as UTC. |

#### 6.3.6.3 State Tag condition

The condition matches with the <contentInstance> resources which the stateTag attribute is in specified numeric value range.

#### 6.3.6.4 Expiration Time condition

The condition matches with the expirationTime attribute of the resources is chronologically in specified chnological time range.

Table 6.3.6.2-1: Defition of ExirationTime condition

| Format Variants | Definition | Note |
| --- | --- | --- |
| exprieBefore | -YYYYMMDDhhmmss- |  |
| expireAfter | YYYYMMDDhhmmss- |  |
| expireBetween | YYYYMMDDhhmmss-YYYYMMDDhhmmss |  |
| NOTE: YYYY represents year, MM represents month, DD represents day of month, hh represets hour, mm represents minute, and ss represents second. The timezone is interpreted as UTC. |

Example) ex=20140401150020-

#### 6.3.6.5 Label Match condition

The condition matches with the resource which labels attribute contains the specified value.

Table 6.3.6.2-1: Defition of Lebel Match condition

| Format Variants | Definition | Note |
| --- | --- | --- |
| label contains | xs:token |  |
| any of label matches | list of xs:token | separator of list elements shall be specified in protocol bindings. |
| NOTE: |

#### 6.3.6.6 Resource Type Match condition

The condition matches with the resource which resourceType attribute value is specified value.

Table 6.3.6.2-1: Defition of Resource Type Match condition

| Format Variants | Definition | Note |
| --- | --- | --- |
| single type | m2m:resourceType |  |
| multiple types | list of m2m:resourceType | separator of list elements shall be specified in protocol bindings. |
| NOTE: |

#### 6.3.6.7 Content Size condtion

The condition matches with the contentSize attribute of the <contentInstance> resources is in range of specified numerica value range.

Table 6.3.6.2-1: Defition of Content Size Match condition

| Format Variants | Definition | Note |
| --- | --- | --- |
| sizeBelow | xs:nonNegativeInteger after ‘-‘ . |  |
| sizeAbove | xs:nonNegativeInteger followed by ‘-‘. |  |
| NOTE: |

#### 6.3.6.8 Content Type condition

The condition matches with the typeOfContent attribute of the <contentInstance> resource is the specified value.

Table 6.3.6.2-1: Defition of Content Type Match condition

| Format Variants | Definition | Note |
| --- | --- | --- |
| content type | xs:token | The one of the Content-Type string shall be specified |
| content sub-types | xs:token after ‘:’ character. | The one of the Content sub-type strings shall be specified. |
| NOTE: |

#### 6.3.6.9 Attribute Match condition

The condition matches with the resources which all attribute/value pairs are specified combination.

Table 6.3.6.2-1: Defition of Attribute Match condition

| Format Variants | Definition | Note |
| --- | --- | --- |
| single pair | concatenation of xs:token with ‘:’ character. | first token shall be shortname of attribute and second token shall be its value. |
| multiple pairs | list of single pairs. | separator of list elements shall be specified in protocol bindings. |
| NOTE: |

#### 6.3.6.10 Limit conditions

Limitation the number of matching resources to the specified value.

Table 6.3.6.2-1: Defition of Limit conditions

| Format Variants | Definition | Note |
| --- | --- | --- |
| limits | xs:nonNegativeInteger |  |
| NOTE: |

#### 6.3.6.11 Filter Usage

Indicates how the filter criteria is used. E.g. if this parameter is not provided, the Retrieve operation is for generic retrieve operation.

Table 6.3.3.2.33-1: Definition of Filter Usage

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | Discovery Criteria |  |
| 2 | Event Notification Criteria |  |
| NOTE: |

Editors Note: consider moving this to enumeration type definition section.

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### -----------------------End of change 2---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?