| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG3 |
| Title:* | Notifications modifications |
| Source:* | Telecom Italia, InterDigital |
| Contact: | Michele LUPANO, michele.lupano@telecomitalia.it Dale SEED, dale.seed@interdigital.com |
| Date:* | 2014-11-12 |
| Abstract:* | This contribution introduces notification enumeration value in Table 6.3.3.2.1-1 and short name in resource type short names table 8.2.4-1. |
| Agenda Item:* | Core Protocol TS |
| Work item(s): | WI-0009 |
| Document(s) Impacted* |  |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | WG members should agree on proposed resource type short names table modifications. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

============================ Introduction ============================

This contribution introduces notification enumeration value in Table 6.3.3.2.1-1 and short name in resource type short names table 8.2.4-1.

============================ Begin of change 1 ========================

Table 6.3.3.2.1-1: Interpretation of resourceType

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | accessControlPolicy |  |
| 2 | AE |  |
| 3 | container |  |
| 4 | contentInstance |  |
| 5 | CSEBase |  |
| 6 | delivery |  |
| 7 | eventConfig |  |
| 8 | execInstance |  |
| 9 | fanOutPoint |  |
| 10 | Group |  |
| 11 | localPolicy |  |
| 12 | m2mServiceSubscription |  |
| 13 | mgmtCmd |  |
| 14 | mgmtObj |  |
| 15 | Node |  |
| 16 | nodeInfo |  |
| 17 | pollingChannel |  |
| 18 | remoteCSE |  |
| 19 | Request |  |
| 20 | Schedule |  |
| 21 | statsCollect |  |
| 22 | statsConfig |  |
| 23 | Subscription |  |
| 100 | notification | This value is used to distinguish between: normal CREATE and notifications CREATE operations. |
| See Clause 6.4.1 “Request message parameter data types” |

============================ End of change 1 ==========================

============================ Begin of change 2 ========================

Table 8.2.4-1: Resource type short names

| Resource Type Name | Short Name |
| --- | --- |
| accessControlPolicy | acp |
| AE | ae |
| container | cnt |
| contentInstance | cin |
| CSEBase | csb |
| delivery | dlv |
| eventConfig | evcg |
| execInstance | exin |
| fanOutPoint | fopt |
| group | grp |
| locationPolicy | lcp |
| m2mServiceSubscriptionProfile | mssp |
| mgmtCmd | mgc |
| mgmtObj | mgo |
| node | nod |
| notification | not |
| pollingChannelURI | pcu |
| remoteCSE | csr |
| request | req |
| schedule | sch |
| serviceSubscribedNode | svsn |
| statsCollect | stcl |
| statsConfig | stcg |
| subscription | sub |
| firmware | fwr |
| software | swr |
| memory | mem |
| areaNwkInfo | ani |
| areaNwkDeviceInfo | andi |
| battery | bat |
| deviceInfo | dvi |
| deviceCapability | dvc |
| reboot | rbt |
| eventLog | evl |
| cmdhPolicy | cmp |
| activeCmdhPolicy | acmp |
| cmdhDefaults | cmdf |
| cmdhDefEcValue | cmdv |
| cmdhEcDefParamValues | cmpv |
| cmdhLimits | cml |
| cmdhNetworkAccessRules | cmnr |
| cmdhNwAccessRule | cmwr |
| cmdhBuffer | cmbf |

============================ End of change 2 ==========================