| CHANGE REQUEST |
| --- |
| Group Name:* | TP#14 PRO |
| Source:* | IBM |
| Format:* | CR |
| Date:* | <2014-11-13> |
| Contact:* | Peter Niblett, peter_niblett@uk.ibm.com |
| Reason for Change/s:* | The contribution is the clean up of mgmtObj related sections |
| CR against: Release* | <Release 1> |
| CR against: TS/TR* | TS0004 v0.7.1 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The contribution is a cleanup of mgmtObj related sections. It builds upon PRO-2014-0557.

### -----------------------Start of change 1-------------------------------------------

### Resource Type mgmtObj

#### Introduction

The <mgmtObj> resource contains management data which represents individual M2M management functions. It represents a general structure to map to external management technology data models. There are multiple specializations of  <mgmtObj>; these are defined in the Annex D. Each of these specializations has its own schema file. There is no separate schema file just for <mgmtObj>, however the XML schema types for the specializations all conform to the pattern described in this clause.

Table 7.3.14.1-1: Data Type Definitions for <mgmtObj>

| Data Type IDs | File Name | Note |
| --- | --- | --- |
| <<specialization name>> and <<specialization name>>Annc | CDT-<<specialization name>>-v1_0_0.xsd |  |

Table 7.3.14.1-2: Common Attributes on <mgmtObj>

| Attribute Name | Request Optionality | Default Value | Resource Specific Note |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| resourceType | NP | O | O | NP |  |  |
| resourceID | NP | O | O | NP |  |  |
| parentID | NP | O | NP | NP |  |  |
| accessControlPolicyIDs | O | O | NP | NP |  |  |
| creationTime | NP | O | NP | NP |  |  |
| expirationTime | O | O | O | NP |  |  |
| lastModifiedTime | NP | O | NP | NP |  |  |
| labels | O | O | O | NP |  |  |

Table 7.3.14.1-3: Resource Specific Attributes on <mgmtObj>

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | NP | NP | m2m:mgmtDefinition |  |
| objectIDs | O | O | NP | NP | List of xs:anyURI |  |
| objectPaths | O | O | NP | NP | List of xs:anyURI |  |
| description | O | O | O | NP | xs:string |  |
| mgmtLink | O | O | O | NP | m2m:mgmtLinkRef |  |

Unlike other resource attributes, the mgmtLink is permitted to occur multiple times in a resource instance.

Table 7.3.14.1-4: Child resources of <mgmtObj>

| Child Resource Type | Child Resource Name | Multiplicity | Ref. to Resource Type Definition |
| --- | --- | --- | --- |
| <subscription> | [variable] | 0..n | 7.3.7 |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

Table D.5-2: Data Types for resource specific attributes

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | NP | NP | See clause 7.3.14 | 1004 (areaNwkInfo) |
| objectID | O | O | NP | NP | See clause 7.3.14 |  |
| objectPath | O | O | NP | NP | See clause 7.3.14 |  |
| description | O | O | O | NP | See clause 7.3.14 |  |
| areaNwkType | M | O | O | NP | xs:string |  |
| listOfDevices | M | O | O | NP | list of xs:anyURI |  |

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

Table D.6-2: Data Types for resource specific attributes

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | NP | NP | See clause 7.3.14 | 1005 (areaNwkDeviceInfo) |
| objectID | O | O | NP | NP | See clause 7.3.14 |  |
| objectPath | O | O | NP | NP | See clause 7.3.14 |  |
| description | O | O | O | NP | See clause 7.3.14 |  |
| devID | M | O | O | NP | xs:string |  |
| devType | M | O | O | NP | xs:string |  |
| areaNwkId | M | O | O | NP | xs: anyURI |  |
| sleepInterval | O | O | O | NP | xs:NonNegativeInteger | Unit: second |
| sleepDuration | O | O | O | NP | xs:NonNegativeInteger | Unit: second |
| Status | O | O | O | NP | xs:string |  |
| listOfNeighbors | M | O | O | NP | list of xs:anyURI |  |

### -----------------------End of change 3-------------------------------------------

### -----------------------Start of change 4-------------------------------------------

Table D.12-2: Data Types for resource specific attributes

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | NP | NP | See clause 7.3.14 | 1011 (cmdhPolicy) |
| objectID | O | O | NP | NP | See clause 7.3.14 | See Table 7.3.14.1.2 |
| objectPath | O | O | NP | NP | See clause 7.3.14 | See Table 7.3.14.1.2 |
| description | O | O | O | NP | See clause 7.3.14 | See Table 7.3.14.1.2 |
| name | M | O | O | NP | xs:string | None |
| mgmtLink | M | O | O | NP | m2m:mgmtLinkRef | 1 link to [cmdhDefaults] resource instance, 1 or more link(s) to [cmdhLimits] resource instance(s), 1 or more link(s) to [cmdhNetworkAccessRules] resource instance(s), 1 or more link(s) to [cmdhBuffer] resource instance(s) |

The Resource Specific Procedure on CRUD Operations as specified in clause 7.3.14 for the generic <mgmtObj> resource type apply.

### -----------------------End of change 4-------------------------------------------

### -----------------------Start of change 5------------------------------------------

Table D.12.1-2: Data Types for resource specific attributes

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | NP | NP | See clause 7.3.14 | 1012 (activeCmdhPolicy) |
| objectID | O | O | NP | NP | See clause 7.3.14 | See Table 7.3.14.1.2 |
| objectPath | O | O | NP | NP | See clause 7.3.14 | See Table 7.3.14.1.2 |
| description | O | O | O | NP | See clause 7.3.14 | See Table 7.3.14.1.2 |
| mgmtLink | M | O | O | NP | m2m:mgmtLinkRef | 1 link to the instance of [cmdhPolicy] resource that is active |

### -----------------------End of change 5-------------------------------------------

### -----------------------Start of change 6-------------------------------------------

Table D.12.2-2: Data Types for resource specific attributes

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | NP | NP | See clause 7.3.14 | 1013 (cmdhDefaults) |
| objectID | O | O | NP | NP | See clause 7.3.14 | See Table 7.3.14.1-2 |
| objectPath | O | O | NP | NP | See clause 7.3.14 | See Table 7.3.14.1-2 |
| description | O | O | O | NP | See clause 7.3.14 | See Table 7.3.14.1-2 |
| mgmtLink | M | O | O | NP | m2m:mgmtLinkRef | 1 or more link(s) to [cmdhDefEcValue] resource instance(s) |

### -----------------------End of change  6-------------------------------------------

### -----------------------Start of change 7-------------------------------------------

Table D.12.3-2: Data Types for resource specific attributes

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | NP | NP | See clause 7.3.14 | 1014 (cmdhDefEcValue) |
| objectID | O | O | NP | NP | See clause 7.3.14 | See Table 7.3.14.1-2 |
| objectPath | O | O | NP | NP | See clause 7.3.14 | See Table 7.3.14.1-2 |
| description | O | O | O | NP | See clause 7.3.14 | See Table 7.3.14.1-2 |
| order | M | O | O | NP | xs:positiveInteger | None |
| defEcValue | M | O | O | NP | m2m:eventCat | None |
| requestOrigin | M | O | O | NP | m2m:listOfM2MID | None |
| requestContext | O | O | O | NP | xs:string | None |
| requestContextNotification | O | O | O | NP | xs:boolean | None |
| requestCharacteristics | O | O | O | NP | xs:string | None |

### -----------------------End of change  7-------------------------------------------

### -----------------------Start of change 8-------------------------------------------

Table D.12.4-2: Data Types for resource specific attributes

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | NP | NP | See clause 7.3.14 | 1015 (cmdhEcDefParamValues) |
| objectID | O | O | NP | NP | See clause 7.3.14 | See Table 7.3.14.1-2 |
| objectPath | O | O | NP | NP | See clause 7.3.14 | See Table 7.3.14.1-2 |
| description | O | O | O | NP | See clause 7.3.14 | See Table 7.3.14.1-2 |
| applicableEventCategory | M | O | O | NP | m2m:listOfEventCat | None |
| defaultRequestExpTime | M | O | O | NP | xs:long | -1 means infinity, unit: ms |
| defaultResultExpTime | M | O | O | NP | xs:long | -1 means infinity, unit: ms |
| defaultOpExecTime | M | O | O | NP | xs:long | -1 means infinity, unit: ms |
| defaultRespPersistence | M | O | O | NP | xs:long | -1 means infinity, unit: ms |
| defaultDelAggregation | M | O | O | NP | xs:boolean | None |

### -----------------------End of change  8-------------------------------------------

### -----------------------Start of change 9-------------------------------------------

Table D.12.5-2: Data Types for resource specific attributes

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | NP | NP | See clause 7.3.14 | 1016 (cmdhLimits) |
| objectID | O | O | NP | NP | See clause 7.3.14 | See Table 7.3.14.1-2 |
| objectPath | O | O | NP | NP | See clause 7.3.14 | See Table 7.3.14.1-2 |
| description | O | O | O | NP | See clause 7.3.14 | See Table 7.3.14.1-2 |
| order | M | O | O | NP | xs:positiveInteger | None |
| requestOrigin | M | O | O | NP | m2m:listOfM2MID | None |
| requestContext | O | O | O | NP | xs:string | None |
| requestContextNotification | O | O | O | NP | xs:boolean | None |
| requestCharacteristics | O | O | O | NP | xs:string | None |
| limitsEventCategory | M | O | O | NP | m2m:listOfEventCat | None |
| limitsRequestExpTime | M | O | O | NP | m2m:listOfMinMax | -1 means infinity, unit: ms |
| limitsResultExpTime | M | O | O | NP | m2m:listOfMinMax | -1 means infinity, unit: ms |
| limitsOpExecTime | M | O | O | NP | m2m:listOfMinMax | -1 means infinity, unit: ms |
| limitsRespPersistence | M | O | O | NP | m2m:listOfMinMax | -1 means infinity, unit: ms |
| limitsDelAggregation | M | O | O | NP | m2m:listOfBoolean | None |

### -----------------------End of change  9-------------------------------------------

### -----------------------Start of change 10-------------------------------------------

Table D.12.6-2: Data Types for resource specific attributes

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | NP | NP | See clause 7.3.14 | 1017 (cmdhNetworkAccessRules) |
| objectID | O | O | NP | NP | See clause 7.3.14 | See Table 7.3.14.1.2 |
| objectPath | O | O | NP | NP | See clause 7.3.14 | See Table 7.3.14.1.2 |
| description | O | O | O | NP | See clause 7.3.14 | See Table 7.3.14.1.2 |
| applicableEventCategories | M | O | O | NP | m2m:listOfEventCat | None |
| mgmtLink | O | O | O | NP | m2m:mgmtLink | Zero or more links to [cmdhNwAccessRule] resource instance(s) |

### -----------------------End of change  10-------------------------------------------

### -----------------------Start of change 11-------------------------------------------

Table D.12.7-2: Data Types for resource specific attributes

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | NP | NP | See clause 7.3.14 | 1018 (cmdhNwAccessRule) |
| objectID | O | O | NP | NP | See clause 7.3.14 | See Table 7.3.14.1-2 |
| objectPath | O | O | NP | NP | See clause 7.3.14 | See Table 7.3.14.1-2 |
| description | O | O | O | NP | See clause 7.3.14 | See Table 7.3.14.1-2 |
| targetNetwork | M | O | O | NP | m2m:listOfM2MID | None |
| minReqVolume | M | O | O | NP | xs:nonNegativeInteger | Unit: byte |
| backOffParameters | M | O | O | NP | m2m: backOffParameters | Ordered sequence of 3 values: backoffTime, backoffTimeIncrement, maximumBackoffTime, Unit: ms |
| otherConditions | O | O | O | NP | xs:string | None |
| mgmtLink | M | O | O | NP | m2m:mgmtLink | Link to an instance “allowedSchedule” of a <schedule> resource |

### -----------------------End of change  11-------------------------------------------

### -----------------------Start of change 12-------------------------------------------

Table D.12.8-2: Data Types for resource specific attributes

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | NP | NP | See clause 7.3.14 | 1019 (cmdhBuffer) |
| objectID | O | O | NP | NP | See clause 7.3.14 | See Table 7.3.14.1-2 |
| objectPath | O | O | NP | NP | See clause 7.3.14 | See Table 7.3.14.1-2 |
| description | O | O | O | NP | See clause 7.3.14 | See Table 7.3.14.1-2 |
| applicableEventCategory | M | O | O | NP | m2m:listOfEventCat | None |
| maxBufferSize | M | O | O | NP | xs:nonNegativeInteger | Unit: byte |
| storagePriority | M | O | O | NP | xs:positiveInteger | The range of storage priority is from 1 to 10. |

### -----------------------End of change  12-------------------------------------------

### -----------------------Start of change 13-------------------------------------------

Table 6.3.3.2.25-1: Interpretation of mgmtDefinition

| Value | Interpretation | Note |
| --- | --- | --- |
| 1001 | [firmware] |  |
| 1002 | software |  |
| 1003 | memory |  |
| 1004 | areaNwkInfo |  |
| 1005 | areaNwkDeviceInfo |  |
| 1006 | battery |  |
| 1007 | deviceInfo |  |
| 1008 | deviceCapability |  |
| 1009 | reboot |  |
| 1010 | eventLog |  |
| 1011 | cmdhPolicy |  |
| 1012 | activeCmdhPolicy |  |
| 1013 | cmdhDefaults |  |
| 1014 | cmdhDefEcValue |  |
| 1015 | cmdhEcDefParamValues |  |
| 1016 | cmdhLimits |  |
| 1017 | cmdhNetworkAccessRules |  |
| 1018 | cmdhNwAccessRule |  |
| 1019 | cmdhBuffer |  |
| 0 | Unspecified | Permits vendor-specific extensions |
| See Clause 7.3.13 mgmtObj |

### -----------------------End of change  13-------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Comments

This item has been moved to the top of the list

This item has been moved tocome before mgmtLink