| CHANGE REQUEST |
| --- |
| Meeting:* | PRO 14.2 |
| Source:* | FUJITSU |
| Date:* | 2014-12-16 |
| Contact:* | Shingo Fujimoto, FUJITSU, Shingo_fujimoto@jp.fujitsu.com |
| Reason for Change/s:* | Response Code assignement is inconsist within clause 6.6 |
| CR against: Release* | 1.0 (DRAFT) |
| CR against: TS/TR* | TS-0004-V0.8.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Response Status codes are assigned at clause 6.6.3, but they are inconsistent with the text in clause 6.6.2.

This contribution aims to remove inconsistency and proposed to reorganize them.

### -----------------------Start of change 1-------------------------------------------

## 6.6	 Response status codes

### 6.6.1 Introduction

The present clause specifies the assignment of oneM2M Response Status Codes (RSC), which is returned as the content of Response primitive.

The specific protocol binding may allow CSE not to return Response Status Code as  the content of Response primitive when the Response type is other than Success response, and the Response Status Code can be mapped to the status code of the transport protocols (ex. HTTP, CoAP). .

### 6.6.2 RSC framework overview

The RSCs are categorised as one of three classes:

Table 6.6.2-1: Definition of Response Status Code class

| Status Class | Codeclass | Interpretation |
| --- | --- | --- |
| Informational | 1xxx | The request is successfully received, but the request is still on process. |
| Success | 2xxx | The request is successfully received, understood, and accepted. |
| Redirection | 3xxx | (Not used in present release) |
| Originator Error | 3xxx | The Originator seems to have erred and the request is rejected. |
| Receiver Error | 4xxx | The requested operation cannot be performed the error on receiver CSE. |
| Network Service Error | 5xxx | The requested operation cannot be performed because of error on Network Serivce Entity. |

### 6.6.3	Definition of Response Status Codes

The tables in the following clauses specify the RSCs for oneM2M releases. Each RSC includes: a response status description, a numeric code, arguments, and applicable APIs (indicated by reference points). The response status description shall be unique within the set of response status descriptions for a release. Response status descriptions may be re-used among RSCs associated with different releases.

#### 6.6.3.1 Informational response class

Table 6.6.3.1-1 specify the RSCs for Informational responses.

Table 6.6.3.3-1: RSCs for Informational Responses class

| Numeric Code | Description | Argument |
| --- | --- | --- |
| 1000 | STATUS_ACCEPTED | URI for <request> resource which is associated with the request. |

#### 6.6.3.2 Successful response class

Table 6.6.3.2-1 specify the RSCs for Successful responses.

Table 6.6.3.2-1: RSCs for Success response class

| Numeric Code | Description | Additional Information |
| --- | --- | --- |
| 2000 | STATUS_OK |  |
| 2001 | STATUS_CREATED | URI of the created resource |
| 2002 | STATUS_DELETED |  |
| 2003 | STATUS_VALID |  |
| 2004 | STATUS_CHANGED | Changed content at the resource |
| 2005 | STATUS_CONTENT |  |

#### 6.6.3.3 Redirection response class

This Response Status Code class is not used in present release.

#### 6.6.3.4 Originator Error response class

Table 6.6.3.4-1 specify the RSCs for Originator Error responses.

Table 6.6.3.4-1: RSCs for Originator Error response class

| Numeric Code | Description | Additional Information |
| --- | --- | --- |
| 4000 | STATUS_BAD_REQUEST | Missing parameter |
| 4001 | STATUS_UNAUTHORIZED |  |
| 4002 | STATUS_PAYMENT_REQUIRED |  |
| 4003 | STATUS_FORBIDDEN |  |
| 4004 | STATUS_NOT_FOUND |  |
| 4005 | STATUS_OPERATION_NOT_ALLOWED |  |
| 4006 | STATUS_NOT_ACCEPTABLE |  |
| 4007 | STATUS_REGISTRAR_AUTHENTICATION_REQUIRED |  |
| 4008 | STATUS_REQUEST_TIMEOUT |  |
| 4011 | STATUS_CONTENT_LENGTH_REQUIRED |  |
| 4012 | STATUS_PRECONDITION_FAILED |  |
| 4013 | STATUS_REQUEST_ENTITY_TOO_LARGE |  |
| 4014 | STATUS_REQUEST_URI_TOO_LONG |  |
| 4015 | STATUS_UNSUPPORTED_MEDIA_TYPE |  |
| 4101 | Subscription verification failed - creator | creator |
| 4102 | Update error – unacceptable contents | Attribute URI |

#### 6.6.3.5 Receiver Error response class

Table 6.6.3.2-1 specify the RSCs for Receiver Error  responses.

Table 6.6.3.5-1: RSCs for Receiver Error response class

| Numeric Code | Description | Additional Information |
| --- | --- | --- |
| 5000 | STATUS_INTERNAL_SERVER_ERROR |  |
| 5001 | STATUS_NOT_IMPLEMENTED |  |
| 5002 |  |  |
| 5003 | STATUS_SERVICE_UNAVAILABLE |  |
| 5004 | STATUS_NEXT_CSE_TIMEOUT |  |
| 5005 | STATUS_PROTOCOL_VERSION_NOT_SUPPORTED |  |
| 5006 |  |  |
| 5007 | STATUS_INSUFFICIENT_STORAGE |  |
| 5009 | STATUS_BANDWIDTH_LIMITE_EXCEEDED |  |
| 5101 | Unsupported resource | Resource URI |
| 5102 | Unsupported attribute | Attribute URI |
| 5103 | Target not reachable | Resource URI |
| 5104 | Cannot forward, other reason TBD | Resource URI |
| 5105 | No privilege | Resource URI |
| 5106 | Already exists | Resource URI |
| 5109 | Retrieve error - does not exist |  |
| 5115 | Create delivery - not able to take on responsibility |  |
| 5201 | Retrieve CSEBase - format error | CSEBase URI |
| 5202 | CMDH rules -non compliant |  |
| 5203 | Target is not subscribable |  |
| 5204 | Cannot initiate subscription verification |  |
| 5205 | Subscription verification failed – Originator ID | Originator ID |

#### 6.6.3.6 External System Error response class

Table 6.6.3.2-1 specify the RSCs for when the External System reported some errors.

Table 6.6.3.6-1: RSCs for Network Service Error response class

| Numeric Code | Description | Argument |  |
| --- | --- | --- | --- |
| 6001 | Location info not authorized |  |  |  |  |
| 6003 | External object not reachable |  |  |  |  |
| 6004 | Create mgmtObj - memory shortage |  |  |  |  |
| 6005 | External object not found |  |  |  |  |
| 6006 | Cancel execInstance - not cancellable |  |  |  |  |
| 6007 | Cancel execInstance - already complete |  |  |  |  |
| 6008 | Delete execInstance - not cancellable |  |  |  |  |
| 6009 | Delete execInstance - already complete |  |  |  |  |
| 6010 | Max number of member exceeded |  |  |  |  |
| 6011 | Member type inconsistent |  |  |  |  |
| 6003 | Management session establishment timeout |  |  |  |  |
| 6003 | Create mgmtCmd – invalid cmdType |  |  |  |  |
| 6004 | Create mgmtCmd – invalid arguments |  |  |  |  |
| 6005 | Create mgmtCmd – insufficient arguments |  |  |  |  |
| 6006 | MgmtCmd – conversion error |  |  |  |  |
| 6007 | Delete mgmtCmd- execInstance cancellation error |  |  |  |  |
| 6008 | Cancel execInstance – cancellation error |  |  |  |  |
| 6009 | Delete execInstance – cancellation failed |  |  |  |  |
| 6022 | Management session cannot be established |  |  |  |  |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change n-------------------------------------------

### -----------------------End of change n---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?