| CHANGE REQUEST |
| --- |
| Group Name:* | PRO#15 |
| Title: * | add resourceName to common attributes |
| Source:* | Huawei Technologies Co., Ltd. |
| Format:* | Physical meeting |
| Date:* | 2015-1-7 |
| Contact:* | Jiaxin Yin, Huawei Technologies, yinjiaxin@huawei.com |
| Reason for Change/s:* | resource name should be added as part of each resource to form the hierarchical resource URI |
| CR against: Release* | Release 1 |
| CR against: TS/TR* | TS-0001, ver 0.8.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The contribution adds the resource name to each resource.

### -----------------------Start of Change 1-------------------------------------------

Table 6.3.5-1: Resource Common Attributes

| Attribute Name | Data Type | Default | Value restrictions | Notes |
| --- | --- | --- | --- | --- |
| resourceType | m2m:resourceType | Not applicable |  |  |
| resourceID | m2m:ID | Not applicable |  |  |
| parentID | m2m:nhURI | Not applicable | Must be a non-hierarchical URI |  |
| accessControlPolicyIDs | m2m:acpType | Policy is inherited from the parent resource |  |  |
| creationTime | xs:dateTime | Not applicable |  |  |
| expirationTime | xs:dateTime | Absence of the attribute means that the resource has no explicit expirationTime |  |  |
| lastModifiedTime | xs:dateTime | Not applicable |  |  |
| stateTag | xs:nonNegativeInteger | Not applicable |  |  |
| labels | list of xs:token | Absence of this attribute means there are no labels |  |  |
| link | xs:anyURI | Absence of this attribute means that this is not an announced resource |  |  |
| announceTo | list of xs:anyURI | Absence of this attribute means that this is not an announced resource |  |  |
| announcedAttribute | list of xs:token | Absence of this attribute means that this is not an announced resource |  |  |
| resourceName | xs:NCName | Not applicable |  |  |

### -----------------------End of Change 1-------------------------------------------

### -----------------------Start of Change 2-------------------------------------------

Table 6.3.5-2: Complex Data Types declaring groups of resource common attributes

| XSD type name | Child Elements | Child Element Datatype | Multiplicity | Description |
| --- | --- | --- | --- | --- |
| M2m:regularResourceType | @resourceName | xs:string | 1 | Declares the common attributes included in the majority of non-announceable resource types. |
|  | resourceType | m2m:resourceType | 1 |  |
|  | resourceID | m2m:ID | 1 |  |
|  | parentID | xs:anyURI | 1 |  |
|  | accessControlPolicyIDs | m2m:acpType | 0..1 |  |
|  | creationTime | xs:dateTime | 1 |  |
|  | expirationTime | xs:dateTime | 1 |  |
|  | lastModifiedTime | xs:dateTime | 1 |  |
|  | stateTag | xs:nonNegativeInteger | 1 |  |
|  | Labels | m2m:labelsType | 0..1 |  |
| M2m:announceableResourceType | @resourceName | xs:string | 1 | Declares the common attributes included in announceable resource types. |
|  | resourceType | m2m:resourceType | 1 |  |
|  | resourceID | m2m:ID | 1 |  |
|  | parentID | xs:anyURI | 1 |  |
|  | accessControlPolicyIDs | m2m:acpType | 0..1 |  |
|  | creationTime | xs:dateTime | 1 |  |
|  | expirationTime | xs:dateTime | 1 |  |
|  | lastModifiedTime | xs:dateTime | 1 |  |
|  | stateTag | xs:nonNegativeInteger | 1 |  |
|  | Labels | m2m:labelsType | 0..1 |  |
|  | Link | xs:anyURI | 0..1 |  |
|  | announceTo | list of xs:anyURI | 0..1 |  |
|  | announcedAttribute | list of xs:token | 0..1 |  |
| M2m:subordinateResourceType | @resourceName | xs:string | 1 | Declares the common attributes used by resource types that are subordinate children of other resources |
|  | resourceType | m2m:resourceType | 1 |  |
|  | resourceID | m2m:ID | 1 |  |
|  | parentID | xs:anyURI | 1 |  |
|  | creationTime | xs:dateTime | 1 |  |
|  | lastModifiedTime | xs:dateTime | 1 |  |
|  | stateTag | xs:nonNegativeInteger | 1 |  |
|  | labels | m2m:labelsType | 0..1 |  |

NOTE: In the above table, names of XML schema attributes are prefixed with a “@” character to differentiate these from Resource attribute names. The “@” character is not part of the actual attribute name.

### -----------------------End of Change 2-------------------------------------------

### -----------------------Start of Change 3-------------------------------------------

##### Create the resource

A new resource shall be created and correlated to the addressed and existing parent resource. As the result of the resource creation, the lastModifiedTime attribute of the parent resource shall be set to the same value as the creationTime attribute of the created resource. The following rules shall be applied.

The URI of the created resource shall be the URI of its parent resource with the resourceName appended. (e.g. http://CSEbase.operator.org/myAppID, for an application resource with resourceName "myAppID" created in the parent resource http://CSEbase.operator.org).

If a resource with the same resourceName already exists among the siblings of the addressed parent resource, the hosting CSE shall provide a new resourceName  that is unique within the parent.

If expirationTime attribute is present in the resource representation of the to be created resource and the expirationTime is set to a non-negative time, then an expiration timer shall be started by the hosting CSE. At timer expiration the related resource is deleted by "Delete the addressed resource".

For setting the attributes in the resource representation the following rules shall apply in CREATE request primitives:

M attribute

If the provided value is acceptable, the server shall use the provided value in the resource representation of the created resource.

O attribute

If a value is provided and accepted, then the server shall use the provided value in the resource representation of the created resource.

If the attribute is not provided or accepted, but the attribute is marked M in the response, the hosting CSE shall assign default value or assign value based on local policy.

If the attribute is not present in the resource representation in the CREATE request and the response column is marked O then the hosting CSE shall create the resource without the attribute.

NP attribute

If the attribute is not present in the resource representation in the CREATE request, and the response column is marked M, then the hosting CSE shall create the resource with the default value.

### -----------------------End of Change 3-------------------------------------------

### -----------------------Start of Change 4-------------------------------------------

##### Check validity of resource representation for CREATE

The handling below shall apply to each attribute in the resource for CREATE request primitives and the handling depends on the "presence in CREATE request" column of the resource table. If the request is rejected based on the rules below, then the other attributes do not have to be checked.

If no resource representation is present in the CREATE request, then the request is rejected with a STATUS_BAD_REQUEST statusCode.

The resourceName attribute has special handling. If the resourceName attribute is present in the CREATE request, the hosting CSE shall check if a resource with the same resourceName already exists in the addressed collection. If such a resource exists and the response column is marked as M, then the hosting CSE shall reject the request with a "STATUS_CONFLICT".

If the expirationTime attribute is present in the resource representation, but its value indicates a time in the past, then the request shall be rejected with a STATUS_BAD_REQUEST.

N/A attribute

Indicates that the attribute is not supported in the CREATE request.

The resource indicated as N/A shall be created when the parent resource was created, or the resource shall permanently exist in oneM2M System.

M attribute

If the attribute is present in the resource representation in the CREATE request, the hosting CSE shall check if the value is acceptable according to internal policies.

If the provided value is not accepted and the response column is marked M then the hosting CSE shall reject the request with a "STATUS_BAD_REQUEST".

If the attribute is not present in the resource representation in the CREATE request the hosting CSE shall reject the request with a "STATUS_BAD_REQUEST".

O attribute

If the attribute is present in the resource representation in the CREATE request, the hosting CSE shall check if the value is acceptable according to internal policies.

If the provided value is not accepted and the response column is marked M or O then the hosting CSE shall reject the request with a "STATUS_NOT_IMPLEMENTED".

NP attribute

If the attribute is present in the resource representation in the CREATE request, the hosting CSE shall reject the request with a "STATUS_BAD_REQUEST".

### -----------------------End of Change 4-------------------------------------------

### -----------------------Start of Change 5------------------------------------------

### Resource attributes

In protocol bindings resource attributes names shall be translated into short names of Table 8.3-1.

Table 8.2.3-1: Resource attribute short names (1/5)

| Attribute Name | Occurs in | Short Name |
| --- | --- | --- |
| accessControlPolicyIDs | All except accessControlPolicy, contentInstance | acpi |
| announcedAttribute | accessControlPolicy, AE, container, contentInstance, group, locationPolicy, mgmtObj, node, remoteCSE, schedule | aa |
| announceTo | accessControlPolicy, AE, container, contentInstance, group, locationPolicy, mgmtObj, node, remoteCSE, schedule | at |
| creationTime | All | ct |
| expirationTime | All except contentInstance, CSEBase | et |
| lastModifiedTime | All | lt |
| parentID | All except CSEBase | pi |
| resourceID | All | ri |
| stateTag | container, contentInstance, delivery, request | st |
| resourceName | All | rn |

### -----------------------End of Change 5-------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?