| CHANGE REQUEST |
| --- |
| Group Name:* | PRO |
| Source:* | LG Electronics |
| Format:* |  |
| Date:* | 2015-01-12 |
| Contact:* | SeungMyeong JEONG (seungmyeong.jeong@lge.com) |
| Reason for Change/s:* |  |
| CR against: Release* | v.0.8.0 |
| CR against: TS/TR* | TS-0004 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

A receiver cannot guarantee that it can distinguish reference points for incoming requests. It may be possible by implementation. Even it can do that, the Originator still can fake its entity type as well as its ID in this release.

In R01: after the discussion with SEC WG, there would be another CR for impersonation issue for TS-0004. With that, this revision reverts the way forward, meaning the Receiver can distinguish if the Originator is AE or CSE. There’s an assumption that it is guaranteed by implmentation. Added “NOTE: Determination of the reference point is to the discretion of the Receiver CSE implementation.” in every corresponding texts.

## ----------------------- Start of change 1 -----------------------

#### <remoteCSE> resource specific procedure on CRUD operations

##### Create

Originator:

No change from the generic procedures in clause 7.1.2.1 with the following exception:

An AE shall not originate a Create <remoteCSE> resource request.

Receiver:

Primitive specific operation on Recv-1.0 "Check the syntax of received message":

- If the request is received over the Mca reference point, the Receiver CSE shall execute the following steps in order.

- "Create an unsuccessful Response primitive" with the response status code  “OPERATION_NOT_ALLOWED”.

- "Send the Response primitive"

- NOTE: Determination of the reference point is to the discretion of the Receiver CSE implementation.

## ----------------------- End of change 1 -----------------------

## ----------------------- Start of change 2 -----------------------

#### <AE> resource specific procedure on CRUD+N operations

This sub-clause describes AE resource specific behaviour for CRUD+N operations.

##### Create

Originator:

No change from the generic procedures in clause 7.1.2.1 with the with the following exception:

- A CSE shall not originate a Create <AE> resource request.

Receiver:

Primitive specific operation on Recv-1.0 "Check the syntax of received message":

- If the request is received over Mcc or Mcc’ reference point, the Receiver CSE shall execute the following steps in order.

- "Create an unsuccessful Response primitive" with the Response Status Code indicating  “OPERATION_NOT_ALLOWED” error.

- "Send the Response primitive".

- NOTE: Determination of the reference point is to the discretion of the Receiver CSE implementation.

- Otherwise,

- No change from the generic procedures in clause 7.1.2.2.

## ----------------------- End of change 2 -----------------------

## ----------------------- Start of change 3 -----------------------

#### <delivery> resource specific procedure on CRUD operations

This clause describes <delivery> resource specific behaviour for CRUD operations.

##### Create

Originator:

An AE shall not originate a Create <delivery> resource request.

Primitive specific operation on Org-1.0 "Compose Request primitive":

- The Originator shall use a blocking request (i.e. Response Type=blockingRequest).

- The Originator shall provide the content of the <delivery> resource.

No change for the remaining steps from the generic procedures in clause 7.1.2.1.

Receiver:

Primitive specific operation on Rcv-1.0 "Check the syntax of received message":

- If the request is received over Mca reference point, the Receiver CSE shall execute the following steps in order.

  - "Create an error response" with the Response Status Code indicating “OPERATION_NOT_ALLOWED” error.

  - "Send Response primitive".

NOTE: Determination of the reference point is to the discretion of the Receiver CSE implementation.

Primitive specific operation after Rcv-6.8 "Check the syntax of received message".

- If the target attribute in <request> resource does not start with the CSEBase URI of the Receiver CSE, the Receiver CSE shall forward the request.

No change for the remaining steps from the generic procedures in clause 7.1.2.2.

## ----------------------- End of change 3 -----------------------

## ----------------------- Start of change 4 -----------------------

##### Update

Originator:

An AE shall not originate a Create <delivery> resource request.

Primitive specific operation on Org-1.0 "Compose Request primitive":

- The Originator shall use a blocking request (i.e. Response Type=blockingRequest).

- The Originator shall provide the content of the <delivery> resource.

No change for the remaining steps from the generic procedures in clause 7.1.2.1.

Receiver:

Primitive specific operation on Rcv-1.0 "Check the syntax of received message":

- If the request is received over Mca reference point, the Receiver CSE shall execute the following steps in order.

  - "Create an error response" with the Response Status Code indicating “OPERATION_NOT_ALLOWED” error.

  - "Send Response primitive".

  - NOTE: Determination of the reference point is to the discretion of the Receiver CSE implementation.

No change for the remaining steps from the generic procedures in clause 7.1.2.2.

##### Delete

Originator:

An AE shall not originate a Create <delivery> resource request.

Primitive specific operation on Org-1.0 "Compose Request primitive":

- The Originator shall use a blocking request (i.e. Response Type=blockingRequest).

No change for the remaining steps from the generic procedures in clause 7.1.2.1.

Receiver:

Primitive specific operation on Rcv-1.0 "Check the syntax of received message":

If the request is received over Mca reference point, the Receiver CSE shall execute the following steps in order.

  - "Create an error response" with the Response Status Code indicating “OPERATION_NOT_ALLOWED” error.

  - "Send Response primitive".

  - NOTE: Determination of the reference point is to the discretion of the Receiver CSE implementation.

No change for the remaining steps from the generic procedures in clause 7.1.2.2.

## ----------------------- End of change 4 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?