| CHANGE REQUEST |
| --- |
| Group Name:* | PRO |
| Source:* | LG Electronics |
| Format:* |  |
| Date:* | 2015-01-12 |
| Contact:* | SeungMyeong JEONG (seungmyeong.jeong@lge.com) |
| Reason for Change/s:* |  |
| CR against: Release* | v.0.8.0 |
| CR against: TS/TR* | TS-0004 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

change 1

Original intention of this contribution is to update the stale sentence:

Create a Response primitive including Pending Requests primitive parameter.

Pending Requests primitive parameter was used to deliver requests stored/accumulated at the <pollingChannel> resource hosting CSE. It had been removed, so this contribution proposes to use m2m:aggregatedRequests data type, which was agreed at PRO#14.

change 2

There’s missing clause title.

content (parameter) of a request has been renamed as primitive content (see clasue 7.1.1 primitive format). Also the corresponding data type was renamed as m2m:primitiveContent (see clause 6.4 message parameter data types). These changes are reflected in the table.

this change should be appliced to the entire TS.

change 3

The same change, for primitive content parameter, is done here. Also, TBD is replaced by the new table. Information in this new table needs to be discussed enough. Proposal follows the previous practice for “representation” element of m2m:notificationEvent, which supports a very generic data type for any data/information.

Usually, Primitive Content parameter contains pairs of attribute name and its value. Note that in partial retrieval case, names of intereted attributes are contained in Primitive Content parameter.

change 4

Content parameter is renamed as Primitive Content.

## ----------------------- Start of change 1 -----------------------

### Resource Type <pollingChannelURI>

#### Introduction

The <pollingChannelURI> resource is the virtual child resource which is automatically generated during the parent <pollingChannel> resource creation. The detailed description can be found in clause 9.6.22 in TS-0001 Functional Architecture [6].

There is no data type definition for <pollingChannelURI> resource because it’s a virtual resource type.

#### <pollingChannelURI> resource specific procedure on CRUD operations

This clause describes <pollingChannelURI> resource specific behaviour for the Retrieve operation as a service layer long polling request. CUDN requests to the <pollingChannelURI> resource shall be rejected.

##### Create

The present document does not define Create operation on a <pollingChannelURI> resource. A Create request for the resource shall be rejected.

A <pollingChannelURI> virtual resource shall only be created during its parent <pollingChannel> resource creation procedure.

##### Retrieve

Originator: shall execute Originator actions in clause 7.1.2.1 as a service layer long polling request. It's the Originator's responsibility to initiate this procedure after it gets long polling response either successful or unsuccessful. The Originator shall send this Retrieve request as blocking request (clause 8.2.1 in TS-0001 Functional Architecture [6]).

Receiver: shall execute the following steps in order and these are modifications to the generic procedure from Recv-6.3 to Recv-6.5 in clause 7.1.2.2:

Recv-6.3 Check if the request Originator is the creator of the parent <pollingChannel> resource. If it is not the creator, the Hosting CSE shall send access denied error response.

Recv-6.4	No change from the generic procedure.

Recv-6.5

If there is a pending request(s) to be sent to the Originator

Create a Response primitive by setting the Primitive Content parameter with the pending request(s).

Else

Wait for a request for the Originator until the Request Expiration Timestamp of the Originator's request. If a request is available before the Request Expiration Timestamp timeout, create a Response primitive including Pending Requests primitive parameter. Otherwise, create an error response. Error information is request timeout.

##### Update

The present document does not define Update operation on a <pollingChannelURI> resource. An Update request for the resource shall be rejected.

##### Delete

The present document does not define Delete operation on a <pollingChannelURI> resource. A Delete request for the resource shall be rejected.

## ----------------------- End of change 1 -----------------------

## ----------------------- Start of change 2 -----------------------

#### m2m:aggregatedRequest

Used for aggregatedRequest attribute in <delivery> resource.

Table 6.3.4.3-1: Type Definition of m2m:aggregatedRequest

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| request | m2m:request | 1..n |  |

#### m2m:request

Table 6.3.4.4-1: Type Definition of m2m:request

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| operation | m2m:operation | 1 | See Clause 6.3.3.2.5 |
| to | xs:anyURI | 1 |  |
| from | m2m:ID | 1 | See Clause 6.3.2 |
| requestIdentifier | m2m:requestID | 1 | See Clause 6.3.2 |
| primitiveContent | m2m:primitiveContent | 0..1 | See Clause 6.3.4.5 |
| metaInformation | m2m:metaInformation | 0..1 | See Clause 6.3.4.4 |

## ----------------------- End of change 2 -----------------------

rapporteur should update the following clause numbers and references in the Note columns.

## ----------------------- Start of change 3 -----------------------

#### m2m:primitiveContent

Used for Primitive Content parameter in request/response and content attribute in <request> resource.

Table 6.3.4.6-1: Type definition of m2m:primitiveContent

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| <resourceType> | xs:any | 0..1 | Resource representation |
| aggregatedRequest | m2m:aggregatedRequest | 0..1 | Pending requests for <pollingChannelURI> retrieval. See clause 7.3.4.2.2. |
| attributeList | xs:token | 0..1 | List of attribute names used in partial retrieval. See clause 7.2.3.5. |

NOTE: <resourceType> is the one of the resource type names defined in this specification. E.g., “AE” or “container” can be the element path.

## ----------------------- End of change 3 -----------------------

## ----------------------- Start of change 4 -----------------------

##### Retrieve the resource

The content of the attributes and references to child resources of the addressed resource shall be retrieved in form of a resource representation.

When the resource is read to provide a response to RETRIEVE request primitives, attribute(s) shall be present in the resource representation depending on the retrieve request type:

Full retrieve request: the request target is a resource given in the to parameter

All attribute values stored in the resource shall be retrieved.

Partial retrieve request:

Case 1) 	the request target is a resource given in the to parameter and specific attribute names are provided in the primitive content parameter:

The values of the resource attribute(s) provided in the primitive content parameter shall be retrieved.

Case 2)	the request target is a specific attribute provided in the to parameter:

The resource attribute provided in the to parameter shall be retrieved.

## ----------------------- End of change 4 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?