| CHANGE REQUEST |
| --- |
| Group Name:* | PRO |
| Source:* | LG Electronics |
| Format:* |  |
| Date:* | 2015-01-12 |
| Contact:* | Heedong Choi (heedong.choi@lge.com) |
| Reason for Change/s:* | Change the table of resource common attributes in the clause 6.3.5 |
| CR against: Release* | v0.8.0 |
| CR against: TS/TR* | TS-0004 |
| Clauses/Sub Clauses* | 6.3.5 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

In the clause 6.3.5, there is the table of resource common attribute. Although the table is well organized, there are some mismatches. Also, most of parts for value restrictions and notes remain blanks. So, this contribution proposes to change the table of resource common attributes in the clause 6.3.5. The changes are as follows:

- Chane the term from ‘Not applicable’ to ‘No default’

- Clarify the default value and value restrictions (notes)

- Merge and fill in value restrictions and notes in the table 6.3.5-1

## ----------------------- Start of change 1 -----------------------

### Resource universal/common attributes

Resource common attributes are specified in TS-0001 Functional Architecture [6]. The type and values shall be supported according to the description given in table 6.3.5-1.

If a Resource is represented as an XML document then the resource attributes (if present) appear in the order listed in this table. They appear before any resource-specific attributes.

Table 6.3.5-1: Resource Universal/Common Attributes

| Attribute Name | Data Type | Default | Value restrictions and Notes |
| --- | --- | --- | --- |
| resourceType | m2m:resourceType | No default | This attribute is only determined at creation time by the hosting CSE |
| resourceID | m2m:ID | No default | This attribute is determined at creation time by the hosing CSE and used for non-hierarchical addressing method |
| parentID | m2m:nhURI | No default | This attribute is determined by the hosting CSE and specified in all resource types except of <CSEBase> |
| accessControlPolicyIDs | m2m:acpType | No default | None |
| creationTime | xs:dateTime | No default | This attribute is determined by the hosting CSE when the resource is locally created |
| expirationTime | xs:dateTime | Default value is determined by hosting CSE policy | Absence of the attribute means that the resource has no explicit expiration time |
| lastModifiedTime | xs:dateTime | No default | This attribute is determined by the hosting CSE when the addressed resource is modified by means of the UPDATE operation |
| stateTag | xs:nonNegativeInteger | No default | This attribute is determined by the hosting CSE. When a resource is created this counter is set to ‘0’ and it will be incremented on every modification of the resource |
| labels | list of xs:token | No default | Absence of this attribute means there are no labels |
| link | xs:anyURI | No default | Absence of this attribute means that this is not an announced resource |
| announceTo | list of xs:anyURI | No default | Absence of this attribute means that this is not an announced resource |
| announcedAttribute | list of xs:token | No default | Absence of this attribute means that this is not an announced resource |

## ----------------------- End of change 1 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?