| CHANGE REQUEST |
| --- |
| Group Name:* | PRO |
| Source:* | LG Electronics |
| Format:* |  |
| Date:* | 2015-01-09 |
| Contact:* | Heedong Choi (heedong.choi@lge.com) |
| Reason for Change/s:* | Define default values for each resource |
| CR against: Release* | v0.8.0 |
| CR against: TS/TR* | TS-0004 |
| Clauses/Sub Clauses* | 7.3 |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution proposes the default value for each resource including editorial corrections.

## ----------------------- Start of change 1 -----------------------

### Resource type <accessControlPolicy>

…

Table 7.3.1.1-2: Applicable Common Attributes on <accessControlPolicy>

| Attribute Name | Request Optionality | Default Value | Resource Specific Note |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| resourceType | NP | O | NP | NP | See table 6.3.5-1 | None |
| resourceID | NP | O | NP | NP | See table 6.3.5-1 | None |
| parentID | NP | O | NP | NP | See table 6.3.5-1 | None |
| expirationTime | O | O | O | NP | See table 6.3.5-1 | None |
| labels | O | O | O | NP | See table 6.3.5-1 | None |
| creationTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| lastModifiedTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| announceTo | O | O | O | NP | See table 6.3.5-1 | None |
| announcedAttribute | O | O | O | NP | See table 6.3.5-1 | None |

Table 7.3.1.1-3: Data Types for resource specific attributes

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| privileges | M | O | O | NP | m2m:setOfAcrs | No default |
| selfPrivileges | M | O | O | NP | m2m:setOfAcrs | No default |

## ----------------------- End of change 1 -----------------------

## ----------------------- Start of change 2 -----------------------

### Resource Type <CSEBase>

…

Table 7.2.2.1-2: Common Attributes on <CSEBase>

| Attribute Name | Request optionality | Default Value | Resource Specific Note |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| resourceType | NP | O | NP | NP | See table 6.3.5-1 | None |
| resourceID | NP | O | NP | NP | See table 6.3.5-1 | None |
| parentID | NP | O | NP | NP | See table 6.3.5-1 | This is always Null because the <CSEBase> resource is the root for all the resources |
| accessControlPolicyIDs | NP | O | NP | NP | See table 6.3.5-1 | None |
| creationTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| lastModifiedTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| labels | NP | O | NP | NP | See table 6.3.5-1 | None |

Table 7.2.2.1-3: Resource specific attributes on <CSEBase>

| Attribute Name | Request optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| cseType | NP | O | NP | NP | m2m:cseTypeID | No default |
| CSE-ID | NP | O | NP | NP | m2m:id | No default |
| supportedResourceType | NP | O | NP | NP | m2m:resourceTypeList | No default |
| pointOfAccess | NP | O | NP | NP | m2m:pOAList | No default |
| nodeLink | NP | O | NP | NP | xs:anyURI | No default |
| notificationCongestionPolicy | NP | O | NP | NP | m2m:notificationCongestionPolicy | No default |

## ----------------------- End of change 2 -----------------------

## ----------------------- Start of change 3 -----------------------

### Resource Type <remoteCSE>

…

Table 7.3.3.1-2: Common Attributes on <remoteCSE>

| Attribute Name | Request optionality | Default Value | Resource Specific Note |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| resourceType | NP | O | NP | NP | See table 6.3.5-1 | None |
| resourceID | NP | O | NP | NP | See table 6.3.5-1 | None |
| parentID | NP | O | NP | NP | See table 6.3.5-1 | None |
| accessControlPolicyIDs | O | O | O | NP | See table 6.3.5-1 | None |
| creationTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| expirationTime | O | O | O | NP | See table 6.3.5-1 | None |
| lastModifiedTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| labels | O | O | NP | NP | See table 6.3.5-1 | None |
| announceTo | O | O | O | NP | See table 6.3.5-1 | None |
| announcedAttribute | O | O | O | NP | See table 6.3.5-1 | None |

Table 7.3.3.1-3: Resource specific attributes on <remoteCSE>

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| cseType | O | O | NP | NP | m2m:cseTypeID | No default |
| pointOfAccess | O | O | O | NP | m2m:pOAList | No default (Absent if the remote CSE is not request-reachable) |
| CSEBase | M | O | NP | NP | xs:anyURI | No default |
| CSE-ID | M | O | NP | NP | m2m:id | No default |
| M2M-Ext-ID | O | O | O | NP | m2m:externalId | No default |
| Trigger-Recipient-ID | O | O | O | NP | m2m:triggerRecipientId | No default |
| requestReachability | M | O | O | NP | xs:boolean | No default |
| nodeLink | NP | O | NP | NP | xs:anyURI | No default |

## ----------------------- End of change 3 -----------------------

## ----------------------- Start of change 4 -----------------------

### Resource Type <AE>

…

Table 7.3.4.1-2: Applicable Common Attributes on AE

| Attribute Name | Request Optionality | Default Value | Resource Specific Note |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| resourceType | NP | O | NP | NP | See table 6.3.5-1 | None |
| resourceID | NP | O | NP | NP | See table 6.3.5-1 | None |
| parentID | NP | O | NP | NP | See table 6.3.5-1 | None |
| accessControlPolicyIDs | O | O | O | NP | See table 6.3.5-1 | None |
| creationTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| expirationTime | O | O | O | NP | See table 6.3.5-1 | None |
| lastModifiedTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| labels | O | O | NP | NP | See table 6.3.5-1 | None |
| announceTo | O | O | O | NP | See table 6.3.5-1 | None |
| announcedAttribute | O | O | O | NP | See table 6.3.5-1 | None |

Table 7.3.4.1-3: Data Types for resource specific attributes

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| appName | O | O | O | NP | xs:string | No default |
| App-ID | M | O | NP | NP | xs:string | No default |
| AE-ID | NP | O | NP | NP | m2m:ID | No default |
| pointOfAccess | O | O | O | NP | m2m:pOAList | No default |
| ontologyRef | O | O | O | NP | xs:anyURI | No default |
| nodeLink | NP | O | NP | NP | xs:anyURI | No default |

## ----------------------- End of change 4 -----------------------

## ----------------------- Start of change 5 -----------------------

### Resource Type <container>

…

Table 7.2.5.1-2: Common Attributes on <container>

| Attribute Name | Request Optionality | Default Value | Resource Specific Note |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| resourceType | NP | O | NP | NP | See table 6.3.5-1 | None |
| resourceID | NP | O | NP | NP | See table 6.3.5-1 | None |
| parentID | NP | O | NP | NP | See table 6.3.5-1 | None |
| accessControlPolicyIDs | O | O | O | NP | See table 6.3.5-1 | None |
| creationTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| expirationTime | O | O | O | NP | See table 6.3.5-1 | None |
| lastModifiedTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| stateTag | NP | O | NP | NP | See table 6.3.5-1 | None |
| labels | O | O | NP | NP | See table 6.3.5-1 | None |
| announceTo | O | O | O | NP | See table 6.3.5-1 | None |
| announcedAttribute | O | O | O | NP | See table 6.3.5-1 | None |

Table 7.2.5.1-3: Resource specific attributes on <container>

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| creator | NP | O | NP | NP | m2m:id | No default |
| maxNrOfInstances | O | O | O | NP | xs:nonNegativeInteger | No default |
| maxByteSize | O | O | O | NP | xs:nonNegativeInteger | No default |
| maxInstanceAge | O | O | O | NP | xs:nonNegativeInteger | No default |
| currentNrOfInstances | NP | O | NP | NP | xs:nonNegativeInteger | No default (This is generated by the hosting CSE and limited by the maxNrOfInstances) |
| currentByteSize | NP | O | NP | NP | xs:nonNegativeInteger | No default (This is generated by the hosting CSE and limited by the maxByteSize) |
| locationID | O | O | O | NP | xs:anyURI | No default |
| ontologyRef | O | O | O | NP | xs:anyURI | No default |

## ----------------------- End of change 5 -----------------------

## ----------------------- Start of change 6 -----------------------

### Resource Type <contentInstance>

…

Table 7.2.6.1-2: Applicable Common Attributes on <contentInstance>

| Attribute Name | Request Optionality | Default Value | Resource Specific Note |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| resourceType | NP | O | NP | NP | See table 6.3.5-1 | None |
| resourceID | NP | O | NP | NP | See table 6.3.5-1 | None |
| parentID | NP | O | NP | NP | See table 6.3.5-1 | None |
| expirationTime | O | O | O | NP | See table 6.3.5-1 | None |
| creationTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| lastModifiedTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| stateTag | NP | O | NP | NP | See table 6.3.5-1 | None |
| labels | O | O | NP | NP | See table 6.3.5-1 | None |
| announceTo | O | O | NP | NP | See table 6.3.5-1 | None |
| announcedAttribute | NP | O | NP | NP | See table 6.3.5-1 | None |

Table 7.2.6.1-3: Resource specific attributes on <contentInstance>

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| typeOfContent | M | O | NP | NP | m2m:typeOfContent | No default (one of IANA registered Media Types names or experimental Media Types names shall be specified (See [26])) |
| contentSize | O | O | NP | NP | xs:nonNegativeInteger | No default (This is generated by the hosting CSE) |
| ontologyRef | O | O | NP | NP | xs:anyURI | No default |
| content | M | O | NP | NP | xs:anySimpleType | No default (Transfer encoding may be applied, and indicated applied encoding at encoding attribute) |
| encoding | M | O | NP | NP | m2m:encodingType | No default |
| creator | O | O | NP | NP | m2m:id | No default |

## ----------------------- End of change 6 -----------------------

## ----------------------- Start of change 7 -----------------------

### Resource Type <subscription>

…

Table 7.2.7.1-2: Applicable Common Attributes on <subscription>

| Attribute Name | Request Optionality | Default Value | Resource Specific Note |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| resourceType | NP | O | NP | NP | See table 6.3.5-1 | None |
| resourceID | NP | O | NP | NP | See table 6.3.5-1 | None |
| parentID | NP | O | NP | NP | See table 6.3.5-1 | None |
| accessControlPolicyIDs | O | O | O | NP | See table 6.3.5-1 | None |
| creationTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| expirationTime | O | O | O | NP | See table 6.3.5-1 | None |
| lastModifiedTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| labels | O | O | O | NP | See table 6.3.5-1 | None |

Table 7.2.7.1-3: Data Types for resource specific attributes

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| eventNotificationCriteria | O | O | O | NP | m2m:eventNotificationCriteria | No default |
| expirationCounter | O | O | O | NP | xs:positiveInteger | No default |
| notificationURI | M | O | O | NP | list of xs:anyURI | No default |
| groupName | O | O | O | NP | xs:anyURI | No default |
| notificationForwardingURI | O | O | O | NP | xs:anyURI | No default |
| batchNotify | O | O | O | NP | m2m:batchNotify | No default |
| rateLimit | O | O | O | NP | m2m:rateLimit | No default |
| preSubscriptionNotify | O | O | NP | NP | xs:positiveInteger | No default |
| pendingNotification | O | O | O | NP | m2m:pendingNotification | No default |
| notificationStoragePriority | O | O | O | NP | xs:positiveInteger | No default |
| latestNotify | O | O | O | NP | xs:Boolean | No default |
| notificationContentType | O | O | O | NP | m2m:notificationContentType | Default value is set to ‘wholeResource’ |
| notificationEventCat | O | O | O | NP | m2m:eventCat | No default |
| creator | O | O | O | NP | m2m:id | No default |
| subscriberURI | O | O | NP | NP | xs:anyURI | No default |

## ----------------------- End of change 7 -----------------------

## ----------------------- Start of change 8 -----------------------

### Resource Type <schedule>

…

Table 7.3.8.1-2: Common Attributes on <schedule >

| Attribute Name | Request Optionality | Default Value | Resource Specific Note |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| resourceType | NP | O | NP | NP | See table 6.3.5-1 | None |
| resourceID | NP | O | NP | NP | See table 6.3.5-1 | None |
| parentID | NP | O | NP | NP | See table 6.3.5-1 | None |
| accessControlPolicyIDs | O | O | O | NP | See table 6.3.5-1 | None |
| creationTime | O | O | NP | NP | See table 6.3.5-1 | None |
| expirationTime | O | O | O | NP | See table 6.3.5-1 | None |
| lastModifiedTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| labels | O | O | NP | NP | See table 6.3.5-1 | None |
| announceTo | O | O | O | NP | See table 6.3.5-1 | None |
| announcedAttribute | O | O | O | NP | See table 6.3.5-1 | None |

Table 7.3.8.1-3: Resource specific attributes on <schedule>

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| scheduleElement (L) | M | O | O | M | Extended Crontab Data String | No Default (See data type definition for constraints) |

## ----------------------- End of change 8 -----------------------

## ----------------------- Start of change 9 -----------------------

### Resource Type <locationPolicy>

…

Table 7.2.9.1-2: Applicable Common Attributes on [locationPolicy]

| Attribute Name | Request Optionality | Default Value | Resource Specific Note |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| resourceType | NP | O | NP | NP | See table 6.3.5-1 | None |
| resourceID | NP | O | NP | NP | See table 6.3.5-1 | None |
| parentID | NP | O | NP | NP | See table 6.3.5-1 | None |
| expirationTime | O | O | O | NP | See table 6.3.5-1 | None |
| accessControlPolicyIDs | O | O | O | NP | See table 6.3.5-1 | None |
| creationTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| lastModifiedTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| labels | O | O | O | NP | See table 6.3.5-1 | None |
| announceTo | O | O | O | NP | See table 6.3.5-1 | None |
| announcedAttribute | O | O | O | NP | See table 6.3.5-1 | None |

Table 7.2.9.1-3: Data Types for resource specific attributes

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| locationSource | M | O | NP | NP | m2m:locationSource | No default |
| locationUpdatePeriod | O | O | O | NP | xs:duration | No default |
| locationTargetID | O | O | NP | NP | m2m:nodeId | No default |
| locationServer | O | O | NP | NP | xs:anyURI | No default |
| locationContainerID | NP | O | NP | NP | xs:anyURI | No default |
| locationContainerName | O | O | O | NP | xs:string | No default |
| locationStatus | NP | O | NP | NP | xs:string | No default |

## ----------------------- End of change 9 -----------------------

## ----------------------- Start of change 10 -----------------------

### Resource Type <delivery>

…

Table 7.2.10.1-2: Common Attributes on delivery

| Attribute Name | Request Optionality | Default Value | Resource Specific Note |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| resourceType | NP | O | NP | NP | See table 6.3.5-1 | None |
| resourceID | NP | O | NP | NP | See table 6.3.5-1 | None |
| expirationTime | O | O | O | NP | See table 6.3.5-1 | None |
| parentID | NP | O | NP | NP | See table 6.3.5-1 | None |
| creationTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| lastModifiedTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| accessControlPolicyIDs | O | O | O | NP | See table 6.3.5-1 | None |
| labels | O | O | O | NP | See table 6.3.5-1 | None |
| stateTag | NP | O | NP | NP | See table 6.3.5-1 | None |

Table 7.2.10.1-3: Resource Specific Attributes on delivery

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| source | M | O | NP | NP | xs:anyURI | No default |
| target | M | O | NP | NP | xs:anyURI | No default |
| lifespan | M | O | O | NP | xs:dateTime | No default |
| eventCat | M | O | O | NP | m2m:eventCat | No default |
| deliveryMetaData | M | O | O | NP | m2m: deliveryMetaData | No default |
| aggregatedRequest | O | O | O | NP | m2m:aggregatedRequest | No default |

## ----------------------- End of change 10 -----------------------

## ----------------------- Start of change 11 -----------------------

### Resource Type <request>

…

Table 7.2.11.1-2 : Applicable Common Attributes on <request>

| Attribute Name | Request Optionality | Default Value | Resource Specific Note |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| resourceType | NP | O | NP | NP | See table 6.3.5-1 | None |
| resourceID | NP | O | NP | NP | See table 6.3.5-1 | None |
| expirationTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| parentID | NP | O | NP | NP | See table 6.3.5-1 | None |
| creationTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| lastModifiedTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| accessControlPolicyIDs | NP | O | NP | NP | See table 6.3.5-1 | None |
| labels | NP | O | NP | NP | See table 6.3.5-1 | None |
| stateTag | NP | O | NP | NP | See table 6.3.5-1 | None |

Table 7.2.11.1-3 : Data Types for <request> resource specific attributes

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| operation | NP | O | NP | NP | m2m:operation | No default |
| target | NP | O | NP | NP | xs:anyURI | No default |
| originator | NP | O | NP | NP | xs:anyURI | No default |
| requestIdentifier | NP | O | NP | NP | m2m:requestId | No default |
| metaInformation | NP | O | NP | NP | m2m:metaInformation | No default |
| primitiveContent | NP | O | NP | NP | m2m:primitiveContent | No default |
| requestStatus | NP | O | NP | NP | m2m:requestStatus | No default |
| operationResult | NP | O | NP | NP | m2m:operationResult | No default |

## ----------------------- End of change 11 -----------------------

## ----------------------- Start of change 12 -----------------------

### Resource Type <group>

…

Table 7.3.12.1-2: Common Attributes on <group>

| Attribute Name | Request Optionality | Default Value | Resource Specific Note |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| resourceType | NP | O | O | NP | See table 6.3.5-1 | None |
| resourceID | NP | O | O | NP | See table 6.3.5-1 | None |
| parentID | NP | O | NP | NP | See table 6.3.5-1 | None |
| accessControlPolicyIDs | O | O | NP | NP | See table 6.3.5-1 | None |
| creationTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| expirationTime | O | O | O | NP | See table 6.3.5-1 | None |
| lastModifiedTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| labels | O | O | O | NP | See table 6.3.5-1 | None |
| announceTo | O | O | O | NP | See table 6.3.5-1 | None |
| announcedAttribute | O | O | O | NP | See table 6.3.5-1 | None |

Table 7.3.12.1-3: Resource Specific Attributes on <group>

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| memberType | O | O | O | NP | m2m:memberType | Default value is set to ‘MIXED’ |
| currentNrOfMembers | NP | O | NP | NP | xs:integer | No default (This is generated by the hosting CSE and limited by the maxNrOfMembers attribute of the <group> resource) |
| maxNrOfMembers | M | O | O | NP | xs:integer | No default |
| membersList | M | O | O | NP | List of m2m:anyURI | No default |
| membersAccessControlPolicyIDs | O | O | O | NP | xs:anyURI | No default |
| memberTypeValidated | NP | O | NP | NP | xs:boolean | No default (This is generated by the hosting CSE) |
| consistencyStrategy | O | O | NP | NP | m2m:consistencyStrategy | Default value is set to ‘ABANDON_MEMBER’ |
| groupName | O | O | O | NP | xs:string | No default |
| creator | O | O | NP | NP | xs:anyURI | No default |

## ----------------------- End of change 12 -----------------------

## ----------------------- Start of change 13 -----------------------

### Resource Type <mgmtObj>

…

Table 7.3.14.1-2: Common Attributes on <mgmtObj>

| Attribute Name | Request Optionality | Default Value | Resource Specific Note |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| resourceType | NP | O | O | NP | See table 6.3.5-1 | None |
| resourceID | NP | O | O | NP | See table 6.3.5-1 | None |
| parentID | NP | O | NP | NP | See table 6.3.5-1 | None |
| accessControlPolicyIDs | O | O | NP | NP | See table 6.3.5-1 | None |
| creationTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| expirationTime | O | O | O | NP | See table 6.3.5-1 | None |
| lastModifiedTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| labels | O | O | O | NP | See table 6.3.5-1 | None |

Table 7.3.14.1-3: Resource Specific Attributes on <mgmtObj>

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | NP | NP | m2m:mgmtDefinition | No default |
| objectIDs | O | O | NP | NP | List of xs:anyURI | No default |
| objectPaths | O | O | NP | NP | List of xs:anyURI | No default |
| description | O | O | O | NP | xs:string | No default |
| mgmtLink | O | O | O | NP | m2m:mgmtLinkRef | No default |

## ----------------------- End of change 13 -----------------------

## ----------------------- Start of change 14 -----------------------

### Resource Type <mgmtCmd>

…

Table 7.3.15.1-2: Common Attributes on <mgmtCmd>

| Attribute Name | Request Optionality | Default Value | Resource Specific Note |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| resourceType | NP | O | NP | NP | See table 6.3.5-1 | None |
| resourceID | NP | O | NP | NP | See table 6.3.5-1 | None |
| parentID | NP | O | NP | NP | See table 6.3.5-1 | None |
| accessControlPolicyIDs | O | O | NP | NP | See table 6.3.5-1 | None |
| creationTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| expirationTime | O | O | O | NP | See table 6.3.5-1 | None |
| lastModifiedTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| labels | O | O | O | NP | See table 6.3.5-1 | None |

Table 7.3.15.1-3: Resource Specific Attributes on <mgmtCmd>

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| description | O | O | O | NP | xs:string | size: 256 No default |
| cmdType | M | O | O | NP | m2m:cmdType | RESET, REBOOT, UPLOAD, DOWNLOAD, SOFTWAREINSTALL, SOFTWAREUPDATE, SOFTWAREUNINSTALL No default |
| execReqType | O | O | O | NP | m2m:execReqArgsListType | A list of entries which are dependent on cmdType: If cmdType=RESET, execReqArgsList=resetArgsType. If cmdType=REBOOT, execReqArgsList=rebootArgsType. If cmdType=UPLOAD, execReqArgsList=uploadArgsType. If cmdType=DOWNLOAD, execReqArgsList=downloadArgsType. If cmdType=SOFTWAREINSTALL, execReqArgsList=softwareInstallArgsType. If cmdType=SOFTWAREUPDATE, execReqArgsList=softwareUpdateArgsType. If cmdType= SOFTWAREUNINSTALL, execReqArgsList=softwareUninstallArgsType. No default |
| execEnable | O | O | O | NP | xs:anyURI | No default |
| execTarget | M | O | O | NP | m2m:nodeID | No default |
| execMode | M | O | O | NP | m2m:execModeType | IMMEDIATEONCE, IMMEDIATEREPEAT, RANDOMONCE, RANDOMREPEAT Default=IMMEDIATEONCE |
| execFrequency | O | O | O | NP | xs:duration | No default |
| execDelay | O | O | O | NP | xs:duration | Default=0 |
| execNumber | O | O | O | NP | xs:nonNegativeInteger | Default=1 |

## ----------------------- End of change 14 -----------------------

## ----------------------- Start of change 15 -----------------------

### Resource Type <execInstance>

…

Table 7.3.16.1-2: Common Attributes on <execInstance>

| Attribute Name | Request Optionality | Default Value | Resource Specific Note |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| resourceType | NP | O | NP | NP | See table 6.3.5-1 | None |
| resourceID | NP | O | NP | NP | See table 6.3.5-1 | None |
| parentID | NP | O | NP | NP | See table 6.3.5-1 | None |
| accessControlPolicyIDs | O | O | NP | NP | See table 6.3.5-1 | None |
| creationTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| expirationTime | O | O | O | NP | See table 6.3.5-1 | None |
| lastModifiedTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| labels | O | O | O | NP | See table 6.3.5-1 | None |

Table 7.3.16.1-3: Resource Specific Attributes on <execInstance>

| Attribute Name | Request Optionality | Default Value | Resource Specific Note |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| execStatus | NP | O | O | NP | m2m:execStatusType | INITATED, PENDING, FINISHED, CANCELLING, CANCELLED Default=INITIATED |
| execResult | NP | O | O | NP | xs:execResultType | No default |
| execDisable | NP | O | O | NP | xs:string | No default |
| execTarget | O | O | O | NP | m2m:nodeID | No default |
| execMode | O | O | O | NP | m2m:execModeType | IMMEDIATEONCE, IMMEDIATEREPEAT, RANDOMONCE, RANDOMREPEAT Default=IMMEDIATEONCE |
| execFrequency | O | O | O | NP | xs:duration | No default |
| execDelay | O | O | O | NP | xs:duration | Default=0 |
| execNumber | O | O | O | NP | xs:nonNegativeInteger | Default=1 |
| execReqArgs | O | O | O | NP | m2m:execReqArgsListType | No default |

## ----------------------- End of change 15 -----------------------

## ----------------------- Start of change 16 -----------------------

### Resource Type <node>

…

Table 7.3.17.1-2: Common Attributes on <node>

| Attribute Name | Request Optionality | Default Value | Resource Specific Note |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| resourceType | NP | O | NP | NP | See table 6.3.5-1 | None |
| resourceID | NP | O | NP | NP | See table 6.3.5-1 | None |
| parentID | NP | O | NP | NP | See table 6.3.5-1 | None |
| accessControlPolicyIDs | O | O | NP | NP | See table 6.3.5-1 | None |
| creationTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| expirationTime | O | O | O | NP | See table 6.3.5-1 | None |
| lastModifiedTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| labels | O | O | O | NP | See table 6.3.5-1 | None |

Table 7.3.17.1-3: Resource Specific Attributes on <node>

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| nodeID | M | O | O | NP | m2m:nodeID | No default |
| hostedCSEID | O | O | NP | NP | m2m:id | No default |

## ----------------------- End of change 16 -----------------------

## ----------------------- Start of change 17 -----------------------

### Resource Type <m2mServiceSubscriptionProfile>

…

Table 7.3.18.1-2: Common Attributes on <m2mServiceSubscriptionProfile>

| Attribute Name | Request Optionality | Default Value | Resource Specific Note |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| resourceType | NP | O | NP | NP | See table 6.3.5-1 | None |
| resourceID | NP | O | NP | NP | See table 6.3.5-1 | None |
| parentID | NP | O | NP | NP | See table 6.3.5-1 | None |
| expirationTime | O | O | O | NP | See table 6.3.5-1 | None |
| accessControlPolicyIDs | O | O | O | NP | See table 6.3.5-1 | None |
| creationTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| labels | O | O | O | NP | See table 6.3.5-1 | None |
| lastModifiedTime | NP | O | NP | NP | See table 6.3.5-1 | None |

Table 7.3.18.1-3: Resource Specific Attributes on <m2mServiceSubscriptionProfile>

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| serviceRoles | O | O | O | NP | M2m:serviceRoles | No default |

## ----------------------- End of change 17 -----------------------

## ----------------------- Start of change 18 -----------------------

### Resource Type <authorizedNode>

…

Table 7.3.19.1-2: Common Attributes on <authorizedNode >

| Attribute Name | Request Optionality | Default Value | Resource Specific Note |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| resourceType | NP | O | NP | NP | See table 6.3.5-1 | None |
| resourceID | NP | O | NP | NP | See table 6.3.5-1 | None |
| parentID | NP | O | NP | NP | See table 6.3.5-1 | None |
| expirationTime | O | O | O | NP | See table 6.3.5-1 | None |
| accessControlPolicyIDs | O | O | O | NP | See table 6.3.5-1 | None |
| creationTime | NP | O | O | NP | See table 6.3.5-1 | None |
| labels | O | O | O | NP | See table 6.3.5-1 | None |
| lastModifiedTime | NP | O | NP | NP | See table 6.3.5-1 | None |

Table 7.3.19.1-3: Resource Specific Attributes on <authorizedNode >

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| nodeID | M | O | O | NP | m2m:nodeId | No default |
| AE-IDs | O | O | O | NP | m2m:id | No default |
| CSE-ID | O | O | O | NP | m2m:id | No default |

## ----------------------- End of change 18 -----------------------

## ----------------------- Start of change 19 -----------------------

### Resource Type <pollingChannel>

…

Table 7.3.20.1-2: Common Attributes on <pollingChannel>

| Attribute Name | Request Optionality | Default Value | Resource Specific Note |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| resourceType | NP | O | NP | NP | See table 6.3.5-1 | None |
| resourceID | NP | O | NP | NP | See table 6.3.5-1 | None |
| parentID | NP | O | NP | NP | See table 6.3.5-1 | None |
| creationTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| lastModifiedTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| expirationTime | O | O | O | NP | See table 6.3.5-1 | None |
| accessControlPolicyIDs | O | O | NP | NP | See table 6.3.5-1 | None |
| labels | O | O | O | NP | See table 6.3.5-1 | None |

## ----------------------- End of change 19 -----------------------

## ----------------------- Start of change 20 -----------------------

### Resource Type <statsConfig>

…

Table 7.3.22.1-2: Common Attributes on <statsConfig>

| Attribute Name | Request Optionality | Default Value | Resource Specific Note |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| resourceType | NP | O | NP | NP | See table 6.3.5-1 | None |
| resourceID | NP | O | NP | NP | See table 6.3.5-1 | None |
| parentID | NP | O | NP | NP | See table 6.3.5-1 | None |
| accessControlPolicyIDs | O | O | O | NP | See table 6.3.5-1 | None |
| creationTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| expirationTime | O | O | O | NP | See table 6.3.5-1 | None |
| lastModifiedTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| labels | O | O | O | NP | See table 6.3.5-1 | None |

Table  7.3.22.1-3Resource specific attributes on <statsConfig>

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| creator | NP | O | NP | NP | m2m:ID | No default |

## ----------------------- End of change 20 -----------------------

## ----------------------- Start of change 21 -----------------------

### Resource Type <eventConfig>

…

Table 7.3.23.1-2: Common Attributes on <eventConfig>

| Attribute Name | Request Optionality | Default Value | Resource Specific Note |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| resourceType | NP | O | NP | NP | See table 6.3.5-1 | None |
| resourceID | NP | O | NP | NP | See table 6.3.5-1 | None |
| parentID | NP | O | NP | NP | See table 6.3.5-1 | None |
| accessControlPolicyIDs | O | O | O | NP | See table 6.3.5-1 | None |
| creationTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| expirationTime | O | O | O | NP | See table 6.3.5-1 | None |
| lastModifiedTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| labels | O | O | O | NP | See table 6.3.5-1 | None |

Table 7.3.23.1-3: Resource Specific Attributes on <eventConfig>

| Attribute Name | Request Optionality | Default Value | Resource Specific Note |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| creator | NP | O | NP | NP | m2m:ID | No default |
| eventID | NP | O | NP | NP | xs:string | Uniquely identifies a configurable event No default |
| eventType | M | O | O | NP | m2m:eventType | DATAOPERATION STORAGEBASED TIMERBASED No default |
| eventStart | O | O | O | NP | xs:dateTime | No default (present only when eventType is set to TIMERBASED) |
| eventEnd | O | O | O | NP | xs:dateTime | No default (present only when eventType is set to TIMERBASED) |
| operationType | O | O | O | NP | list of m2m:operation | CREATE RETRIEVE UPDATE DELETE NOTIFY No default (present only when eventType is set to DATAOPERATION) |
| dataSize | O | O | O | NP | xs:nonNegativeInteger | No default (present only when eventType is set to STORAGEBASED) |

## ----------------------- End of change 21 -----------------------

## ----------------------- Start of change 22 -----------------------

### Resource Type <statsCollect>

…

Table 7.3.24.1-2: Common Attributes on <statsCollect>

| Attribute Name | Request Optionality | Default Value | Resource Specific Note |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| resourceType | NP | O | NP | NP | See table 6.3.5-1 | None |
| resourceID | NP | O | NP | NP | See table 6.3.5-1 | None |
| parentID | NP | O | NP | NP | See table 6.3.5-1 | None |
| accessControlPolicyIDs | O | O | O | NP | See table 6.3.5-1 | None |
| creationTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| expirationTime | O | O | O | NP | See table 6.3.5-1 | None |
| lastModifiedTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| labels | O | O | O | NP | See table 6.3.5-1 | None |

Table 7.3.24.1-3: Resource Specific Attributes on <statsCollect>

| Attribute Name | Request Optionality | Default Value | Resource Specific Note |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| creator | NP | O | NP | NP | m2m:ID | No default |
| statsCollectID | NP | O | NP | NP | xs:string | Unique ID (within SP domain) for each instance of collected statistics No default |
| collectingEntityID | M | O | NP | NP | m2m:ID | Unique ID of entity (e.g., IN-AE, IN-CSE) requesting the collection of statistics No default |
| collectedEntityID | M | O | NP | NP | m2m:ID | Unique ID of entity (e.g., AE, CSE) for which statistics will be collected No default |
| statsRuleStatus | M | O | O | NP | m2m:statsRuleStatusType | ACTIVE INACTIVE No default |
| statModel | M | O | O | NP | m2m:statModelType | EVENTBASED Default=EVENTBASED |
| collectPeriod | O | O | O | NP | Extended Crontab Data String | No default (see Table 7.3.81-4 for Extended Crontab Data String structure) |
| eventID | O | O | O | NP | xs:string | Uniquely identifies a configurable event No default (present when statModel is set to EVENTBASED; corresponds to an eventID attribute in an <eventConfig> resource that defines a specific event for collection) |

## ----------------------- End of change 22 -----------------------

## ----------------------- Start of change 23 -----------------------

### Announced resource type

…

Table 7.3.25.1-2:  Applicable Common Attributes on Announced Resource

| Attribute Name | Request Optionality | Default Value | Resource Specific Note |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| resourceType | NP | O | NP | NP | See table 6.3.5-1 | The resource type of the announced resource shall be provided |
| resourceID | NP | O | NP | NP | See table 6.3.5-1 | None |
| parentID | NP | O | NP | NP | See table 6.3.5-1 | None |
| accessControlPolicyIDs | O | O | O | NP | See table 6.3.5-1 | None |
| creationTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| expirationTime | O | O | O | NP | See table 6.3.5-1 | None |
| lastModifiedTime | NP | O | NP | NP | See table 6.3.5-1 | None |
| labels | O | O | O | NP | See table 6.3.5-1 | None |
| link | M | O | O | NP | See table 6.3.5-1 | None |

## ----------------------- End of change 23 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?