| CHANGE REQUEST |
| --- |
| Group Name:* | PRO |
| Source:* | LG Electronics |
| Format:* |  |
| Date:* | 2015-01-15 |
| Contact:* | SeungMyeong JEONG (seungmyeong.jeong@lge.com) |
| Reason for Change/s:* | Cleanup all editor’s note in clause 6 |
| CR against: Release* | v.0.6.0 |
| CR against: TS/TR* | TS-0009 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Un-resolved editor’s notes in this version/revision is highlighted in yellow for the moment. They need more discussion or pending due to the related issues in TS-0004.

## ----------------------- Start of change 1 -----------------------

## 6.2 Parameter Mappings on Request-Line

### 6.2.1	Method

The HTTP ‘Method’ shall be specified according to the oneM2M operation parameter of the request primitive.

Table 6.2.1-1: HTTP Method Mapping

| oneM2M Operation | HTTP Method |
| --- | --- |
| Create | POST |
| Retrieve | GET |
| Update | PUT or POST (for partial update) |
| Delete | DELETE |
| Notify | POST |

Editor’s Note: Update operation mapping is TBD until the attribute level manipulation scheme is resolved in TS-0001 and TS-0004.

At the Receiver, an HTTP request message with POST method shall be mapped to a oneM2M Create or Notify request primitive in accordance with the value of the operation parameter.

### 6.2.2	Request-Target

The HTTP Request-Target shall be prepared as origin-form (see [1]).

The to parameter shall be mapped to ‘absolute-path’ in Request-Target.

Other request parameter shall be specified as pair of field-name and value in query-string as shown in Table 6.2.2-1.

Table 6.2.2-1: Request parameters mapped as query-string field

| Request Parameter | Field Name | Note |
| --- | --- | --- |
| Name | nm field |  |
| Request Expiration Timestamp | ret field |  |
| Operation Execution Time | oet field |  |
| Response Type | rt field |  |
| Result Persistence | rp field |  |
| Result Content | rc field |  |
| Delivery Aggregation | da field |  |
| Group Request Identifier | gid field |  |
| Filter Criteria | fc field |  |
| Discovery Result Type | drt field |  |

### 6.2.3	HTTP-Version

This specification supports binding to HTTP 1.1[1], so the version field shall be set to “HTTP/1.1”.

| 6.2.4 |  |  |
| --- | --- | --- |

## 6.3	Status-Line

### 6.3.1	HTTP-Version

This specification supports binding to HTTP 1.1[1], so the version field shall be set to “HTTP/1.1”.

### 6.3.2	Status-Code

The response status code parameter shall be mapped to HTTP Status-Code. Since the response status code parameter have been defined more specifically than HTTP status codes, one or more response status code may be mapped to one Status-Code. The original response status code parameter shall be carried in X-M2M-RSC(see clause 6.4.14).

N:1 status code mapping from the oneM2M request primitive to HTTP request message shall be:

Table 6.3.2-1: Status Code Mapping

| oneM2M Response Status Codes | HTTP Status Codes |
| --- | --- |
| Success | 200 (OK) |
| Accepted | 202 (Accepted) |
| Location info not authorized | 403 (Forbidden) |
| Unsupported resource | 404 (Not Found) |
| Unsupported attribute | 404 (Not Found) |
| Cannot forward, target not reachable | 404 (Not Found) |
| Cannot forward, other reason TBD | 404 (Not Found) |
| Create error – no privilege | 403 (Forbidden) |
| Create error – already exists | 403 (Forbidden) |
| Create error – missing mandatory parameter | 400 (Bad Request) |
| Retrieve error – no privilege | 403 (Forbidden) |
| Retrieve error – does not exist | 404 (Not Found) |
| Update error – no privilege | 403 (Forbidden) |
| Update error – does not exist | 404 (Not Found) |
| Update error – unacceptable contents | 415 (Unsupported Media Type) |
| Delete error – does not exist | 404 (Not Found) |
| Delete error – no privilege | 403 (Forbidden) |
| Create delivery – not able to take on responsibility | 403 (Forbidden) |
| Create fanoutpoint – group request identifier exists | 409 (Conflicts) |
| Retrieve fanoutpoint – group request identifier exists | 409 (Conflicts) |
| Update fanoutpoint – group request identifier exists | 409 (Conflicts) |
| Delete fanoutpoint – group request identifier exists | 409 (Conflicts) |
| Create mgmtObj – memory shortage | 403 (Forbidden) |
| External object not found | 404 (Not Found) |
| Cancel execInstance – not cancellable | 403 (Forbidden) |
| Cancel execInstance – already complete | 403 (Forbidden) |
| Delete execInstance – not cancellable | 403 (Forbidden) |
| Delete execInstance – already complete | 403 (Forbidden) |
| Retrieve CSEBase – format error | 400 (Bad Request) |
| CMDH rules –non compliant | 403 (Forbidden) |
| Target is not subscribable | 403 (Forbidden) |
| Cannot initiate subscription verification | 403 (Forbidden) |
| Subscription verification failed | 403 (Forbidden) |

Editor’s Note: This table needs to be updated aligning with TS-0004.

### 6.3.3	Reason-Phrase

Reason-Phrase shall be omitted.

## 6.4	Header Fields

### 6.4.1	Host

The Host header shall be included in an HTTP request message.

While the Request-Target indicates a target resource on the Hosting CSE, the Host header indicates a Receiver CSE in multi-hop communication. Therefore, the the Request-Target is not changed but the Host header is changed each time when a request is forwarded.

The Host header shall be set as one of pointOfAccess attribute values of the Receiver(i.e., pointOfAccess attribute of the corresponding <remoteCSE> resource). Selection of the proper Receiver is described in TS-0004 [3].

### 6.4.2	Accept

An Originator may use the Accept header to indicate which content-type is supported by the Originator.  The Accept header shall be set to “application/onem2m-resource+xml” or “application/onem2m-resource+json”.

Editor’s Note: Supported types are TBD.

### 6.4.3	Content-type

Any request or response containing message-body shall include the Content-type header set to “application/onem2m-resource+xml” or “application/onem2m-resource+json”.

Editor’s Note: Supported types are TBD.

### 6.4.4	Content-Location

The Content-Location header shall be set to the URI of:

- the created resource, when responding to a Create request primitive;

- the retrieved resource, when responding to a Retrieve request primitive if the retrieved resource location is different from the requested resource location;

- the updated resource, when responding to a Update request primitive

Editor’s Note: Usage of this header needs more investigation.

Editor’s Note: How to indicate the oneM2M URI scheme is TBD

### 6.4.5	Content-Length

If message-body is included, the Content-Length header shall be included indicating the length of the message-body in octets (8-bit bytes).

### 6.4.6	Etag

A retrieve response primitive corresponding to a resource retrieval request primitive should include an Etag header together with the resource representation [1].

Etag facilitates the use of conditional requests (i.e. using the if-match and if-none-match HTTP headers).

If a CSE supports the Etag header, then the CSE shall support conditional requests.

### 6.4.7	From

The From header shall be mapped to the from parameter of the request/response primitive, and shall contain the oneM2M specified ID of the Originator (e.g. CSE-ID or AE-ID).

### 6.4.8	Location

The Location header shall be mapped to the URI of the created resource. This header shall be present in the response primitive corresponding to a create request and shall not be present in any other request or response.

Editor’s Note: if Originator’s nm parameter can be modified and accepted by the Hosting CSE is TBD.

### 6.4.9	X-M2M-RI

### The X-M2M-RI header shall be mapped to the request identifier parameter.

### 6.4.10	X-M2M-OT

The X-M2M-OT header shall be mapped to the originating timestamp parameter if applicable.

### 6.4.11	X-M2M-RST

The X-M2M-RST header shall be mapped to the result expiration timestamp parameter if applicable.

### 6.4.12	X-M2M-ECT

The X-M2M-ECT header shall be mapped to the eventCatType element of the event category parameter if the eventCatType element is used.

### 6.4.13	X-M2M-ECN

The X-M2M-ECN header shall be mapped to the eventCatNo element of the event category parameter if the eventCatNo element is used.

### 6.4.14	X-M2M-RSC

The X-M2M-RSC header shall be mapped to the code element of the response status code parameter.

## 6.5	Message-body

Message-body shall be mapped to the primitive content parameter if applicable.

## 6.6	 Message Routing

HTTP request and response message routing shall be performed as described in HTTP/1.1 [1].

## ----------------------- End of change 1 -----------------------

## ----------------------- Start of change 2 -----------------------

## ----------------------- End of change 2 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Comments

This text can be removed to clause 6.4.3.

TS-0004 has no such description. This needs to be discussed.