| CHANGE REQUEST |
| --- |
| Group Name:* | PRO |
| Source:* | FUJITSU |
| Format:* | Physical Meeting |
| Date:* | 2015-01-16 |
| Contact:* | Shingo Fujimoto, FUJITSU, shingo_fujimoto@jp.fujitus.com |
| Reason for Change/s:* | typeOfContent attribute is changed in TS-0001, and it need to be harmonized with TS-0004. |
| CR against: Release* | v.0.8.0 |
| CR against: TS/TR* | TS-0004 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

typeOfContent attribute is changed in TS-0001, and it need to be harmonized with TS-0004.

### -----------------------Start of change 1-------------------------------------------

### 7.3.6 Resource Type <contentInstance>

#### 7.3.6.1 Introduction

The <contentInstance> resource represents a data instance in the container.

The detailed description can be found in clause 9.6.7 in TS-0001 Functional Architecture [6].

Table 7.2.6.1-1: Data Type Definition of <contentInstance>

| Data Type ID | File Name | Note |
| --- | --- | --- |
| contentInstance | CDT-contentInstance-v1_0_0.xsd |  |

Table 7.2.6.1-2: Applicable Common Attributes on <contentInstance>

| Attribute Name | Request Optionality | Default Value | Resource Specific Note |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| resourceType | NP | O | NP | NP |  |  |
| resourceID | NP | O | NP | NP |  |  |
| parentID | NP | O | NP | NP |  |  |
| creationTime | NP | O | NP | NP |  |  |
| lastModifiedTime | NP | O | NP | NP |  |  |
| stateTag | NP | O | NP | NP |  |  |
| Labels | O | O | NP | NP |  |  |
| announceTo | O | O | NP | NP |  |  |
| announcedAttribute | NP | O | NP | NP |  |  |
| creator | O | O | NP | NP |  |  |

Editor’s Note: creator may be added to resource specific attributes table depends on the resolution on common attributes.

Table 7.2.6.1-3:Resource specific attributes on <contentInstance>

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| contentInfot | M | O | NP | NP | xs:string | The paired values consit with one of IANA registered Media Types names or experimental Media Types names shall be specified (See [26]) and m2m:encodingType. |
| contentSize | O | O | NP | NP | xs:nonNegativeInteger |  |
| ontologyRef | O | O | NP | NP | xs:anyURI |  |
| content | M | O | NP | NP | xs:anySimpleType | Transfer encoding may be applied, and indicated applied encoding at encoding attribute |

#### 7.3.6.2 <contentInstance> resource specific procedure on CRUD operations

##### 7.3.6.2.1 Create

Originator:

No change from the generic procedures in clause 7.1.2.1.

Receiver:

No change from the generic procedures in clause 7.1.2.2. The Originator may omit the name of the <contentInstance> resource unless the Originator need to refer specific content later.

##### 7.3.6.2.2 Retrieve

Originator:

No change from the generic procedures in clause 7.1.2.1.

Receiver:

No change from the generic procedures in clause 7.1.2.2. The Originator may omit the name of the targeted <contentInstance> resource when the latest version of stored content is requested.

##### 7.3.6.2.3 Update

Originator:

The <contentInstance> resource shall not be Updated via API.

Receiver:

Primitive specific operation on Recv-1.0 "Check the syntax of received message":

If the request is received, the Receiver CSE shall execute the following steps in order.

- "Create an unsuccessful Response primitive" with the response status code ‘Request not allowed’.

- "Send the Response primitive".

##### 7.3.6.2.4 Delete

Originator:

No change from the generic procedures in clause 7.1.2.1.

Receiver:

No change from the generic procedures in clause 7.1.2.2.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?