| CHANGE REQUEST |
| --- |
| Group Name:* | TP#15 |
| Source:* | Yuan Tao, Huawei Technologies, Co. Ltd., taoyuan.tao@huawei.com |
| Format:* | Plenary |
| Date:* | <2015-01-19~23> |
| Contact:* | Yuan Tao, Huawei Technologies, Co. Ltd. ,taoyuan.tao@huawei.com |
| Reason for Change/s:* | This contribution intends to revise Annex E base on the discussion in the PRO 14.3. |
| CR against: Release* | Release 1 |
| CR against: TS/TR* | TS-0004 v0.8.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution intends to revise Annex E base on the discussion in the PRO 14.3.

### -----------------------Start of change 1-------------------------------------------

(informative) Procedures for accessing resources

Accessing resources in CSEs – blocking requests

The result of a Request is sent back to the originator as part of the Response of the Request. The Originator of the Request typically has a thread of excecution that is blocked waiting for the Response to come back. This communication mode could  result in long blocking times.

The interaction employing blocking involves the following steps in this order:

Figure E.1-2: Blocking access to resource

- The Originator sends a request to accessing a resource. The Response Type parameter of the request is set  to ‘blockingRequest’. The Response Type parameter can be omitted in this case since ‘blockingRequest’ is its default value

- The Hosting CSE receives the request, and it completes the requested processing of resources.

- The Hosting CSE responds to Originator, the response contains the requested results in resource content, and the Response Status Code parameter of response is set to successful.

Accessing Resources in CSEs - non-blocking requests

Non-blocking modes

If the Originator chooses the Blocking mode described in clause E.1, it might have to wait a long time for a response from the Receiver. To avoid this possibility it can choose a Non-Blocking mode. In Non-blocking modes, the Receiver sends an Acknowledgement of the request, which provides a reference to the result of the requested operation. The Originator can retrieve the result at a later time.

There are two forms of Non-blocking mode: Synchronous and Asynchronous.

Synchronous case

The Originator asks for non-Blocking Communication by setting  the Response Type parameter of the Request  to 'nonBlockingRequestSynch'. The Receiver  CSE responds after acceptance with an Acknowledgement confirming, that it will process the Request further. The Receiver CSE creates a local <request> resource pertaining to the Request received and returns a reference to this created <request> resource as the Content of the acknowledgement Response. Then the Receiver needs to forward the Request to the next CSE if the Receiver  CSE is not the Hosting CSE of the addressed resource. Or the Hosting CSE needs to start handling the Request if the Receiver CSE is the Hosting CSE of the addressed resource.

The Originator of the Request may retrieve the <request> resource afterwards to check on the status of its Request and to inspect the final result of the Request when this is available.

Figure E.2.1-1 illustrates the steps involved in a synchronous  non-blocking interaction. In this example the Receiver CSE is the CSE that hosts the resource that is the target of the Originator’s request.

Figure E.2.1-1: non-Blocking access to resource in synchronous mode (no hop)

- The originator sends a request to access a resource, setting the Response Type parameter of request to ‘nonblockingRequestSynch’.

- If the Receiver CSE supports non-blocking synchronouse interactions (this is indicated by its support for the <request> resource), it creates an instance of <request> resource. The requestStatus attribute of the <request> resource is set to “LOCALLY_ACCEPTED”.  Please refer to Table 7.1.2.2.4-1 and Table 7.1.2.2.4-2for other attributes.

- The Hosting CSE sends a response to the Originator, the Response Status  Code parameter of its response is set to ‘Locally accepted’ , and a reference to the <request> resource is provided in the Content.

- The Hosting CSE processes the resource according to the requested operation . When the requested operation has finished, the Hosting CSE will UPDATE the <request> resource, putting the results of the operation into the operationResult attribute,  and updating the values of requestStatus, stateTag and lastModifiedTime.

- The Originator requests to RETRIEVE the original requested results by addressing the <request> resource using a non-blocking request.

- The Hosting CSE responds to Originator. The response contains the <request> resource as  its Content, and the Originator can examine the <request> resource’s requestStatus attribute to check that the operation has completed and retrieve its results from the operationResult attribute.

A variation of synchronous case is depicted in the following clauses. In this variation it is assumed that the addressed resource is not stored in the Registrar CSE, then the Registrar CSE needs to be a Transit CSE to forward the request to the Hosting CSE.

Figure E.2.1-2 illustrates this case. :

Figure E.2.1-2: non-Blocking access to resource in synchronous mode (one hop)

- 1. The Originator sends a request to its Registrar CSE (this is aTransit CSE, not the Hosting CSE), setting the Response Type parameter of the request to ‘nonblockingRequestSynch’.

- If the Transit CSE supports non-blocking synchronouse interactions (this is indicated by its support for the <request> resource), it creates an instance of <request> resource. The requestStatus attribute of the <request> resource is set to TBD. The Please refer to Table 7.2.11.1-2 for other attributes.

- The Transit  CSE sends a response to the Originator, the Response Status Code parameter of its response is set to acknowledgement, and a reference to the <request> resource is provided in the Content.

- The Transit CSE forwards the original request to the Hosting CSE.

- If the Hosting  CSE supports non-blocking synchronouse interactions (this is indicated by its support for the <request> resource), it creates an instance of <request> resource. The requestStatus attribute of the <request> resource is set to “LOCALLY_ACCEPTED”. Please refer to Table 7.1.2.2.4-1 and Table 7.1.2.2.4-2for other attributes..

- The Hosting CSE sends a response to the Transit CSE, the Response Status Code parameter of its response is set to‘Loocally accepted’ and a reference to the <request> resource is provided in the Content.

- The Hosting CSE processes the resource according to the requested operation. When the requested operation has finihsed, the Hosting CSE will UPDATE the <request> resource, putting the results of the operation into the operationResult attribute, and updating the values of requestStatus, stateTag and lastModifiedTime.

- The Transit CSE requests to RETRIEVE the original requested results by addressing the <request> resource using a non-blocking request.

- The Hosting CSE sends a response to the Transit CSE. The response contains the <request> resource as  its Content.

- The Transit CSE UPDATEs its <request> resource, copying  the operationResult from the response that it received from the Hosting CSE. It also updates the values of requestStatus, stateTag and lastModifiedTime.

- The Originator requests to RETRIEVE the original requested results by addressing the <request> resource using a non-blocking request.

- The Transit CSE responds to Originator. The response contains the <request> resource as  its Content, and the Originator can examine the <request> resource’s requestStatus attribute to check that the operation has completed and retrieve its results from the operationResult attribute.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Comments

It’s not appropriate to talk about  connections here, as different protocols have different connection  strategies

I can’t find anything in TS-0001 or TS-0004 about the default value for ResponseType. I think we should define what the default value is (if indeed there is one)  in TS-0004. If we decide that blockingRequest is the default, then this needs to be adjusted to say that the parameter may be omitted (as blockingRequest is its default value). If we decide the blockingRequest is not the default, then this text must be deleted.

Step 5 looks wrong. I would expect the originator to  make a  RETRIEVE request on the <request> resoiurce, rather than making a request against the CSE passing the <request>’s URI as the primitive’s content paramter. Also i would expect in step 6 the cn: is the entire <request> resource not just the requested results. Finally there is no rsc: parameter in TS0001.

I think this is what the intention of the text is..  It seems from TS-0001 that support for non-blocking is Optional.

Need to provide the correct value here, and also make sure that the Link to the table is updated correctly

Should we also mention how the CSE sets the expiration time of this resource?

TS-0001 states that there are two parameters, one called "Response Code" and the other called "Status Code". Have we decided to combine the the two?

I think this is the intention of TS-0001.

See my comment on the other figure

I think this is what the intention of the text is..  It seems from TS-0001 that support for non-blocking is Optional.

Need to provide the correct value here, and also make sure that the Link to the table is updated correctly

Should we also mention how the CSE sets the expiration time of this resource?

TS-0001 states that there are two parameters, one called "Response Code" and the other called "Status Code". Have we decided to combine the the two?

I think this is what the intention of the text is..  It seems from TS-0001 that support for non-blocking is Optional.

Need to provide the correct value here, and also make sure that the Link to the table is updated correctly

Should we also mention how the CSE sets the expiration time of this resource?

I think this is the intention of TS-0001.