| CHANGE REQUEST |
| --- |
| Meeting:* | PRO 14.2bis |
| Source:* | FUJITSU |
| Date:* | 2015-01-22 |
| Contact:* | Shingo Fujimoto, FUJITSU, Shingo_fujimoto@jp.fujitsu.com |
| Reason for Change/s:* | filterCriteria in use as request parameter should have shortname. |
| CR against: Release* | 1.0 (DRAFT) |
| CR against: TS/TR* | TS-0009-V0.6.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

### filterCriteria in use as request primitive parameter should have its own shortname definition with same name in filterCritera attributes.

### -----------------------Start of change 1-------------------------------------------

### 6.2.2. Request-Target

The path component of HTTP Request-Target shall be interpreted as the mapping of oneM2M To parameter, and the query component (e.g. query-string) shall be interpreted as other primitive parameters  (see [1]).

The Originator shall add the prefix string "http:" to the absolute form of oneM2M address (see [3]) when the address is used in the absolute-form URI in the request-target.

The request parameters which are not specified as oneM2M extension header in clasue 6.4, shall be specified as pair of field-name and value in query-string as shown in Table 6.2.2-1.

Table 6.2.2-1: oneM2M Request parameters mapped as query-string field

| Request Parameter | Field Name | Note |
| --- | --- | --- |
| Name | nm field |  |
| Request Expiration Timestamp | ret field |  |
| Operation Execution Time | oet field |  |
| Response Type | rt field |  |
| Result Persistence | rp field |  |
| Result Content | rc field |  |
| Delivery Aggregation | da field |  |
| Group Request Identifier | gid field |  |
| createdBefore | crb field | filterCriteria condition |
| createdAfter | cra field | filterCriteria condition |
| modifiedSince | ms field | filterCriteria condition |
| unmodifiedSince | us field | filterCriteria condition |
| stateTagSmaller | sts field | filterCriteria condition |
| stateTagBigger | stb field | filterCriteria condition |
| expireBefore | exb field | filterCriteria condition |
| expireAfter | exa field | filterCriteria condition |
| labels | lbl field | filterCriteria condition |
| resourceType | rty field | filterCriteria condition |
| sizeAbove | sza field | filterCriteria condition |
| sizeBelow | szb field | filterCriteria condition |
| contentType | cty field | filterCriteria condition |
| limit | lim field | filterCriteria condition |
| attribute | atr field | filterCriteria condition |
| filterUsage | fc field | filterCriteria condition |
| Discovery Result Type | drt field |  |

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?