| INPUT CONTRIBUTION |
| --- |
| Group Name:* | PRO |
| Title:* | CoAP New Options Descriptions |
| Source:* | LG Electronics |
| Contact: | Seongyoon Kim, LG Electronics, seongyoon.kim@lge.com |
| Date:* | 2014-01-15 |
| Abstract:* | CoAP New Options Descriptions |
| Agenda Item:* | PRO |
| Work item(s): | WI 0009 |
| Document(s) Impacted* | Technical Specification – CoAP Protocol Binding |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Approve the proposed change and integrate it into the TS document |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Rationale

This contribution defines new CoAP options used to bind oneM2M parameters.

- Mandatory parameters are marked as Critical; Optional parameters are marked as Elective.

- Since we don’t use CoAP proxy function, Unsafe & NoCacheKey are not used

- R01:

1. Move From, Request Expiration Timestamp , Operation Execution Time, responseType element of Response Type , Name, Group Request Identifier (Variable Values) from query string to CoAP Option.

2. Combine Event Category Type and Event Category Name into Event Category aligned with TS-0004.

3. Add Resource Type parameter which was missing.

4. Move Filter Criteria to Query String

R02:

Remove default value.

========================Start of 1st Change==========================

## 6.2.4	New Options Definitions

## This clause describes new CoAP Options used for binding several oneM2M request/response parameters. The table 6.2.4-1 contains definitions of the new CoAP Options and sub-clauses specify oneM2M parameter mapping with the newly defined CoAP Options in table 6.2.4-1.

Table 6.2.4-1: New Options Definitions

| No | C | U | N | R | Name | Format | Length | Default |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 256 | X |  |  |  | oneM2M-FR | string | 0-255 | (None) |
| 257 | X |  |  |  | oneM2M-RQI | string | 0-255 | (None) |
| 258 |  |  |  |  | oneM2M-NM | string | 0-255 | (None) |
| 259 |  |  |  |  | oneM2M-OT | string | 15 | (None) |
| 260 |  |  |  |  | oneM2M-RQET | string | 15 | (None) |
| 261 |  |  |  |  | oneM2M-RSET | string | 15 | (None) |
| 262 |  |  |  |  | oneM2M-OET | string | 15 | (None) |
| 263 |  |  |  |  | oneM2M-RTURI | string | 0-255 | (None) |
| 264 |  |  |  |  | oneM2M-EC | uint | 1 | (None) |
| 265 |  |  |  |  | oneM2M-RSC | uint | 2 | (None) |
| 266 |  |  |  |  | oneM2M-GID | string | 0-255 | (None) |

## Note: table 6.2.4-1 follows the template used in section 5.10 Option Definitions of CoAP specification [1].

# 6.2.4.1	From

# The From parameter shall be mapped to the oneM2M-FR Option.

# 6.2.4.2	Request Identifier

The Request Identifier parameter shall be mapped to the oneM2M-RQI Option.

# 6.2.4.3	Name

The Name parameter shall be mapped to the oneM2M-NM Option.

# 6.2.4.4	Originating Timestamp

The Originating Timestamp parameter shall be mapped to the oneM2M-OT Option.

# 6.2.4.5	Request Expiration Timestamp

The Request Expiration Timestamp parameter shall be mapped to the oneM2M-RQET Option.

# 6.2.4.6	Result Expiration Timestamp

The Result Expiration Timestamp parameter shall be mapped to the oneM2M-RSET Option.

# 6.2.4.7	Operation Execution Time

The Operation Execution Time parameter shall be mapped to the oneM2M-OET Option.

# 6.2.4.8	notificationURI of Response Type

The notificationURI element of Response Type parameter shall be mapped to the oneM2M-RTURI Option.

# 6.2.4.9	Event Category

The Event Category parameter shall be mapped to the oneM2M-EC Option.

# 6.2.4.10	Response Status Code

The Response Status Code parameter shall be mapped to the oneM2M-RSC Option.

# 6.2.4.11	Group Request Identifier

The Group Request Identifier parameter shall be mapped to the oneM2M-GID Option.

========================End of 1st Change==========================

========================Start of 1st Change==========================

#### 6.2.2.3	URI Options

This clause describes how to configure CoAP Uri-Host, Uri-Port, Uri-Path, and Uri-Query Options.

Host and port part of the address specified in pointOfAccess attribute of <remoteCSE> resource shall be mapped to Uri-Host and Uri-Port respectively.

To parameter shall be mapped to Uri-Path.

Resource Type, responseType element of Response Type, Result Persistence, parameters of Filter Criteria, Delivery Aggregation, Result Content, and Discovery Result Type parameters shall be carried in Uri-Query Option in a short name form as specified in clause 8.2.2 [2].

========================End of 1st Change==========================