| INPUT CONTRIBUTION |
| --- |
| Group Name:* | PRO |
| Title:* | CoAP Content Format |
| Source:* | LG Electronics |
| Contact: | Seongyoon Kim, LG Electronics, seongyoon.kim@lge.com |
| Date:* | 2014-01-15 |
| Abstract:* | CoAP Content Format |
| Agenda Item:* | PRO |
| Work item(s): | WI 0009 |
| Document(s) Impacted* | Technical Specification – CoAP Protocol Binding |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Approve the proposed change and integrate it into the TS document |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Rationale

This contribution specifies possible values for content format / accept option in CoAP layer.

========================Start of 1st Change==========================

## 6.2.1	Content Format Negotiation Options

The CoAP Accept option may be used to indicate which Content-Format is acceptable to an Originator. If a Hosting CSE supports the Content-Format specified in Accept option of the request, the Hosting CSE shall respond with that Content-Format. If the Hosting CSE doesn’t support the Content-Format specified in Accept option of the request, 4.06 "Not Acceptable" shall be sent as a response, unless another error code takes precedence for this response.

Possible values for Content-Format and Accept options are listed as below.

- application/vnd.onem2m-resource-data+xml

- application/vnd.onem2m-response-status+xml

- application/vnd.onem2m-partial-updates+xml

========================End of 1st Change==========================