| CHANGE REQUEST |
| --- |
| Meeting:* | PRO 15 |
| Source:* | FUJITSU |
| Date:* | 2015-01-20 |
| Contact:* | Shingo Fujimoto, FUJITSU, Shingo_fujimoto@jp.fujitsu.com |
| Reason for Change/s:* | oneM2M specifi media types should be updated |
| CR against: Release* | 1.0 (DRAFT) |
| CR against: TS/TR* | TS-0004-V0.8.1 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The use of registered MIME media type ease the process of validation check on received data.

However, there are some needs to allow implementation choosing use of 'application/xml' or 'application/json' media types when the implementation is capable to validate data using XSD definition.

This contribution propose to change existing text to allow use of application/xml or application/json if the imeplementor wished not to use the registerd MIME media types.

This contribution also add the information about use of media type and mapping between oneM2M specific XSD definition and MIME media types.

### -----------------------Start of change 1-------------------------------------------

## 6.7 oneM2M specific MIME media types

The present sub-clause describes the mapping between oneM2M specific data types and the oneM2M specific media types.

The oneM2M specific media types is registered under the vendor tree of "application" mediate type which is prefixed with ‘application/vnd.onem2m-‘on IANA registry.

Use of oneM2M specific MIME media typesEach protocol binding for oneM2M Core Protocol Specification may specify the negotiation mechanism to use or not to use the oneM2M specific media types.

When the AE wished to narrow the scope of coverage on validating exchanged data between CSE and AE, the oneM2M specific MIME types shall be used to indicate the type of data sending to Receiver of the oneM2M primitive.

| oneM2M specific MIME subtype | mapped oneM2M data type | Note |
| --- | --- | --- |
| vnd.onem2m-res+xml | choice of m2m:regularResource or m2m:announceableResource or m2m:announcedResource or m2m:subordinaryResource | The type of oneM2M resource in content shall be indicated by "ty" parameter. XML serialization rule is applied. |
| vnd.onem2m-res+json | choice of m2m:regularResource or m2m:announceableResource or m2m:announcedResource or m2m:subordinaryResource | Same information of above. JSON serialization rule is applied. |
| vnd.onem2m-ntfy+xml | m2m:notificationContent | The type of notified event shall be indicated by 'eventType' parameter. XML serialization rule is applied. |
| vnd.onem2m-ntfy+json | m2m:notificationContent | Same information of above. JSON serialization rule is applied. |
| vnd.onem2m-attrs+xml | m2m:attributeList | The list of name-value pair of attributes. XML serialization rules is applied. |
| vnd.onem2m-attrs+json | m2m:attributeList | Same information of above. JSON serialization rule is applied. |
| vnd.onem2m-prim+xml | m2m:primitiveMessage | The serialized primitive mesaage. XML serialization rule is applied. |
| vnd.onem2m-prim+json | m2m:primitiveMessage | Same information of above. JSON serialization rule is applied. |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

#### 6.3.4.x m2m:notificationContent

Table 6.3.4.x-1: Type Definition of m2m:notificationContent

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| @notifinationType | m2m:notificaitonType | 1 |  |
| subscribedEvent | m2m:singleNotification | 0..n | In case of subscribed notificaiton |
| operationResult | m2m:requestHandingEvent | 0..n | In case of non-blocking async |

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

#### 6.3.4.x m2m:attributeList

Table 6.3.4.x-1: Type Definition of m2m:attributeList

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| attribute | xs:complexType | 1..n |  |
| @name | xs:string | 1 |  |
| value | xs:string | 0..1 |  |

### -----------------------End of change 3---------------------------------------------

### -----------------------Start of change 4-------------------------------------------

#### 6.3.4.x m2m:primitiveMessage

Table 6.3.4.x-1: Type Definition of m2m:primitiveMessage

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| @primitiveType | m2m:primitiveType | 1 | 1: request, 2: response |
| @DeliveryAggregation | xs:boolean | 0..1 |  |
| @EventCategory | m2m:eventCat | 0..1 |  |
| @Operational Execution Timestamp | m2m:timestamp | 0..1 |  |
| @Originating Timestamp | m2m:timestamp | 1 |  |
| @Request Message Expiration Timestamp | m2m:timestamp | 0..1 |  |
| @Request Identifier | m2m:requestID | 1 |  |
| @Result Expiration Timestamp | m2m:timestamp | 0..1 |  |
| @Resource Type | m2m:resourceType | 0..1 |  |
| @Response Message Type | m2m:responseTypeInfo | 1 |  |
| @Result Content | m2m:resultContent | 0..1 |  |
| @From | m2m:ID | 1 |  |
| content | m2m:any | 0..1 |  |
| filterCriteria | m2m:filterCriteria | 0..1 |  |
| Group Request Identifier | xs:string | 0..1 |  |
| Group Request Identifier | xs:string | Group Request Identifier | xs:string |
| Result Expiration Timestamp | m2m:timestamp |  |  |

### -----------------------End of change 4---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?