| CHANGE REQUEST |
| --- |
| Meeting:* | PRO 15 |
| Source:* | FUJITSU |
| Date:* | 2015-01-21 |
| Contact:* | Shingo Fujimoto, FUJITSU, Shingo_fujimoto@jp.fujitsu.com |
| Reason for Change/s:* |  |
| CR against: Release* | 1.0 (DRAFT) |
| CR against: TS/TR* | TS-0004-V0.8.1 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change/correction to existing feature or functionality New feature or functionality |
| Post Freeze checking:* | This CR contains only essential changes and corrections YES NO |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Notification procedure for Non-blocking Async should be specified.R01: correction on typo

### -----------------------Start of change 1-------------------------------------------

#### 7.4.1.2.4 Notification for Asynchronous Non-blocking Request

Originator:

When the process for  a pending Non-blocking-Async request is completed, the Originator (=hosting CSE of the resource) shall send a Notification message to inform the final result of requested operation against the oneM2M resource.

The request primitive message shall be composed as new Non-blocking async with following parameter settings:

- The From parameter shall be set with the address of oneM2M resource which was targeted by the Non-blocking-Async request.

- The To parameter shall be set with the address of Originator in request primitive.

- The Response Type Info shall be set with the value of 'NonBlockingRequestAsync'.

- The Result Content parameter shall be set with the value of 'Nothing'.

- The Content parameter shall be specified with the data which is defined as m2m:singleNotification (see clause 6.3.4.9).

Then, composed Notification request shall be sent to the next-hop CSE.

Receiver:

When the Notification for Non-blocking-Async request is received, and if te <request> resource regarding the Non-blocking Request is exist, the <request> resource shall be Deleted, and if the Notification is not targeted the CSE then the Notification request shall be forwarded to the next-hop CSE. When the forwarding the Notification is successfully completed the internal state holding pending Non-blocking-Async requests shall be updated as the request is completed.

If the received Notification for Non-blocking-Async request was targeted to the CSE, the request shall be re-targeted following procedure described in clause 7.2.3.8. When the re-targeting Notification is successfully completed, the internal state holding pending Non-blocking-Async request shall be updated as the requested is completed.

### -----------------------End of change 1---------------------------------------------

### -

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?