| CHANGE REQUEST |
| --- |
| Meeting:* | PRO#17 |
| Source:* | Sung-Chan Choi, Jaeho Kim |
| Date:* | 2015-05-08 |
| Contact:* | Sung-Chan Choi (csc@keti.re.kr) |
| Reason for Change/s:* | This defines the format indicator (content-type) of the payload in MQTT binding. |
| CR against: Release* | Rel-2 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0010-v1.1.0 |
| Clauses/Sub Clauses* | 6.5.4 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

In CoAP and HTTP binding specification, they defines content-type field in header which indicates content type of message body (payload). However, MQTT does not support something like message type indicators because MQTT protocol was designed as being agnostic to its message payload.

Therefore MQTT binding specification needs to support such a mechanism but, a differenct way comparing to CoAP and HTTP for indicating payload message format such as application/xml or application/json which is defined in TS-0004. This CR defines topic name for message format indicator.

R01: modified topic name to support content-type of MQTT payload

### -----------------------Start of change 1-------------------------------------------

### 6.4.2 Sending a Request

A request is transmitted by sending it as an MQTT PUBLISH protocol packet to the MQTT Server. It uses a Topic that identifies both the Originator and the Receiver of the request as follows:

- /oneM2M/req/<originator>/<receiver>/<type>

- “oneM2M” is a literal string identifying the topic as being used by oneM2M.

- <originator> is the SP-relative-AE-ID or SP-relative-CSE-ID of the entity that sent the request on this hop, omitting any leading / . In the AE-ID case, an / characters embedded in the ID shall be replaced with : characters.

- <receiver> is the SP-relative-CSE-ID of the Receiver (Transit or Hosting CSE), omitting any leading / .

- “req” is a literal string identifying this as a request.

- <type> is “xml” or “json” which indicates the MQTT payload data type in clause 6.5.4.

The payload of the MQTT PUBLISH packet is used to carry the request primitive, as described in clause 6.5.

### -----------------------Start of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 6.5.4	Content-type

A MQTT message payload contains oneM2M request or reponse primitives which are serialized by XML or JSON encoding given in clause 8 of [3].

When a MQTT client publishes a message, it shall use a Topic name to indicate the format of the payload included in a PUBLISH message. As defined in clause 8 of [3], the payload of request or response message shall include oneM2M primitives serilaized using XML or JSON.

The Topic name takes this form:

- /oneM2M/req/<originator>/<receiver>/xml or /oneM2M/req/<originator>/<receiver>/json

- /oneM2M/resp/<originator>/<receiver>/xml or /oneM2M/resp/<originator>/<receiver>/json

In order to receive PUBLISH message with the Topic name, each MQTT client shall subscribe to the Topic name as follows:

- /oneM2M/req/+/<receiver>/#

- /oneM2M/resp/<originator>/#

### -----------------------End of change 2---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?