| CHANGE REQUEST |
| --- |
| Meeting:* | PRO 17.0 |
| Source:* | KT Corp. (TTA) |
| Date:* | 2015-05-21 |
| Contact:* | Francisco Sang-Eon Kim (kim.sangeon@kt.com) |
| Reason for Change/s:* | Descriptioin to clearly understand for Generic procedure of Originator at section 7.1.2.1 |
| CR against: Release* | Release 1 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004-V1.1.0 |
| Clauses/Sub Clauses* | 7.1.2.1 Generic resource request procedure for originator |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution proposes to discriminate primitive, parameters of primitive and <resource> for generic procedures.

The rationale is that TS shall describe to clearly understand generic procedure, because current description has a little bit confusion e.g. “Communication Method?”, implicit parameters.

A bold types indicate primitives delimited with '“' and '”' e.g. “Request” and “Response”.

An italic types indicate parameters of primitives delimited with '“' and '”' e.g. “To”, “From”, “Operation”, “Response Type”, “Content”, etc.

A string containing resource type name delimited with '<' and '>' e.g. <resourceType> is used as an  abbreviation referring to the type of a resource. For example the text "a <container> resource" could be used as an abbreviation for "a resource of type container".

The Orig-1.0 and Orig-2.0 are used  “Request” primitive for clarification.

The Orig-3.0 is used  “Response” primitive for clarification.

At Orig-4.0, an originator needs to decide “communication method” for which the “Response Type” parameter is used.

In case of ‘blockingRequest’ based on section 6.3.3.2.6 m2m:responseType, Orig-6.0 process “Response” primitive.

When a value of “Response Type” is nonBlockingRequestSynch, all exchange of information between Originator and Receiver CSE needs to be initiated by the Originator [section 8.2.2.2 in TS-0001]. Therefore, the Originator should send “Request” primitive at Orig-5.0. Operation parameter of “Request” primitive is RETRIEVE and Content parameter is <request> resource according to the 7.2.1.4.

Content parameter is optional for RETRIEVE operation as specified at section 8.1.2 in TS0001 v1.8.0.

After that, originator receives “Response” primitive from the Receiver CSE at Orig-5.1. The value of content parameter of the “Response” primitive is attributes and child resources of <request> resource.

At Orig-5.2, Originator checks whether the complete ot not based on operationResult attribute in <Request> resource for “Request” primitive which sent at Orig2-0. If the “Request” primitive is not completed at Receiver, the Originator retry Orig-5.0 later. Otherwise, when the “Request” primitive is completed at Receiver, the Originator process the results at Orig-6.0.

When a value of “Response Type” is nonBlockingRequestAsynch, Originator or other entities that need to know about the outcome of a “Request” are able to receive notification messages [section 8.2.2.2 in TS-0001].

Therefore, the Receiver should send “Request” primitive to the Origniator at Orig-7.0 when the Receiver completed processing. Operation parameter of “Request” primitive is NOTIFY and Create a “Response” primitive with “operation”=NOTIFY parameter at Orig-8.0

nonBlockingRequestAsync reviewed by Josef

nonBlockingRequestSync reviewed by Seungmyeong and Shingo

### -----------------------Start of change 1-------------------------------------------

#### Generic resource request procedure for originator

A generic resource Request procedure shall be comprised of the following actions. Additional actions specific to individual procedures are listed in the respective sections by referencing these actions and providing additional steps. The Originator shall execute the following steps in order:

Figure 7.1.2.1-1: Generic procedure of Originator

Orig-1.0 Compose “Request” primitive: Please refer to clause 7.2.1.1 for details.

Orig-2.0 Send a “Request” to the Receiver CSE: Please refer to clause 7.2.1.2 for details.

Orig-3.0 Wait for “Response” primitive: Please refer to clause 7.2.1.3 for details.

Orig-4.0 “Response Type” parameter: This step shall be operated after getting the Response primitive from step Oring-3.0 “Wait for Response primitive”. In this step, the Originator checks communication method whether the request was blockingRequest, nonBlockingRequestSynch or nonBlockingRequestAsynch by using Response Type parameter (see detail in clause 8.1.2 in the oneM2M TS-0001 Functional Architecture [6]).

If the Response Type was blockingRequest it goes to step Orig-6.0 “Process Response”. If the request was nonBlockingRequestSync, it goes to step Orig-5.0 “Retrieve result from the <request> resource”. If the request was nonBlockingRequestAsynch, it goes to step Orig-7.0 “Receive Notification”.

Orig-5.0 Send a “Request” primitive with “Operation”=RETRIEVE parameter: See clause 7.2.1.4 for details.

Orig-5.1 Receive a “Response” primitive from the Hosting CSE.

Orig-5.2 Check completion of operation by “Response Status Code” parameter. If the operation is completed, it goes to Orig-5.3. If the operation is not completed, it goes to Orig-5.0.

Orig-5.3 Process a “Response” primitive embedded inside “Content” parameter of the received “Response” primitive of Orig-5.1

Orig-6.0 Process “Response” primitive: the Originator processes the response.

Orig-7.0 Receive “Request” primitive with “operation”=NOTIFY parameter and a “Content” Parameter that contains a serialization of a “Response” primitive with a “Request Identifier” inside the embedded “Response” primitive that matches with the “Request Identifier” originally sent in Orig-2.0: the Originator processes the notification.

Orig-8.0 Create a “Response” primitive with same “Request Identifier” of  Orig-7.0 : Please refer to clause 7.2.2.2 for details.

Orig-9.0 Send “Response” primitive: Please refer to clause 7.2.2.3 for details..

Orig-9.1 Process a “Response” primitive embedded inside “Content” parameter of the received “Request” primitive of Orig-7.0

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Text boxes

Figure 7.1.2.1-1: Generic procedure of Originator

Orig-1.0: “Compose Request primitive”

Orig-2.0: “Send a Request to the Receiver CSE”

Orig-3.0: “Wait for Response primitive”

Orig-4.0: “Communication Method?”

Orig-6.0: Process Response

Orig-5.0: “Retrieve result from <request> resource”

blockingRequest

Start

Finish

nonBlockingRequestSynch

nonBlockingRequestAsynch

Orig-7.0: “Receive Notification”

Orig-8.0: “Create a Response”

Orig-9.0: “Send Response primitive”