| CHANGE REQUEST |
| --- |
| Meeting:* | PRO#17 |
| Source:* | SeungMyeong JEONG (seungmyeong.jeong@lge.com) |
| Date:* | 2015-05-11 |
| Contact:* | SeungMyeong JEONG (seungmyeong.jeong@lge.com) |
| Reason for Change/s:* | See the introduction. |
| CR against: Release* | Rel-1 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0010 v.1.1.0 |
| Clauses/Sub Clauses* | 6.4.3 6.4.4 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

From the Functional Architecture TS(TS-0001), the Originator and the Reciever of the response is the Reciever and the Originator of the request, respectively. In other words, Originator of the request is the Receiver of the corresponding response.

However, in the MQTT binding TS, in the response topic naming rule, the Originator and the Reciever of the response is the Originator and the Receiver of the request, respectively. This may be confusing for readers.

For the moment, to make the minimum change as MNT, this CR proposes to clarify this point in the <originator> and <receiver> descriptions in the MQTT topic. More discussion would be needed on this issue.

## ----------------------- Start of change 1 -----------------------

### 6.4.3 Listening for and responding to a Request

A Receiver listens for requests arriving via MQTT by subscribing to its Topics using a wildcarded topic filter of the following form

- /oneM2M/req/+/<receiver>

- “oneM2M” is a literal string identifying the topic as being used by oneM2M

- + is a wildcard which matches any Originator

- <receiver> is the  SP-relative-CSE-ID of the Receiver  (Transit or Hosting CSE), omitting any leading / .

- “req” is a literal string identifying this as a request.

When it receives a request, the Receiver shall perform the Core Transport operations associated with the request, including any access control policy checks. In particular it shall check the request expiration timestamp (if any) contained in the request, since it is possible that that time might have passed while the message was being stored by MQTT.

It transmits a response by sending an MQTT PUBLISH packet to a response topic. This takes the form:

- /oneM2M/resp/<originator>/<receiver>

"oneM2M" is a literal string identifying the topic as being used by oneM2M.

<receiver> is the SP-relative-CSE-ID of the Receiver  (Transit or Hosting CSE) specified in the corresponding request, omitting any leading / .

<originator> is the SP-relative-AE-ID or SP-relative-CSE-ID of the Originator specified in the corresponding request, omitting any leading / . In the AE-ID case, any / characters embedded in the ID shall be replaced with : characters.

"resp" is a literal string identifying this as a response.

The Originator shall subscribe to this Topic (either explicitly or using a wildcarded filter) in order to see the response.

The payload of the MQTT PUBLISH packet is used to carry the response primitive, as described in clause 6.5.

### Initial Registration

In some security scenarios, an Originator might not initially know its AE-ID or CSE-ID. Initial registration exchanges can use the communication pattern described in clauses 6.4.1 and 6.4.2 except that they use Topics containg a credential ID rather than an AE-ID or CSE-ID, as follows:

- /oneM2M/reg_req/<originator>/<receiver>

- “oneM2M” is a literal string identifying the topic as being used by oneM2M

- <originator> is the Credential-ID. Any / characters embedded in the ID shall be replaced with : characters.

- <receiver> is the  SP-relative-CSE-ID of the Receiver  (Transit or Hosting CSE) specified in the corresponding request, omitting any leading / .

- “reg_req” is a literal string identifying them as registration requests and responses.

and

- /oneM2M/reg_resp/<originator>/<receiver>

- “oneM2M” is a literal string identifying the topic as being used by oneM2M

- <originator> is the Credential-ID of the Originator specified in the corresponding request. Any / characters embedded in the ID shall be replaced with : characters.

- <receiver> is the  SP-relative-CSE-ID of the Receiver  (Transit or Hosting CSE) specified in the corresponding request, omitting any leading / .

- “reg_resp” is a literal string identifying them as registration requests and responses.

## ----------------------- End of change 1 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?