| CHANGE REQUEST |
| --- |
| Meeting:* | PRO17.2 |
| Source:* | FUJITSU |
| Date:* | 2015-06-16 |
| Contact:* | Shingo Fujimoto, FUJITSU, shingo_fujimoto@jp.fujitsu.com |
| Reason for Change/s:* | Add introduction part of WebSocket TS |
| CR against: Release* | Release 2 |
| CR against: WI* | Active WI-0040 MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0020 V.0.1.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

<Provide an introduction containing the problem(s) being solved, and a summary list of proposals>

### -----------------------Start of change 1-------------------------------------------

## 3.1	Definitions

oneM2M WebSocket Client: An AE or a CSE which establish the communication channel over WebSocket.

oneM2M WebSocket Server: A CSE which accepts the request to establish the communication channel over WebSocket.

Upper WebSocket Server: An oneM2M WebSocket Server which is closer to the IN-CSE on the CSE topology.

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

# 5.	WebSocket Protocol Binding

Present clause describes the protocol binding specification to use WebSocket protocol for transport of oneM2M Protocol.

## 5.1. Introduction

The WebSocket protocol enables to establish two-way communication channel from the client to the server no matter if there is a firewall or NAT between them.

The establishing WebSocket communication channel is requested by upgrading an ordinary HTTP request following RFC6455([1]).

AE or CSE shall request to Register as first request to Upper WebSocket Server, and they shall not send further message until the Registration request was returned successfully.

Once Registration procedure was performed successfully, AE or CSE may send non-registration requests and responses bidirectionaly.

When the WebSocket connection is disconnected, the Upper WebSocket Server shall performe un-regstration procedure for the WebSocket Client.

Those procedures are illustration in Figure-X.

Figure 5.1-1: Communication flow of WebSocket binding

### 5.2. oneM2M primitive mapping

The oneM2M primitive request and response message shall be mapped to  "data frame" (e.g. non-control frame) in WebSocket protocol.

When the value of response Type primitive parameter was  'blockingRequest(3)', the request shall be handled as 'nonBlockingSyncRequest'.

### The default serialization format of oneM2M primitive message shall be "JSON serialized primitive message" which is sepecified in TS-0004.

### 5.3. Registration procedure

### (TBD)

### 5.4. Sending Non-Registration Request

### (TBD)

### 5.5. Handling Non-Registartion Request

### (TBD)

### 6. Examples

### The present clause illustrates the example call flow for WebSocket protocol binding.

### (TBD)

### -----------------------End of change 2---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?