| CHANGE REQUEST |
| --- |
| Meeting:* | PRO 17.0 |
| Source:* | KT Corp. (TTA) |
| Date:* | 2015-05-10 |
| Contact:* | Francisco Sang-Eon Kim (kim.sangeon@kt.com) |
| Reason for Change/s:* | Descriptioin to clearly understand for Generic procedure of Receiver at section 7.1.2.2 |
| CR against: Release* | Release 1 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004-V1.1.0 |
| Clauses/Sub Clauses* | 7.1.2.2 Generic response procedure for receiver |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution proposes to discriminate primitive, parameters of primitive and <resource> for generic procedures.

The rationale is that TS shall describe to clearly understand generic procedure, because current description has a little bit confusion e.g. “Communication Method?”, implicit parameters. Secondly, Recv-2.0 and Recv-6.6.1 is duplicated. A check for “CommunicationMethod” doest not required to double check at Receiver.

A bold types indicate primitives delimited with '“' and '”' e.g. “Request” and “Response”.

An italic types indicate parameters of primitives delimited with '“' and '”' e.g. “To”, “From”, “Operation”, “Response Type”, “Content”, etc.

A string containing resource type name delimited with '<' and '>' e.g. <resourceType> is used as an  abbreviation referring to the type of a resource. For example the text "a <container> resource" could be used as an abbreviation for "a resource of type container".

“Request” and “Response”  primitive are used at Recv-1.0, Recv-4.0, Recv-5.0, Recv-6.7, Recv-6.8, Recv-6.10, Recv-7.0, Recv-7.1, Recv-7.2 Recv-7.0, Recv-8.0 and Recv-9.0 for clarification.

Recv-6.1 should check at first rather than after check communication check (Recv-2.0). Recv-2.0 at Figure 7.1.2.2-1 is not reasonable, because it should be performed at the right Receiver. If the receiver is not correct “To” parameter, it should be forward to the right receiver which is indicated by “To” parameter. That is why I propose to Recv-6.1 after Recv-1.0.

Recv-6.9, Recv-6.10 and  Recv-6.11 are basically same as in Figure 7.1.2.2-2.

At Recv-2.0, a receiver decides “communication method” by “Response Type” parameter.

In case of ‘blockingRequest’ based on section 6.3.3.2.6 m2m:responseType, Recv-6.0 processes ‘Resource handling procedure’ which has a step Recv-6.0.1, Recv-6.0.2, Recv-6.2, Recv-6.3, Recv-6.4, Recv-6.5, Recv-6.6, Recv-6.7 and Recv-6.8.

The resource handling procedure is basically same as in Figure 7.1.2.2-2 except for destination check and communication check.

The destination check is already performed at Recv-6.1 at this contribution. The check for communication method is already performed at Recv-2.0.

When a value of “Response Type” is nonBlockingRequestSynch, all exchange of information between Originator and Receiver CSE needs to be initiated by the Originator [section 8.2.2.2 in TS-0001].

Recv-3.0, Recv-4.0, Recv-5.0, Recv-6.0 and Recv-7.0 are basicallysame as in Figure 7.1.2.2-1.

When a value of “Response Type” is nonBlockingRequestAsynch, Originator or other entities that need to know about the outcome of a “Request” are able to receive notification messages [section 8.2.2.2 in TS-0001].

Recv-3.0, Recv-4.0, Recv-5.0, Recv-6.0 Recv-7.0, Recv-8.0 and Recv-9.0 are basicallysame as in Figure 7.1.2.2-1.

### -----------------------Start of change 1-------------------------------------------

#### Generic response procedure for receiver

The Receiver shall execute the following steps in order. In case of error in any of the steps below, the Receiver shall execute "Create an error response" (refer to clause 7.2.3.12 for details) and then "Send Response primitive" (refer to clause 7.2.2.4for details). The corresponding Response code shall be included in the Response primitive.

Figure 7.1.2.2-1: Generic procedure of Receiver

Recv-1.0 Check the validity of received “Request” primitive: See clause 7.2.2.1 for details.

Recv-6.1 Hosting CSE of the targeted CSE at “To” parameter: The step checks if the receiver is a transit CSE or the Hosting CSE of the received Request by examining the To parameter of the Request primitive. If the receiver hosts the resource that the address in the To parameter represents, the receiver is the Hosting CSE (goes to Recv-2.0 “Response Type parameter”, Yes branch). Otherwise, the receiver is the Transit CSE (goes to Recv-6.9 “Queue request primitive and execute CMDH message forwarding procedure”, No branch).

Recv-2.0 “Response Type” parameter: The Receiver CSE checks whether a received request is blockingRequest, nonBlockingRequestSynch or nonBlockingRequestAsynch by using Response Type parameter (see detail in clause 8.1.2 in TS-0001 Functional Architecture [6]). If the request is blockingRequest or Response Type parameter is not included, it goes to step Recv-6.0 “Resource handling procedure”. If the request is nonBlockingRequestSynch, it goes to step Recv-3.0 “Create <request> resource locally”  If the request is nonBlockingRequestAsynch, it goes to step Recv-3.0 “Create <request> resource locally”.

Recv-3.0 Create <resource>  locally: Please refer to clause 7.2.2.2 for details.

Recv-4.0 Create acknowledgement “Response” primitive with “Response Code”=1000 parameter: Please refer to clause 7.2.2.2 for details.

Recv-5.0 Send “Response” primitive: Please refer to clause 7.2.2.4 for details.

Recv-6.0 Resource handling procedure: Please refer to Figure 7.1.2.2-2for details.

Recv-7.0 Update “Request” primitive: Please refer to clause 7.2.2.5 for details. This step is only valid when the request is non-blocking.

Recv-8.0 Send “Request” primitive of “operation”=NOTIFY: Please refer to clause 7.4.1.2.4 for details.

Recv-9.0 Wait for a “Response” primitive: Please refer to clause 7.2.1.3 for details.

Recv-6.0.1 Originator is AE and “operation” is CREATE parameter: The step checks if the receiver is Registrar CSE, the Originator is AE, and operation is create. If the receiver is Registrar CSE and Originator is an AE, goes to Recv-6.0.2 Check <serviceSubscriptionProfile> resource. Otherwise, goes to Recv-6.1.

Recv-6.0.2 Check <serviceSubscriptionProfile> resource: Please refer to clause 7.2.2.7 for details.

Recv-6.2 Check existence of the addressed <resource>: Please refer to clause 7.2.3.1 for details.

Recv-6.3 Check accessColtrilPolicyIDs attribute of the Originator”: Please refer to clause 7.2.3.14 for details.

Recv-6.4 Check validity of resource representation for the given <resource> type: Please refer to clause 7.2.3.2 and clause 7.2.3.3 for details. Notify is not applicable for this step.

Recv-6.5 “operation”=CREATE|UPDATE|RETRIEVE|DELETE|NOTIFY is performed: The step represents five common operations which are “Create the resource (clause 7.2.3.4)”, “Retrieve the resource (clause 7.2.3.5)”, “Update the resource (clause 7.2.3.6)”, “Delete the resource (clause 7.2.3.7)” and “Notify re-targeting (clause 7.2.3.8)”. Notify re-targeting is performed for the Create, Update, Retrieve, Delete, or Notify operation respectively.

Recv-6.6 Announce|De-announce the <resource>: The step represents two common operations which are “Announce the resource” and “De-announce the resource”. Please refer to clause 7.2.3.9 and clause 7.2.3.10 for details. Notify is not applicable for this step.

Recv-6.7 Create successful “Response” primitive: Please refer to clause 7.2.3.11 for details.

Recv-6.8 Send “Response” primitive: Please refer to clause 7.2.2.4 for details. If the Receiver is Hosting CSE, after this step, the procedure is terminated.

Recv-6.9 CMDH processing supported?: This step checks whether the Receiver supports the CMDH processing.

Recv-6.10 Queue “Request” primitive and execute CMDH message forwarding procedure: If CMDH message is supported, the Receiver CSE shall queue the received request primitive and execute the “CMDH message forwarding procedure”. Please refer to Annex H.2.4. for details.

Recv-6.11 Forwarding: If CMDH processing is not supported, carry out message forwarding as defined in clause 7.2.2.6.

### -----------------------End of change 1---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?

# Text boxes

Recv-1.0: “Check the validity of received request primitive”

Recv-2.0: Communication method?

Recv-6.0: Resource handling procedures

Recv-3.0: “Create <request> resource locally”

Recv-4.0: “Create a success Response”

Recv-5.0: “Send Response primitive”

nonBlockingRequestAsynch

nonBlockingRequestSynch

Recv-6.0: Resource handling procedures

Recv-7.0: “Update <request> resource”

Finish

Start

Recv-3.0: “Create <request> resource locally”

Recv-4.0: “Create a success Response”

Recv-5.0: “Send Response primitive”

Recv-6.0: Resource handling procedures

Recv-7.0: “Update <request> resource”

Recv-8.0: “Send Notification”

Recv-9.0: “Wait for Response primitive”

blockingRequest

Recv-6.10: “Queue request primitive and execute CMDH message forwarding procedure”

Recv-6.1: Hosting CSE of the targeted resource?

Start

Recv-6.3: “Check authorization of the Originator”

Recv-6.4: “Check validity of resource representation for the given resource type”

Recv-6.2: “Check existence of the addressed resource”

Recv-6.5: “Create/Update/Retrieve/Delete/Notify operation is performed”

Recv-6.6: “Announce/De-announce the resource”

Finish

Yes

No

Recv-6.7: “Create a success response”

Recv-6.8: “Send Response Primitive”

Recv-6.9: CMDH processing supported?

Recv-6.11: “Forwarding”

No

Yes

Recv-6.0.1: Receiver is Registrar CSE & Originator is AE & operation is create

Recv-6.0.2: “Check Service Subscription Profile”

Yes

No

Recv-6.6.1: “Communication Method?”

Else

blockingRequest