| CHANGE REQUEST |
| --- |
| Meeting:* | PRO #18 |
| Source:* | Seongyoon Kim, LG Electronics, seongyoon.kim@lge.com SeungMyeong JEONG, LG Electronics, seungmyeong.jeong@lge.com Dongtaek Lee, LG Electronics, dongtaek.lee@lge.com Francisco, Sang-Eon Kim, kim.sangeon@kt.com |
| Date:* | 2015-07-21 |
| Contact:* | Seongyoon Kim, LG Electronics, seongyoon.kim@lge.com |
| Reason for Change/s:* | Correction |
| CR against: Release* | Release 1 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0009 V1.1.0 |
| Clauses/Sub Clauses* | 6.2.1 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

There is no way to distingush oneM2M request from receiver when HTTP method is POST.

- POST with “Resource Type” ( Create

- POST ( Notify (?)

- POST ( Partial Update (?)

This contribution proposes to map HTTP PUT to oneM2M Update operation regardless of whether that operation is partial or full update.

R01:

This contribution is regarded as MNT for release 1 due to the following aspects.

- Create, partial update, and notify operation are mapped to HTTP POST method. Create operation is easily distinguishable due to existence of resource type parameter. The only difference of partial update and notify HTTP message is the content type of HTTP body. However, since Transit CSE doesn’t even validate resource representation (doesn’t see inside of HTTP body), if Transit CSE converts HTTP to another protocol (e.g., MQTT, CoAP), Transit CSE can’t distingush between partial update and notify operation.

- HTTP and CoAP have an inconsistency on the operation mapping (HTTP: partial update ( POST, CoAP: partial update ( PUT).

### -----------------------Start of change 1-------------------------------------------

## 6.2	Parameter Mappings on Request-Line

### 6.2.1	Method

The HTTP 'Method' shall be derived from the Operation request primitive parameter of the request primitive.

Table 6.2.1-1: HTTP Method Mapping

| oneM2M Operation | HTTP Method |
| --- | --- |
| Create | POST |
| Retrieve | GET |
| Update | PUT |
| Delete | DELETE |
| Notify | POST |

At the Receiver, an HTTP request message with POST method shall be mapped to a oneM2M Create or Notify Operation parameter in accordance with the existence of Resource Type parameter. If Resource Type parameter exists in a HTTP request message with POST method, the value of Operation parameter is Create and if Resource Type parameter doesn’t exist, the value of Operation parameter is Notify.

### -----------------------End of change 1-------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?