| CHANGE REQUEST |
| --- |
| Meeting:* | PRO#18 |
| Source:* | Qualcomm Inc. (TIA) |
| Date:* | 2015-07-21 |
| Contact:* | Nobu Uchida, Qualcomm, nuchida@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com |
| Reason for Change/s:* | XSD name for Content primitive parameter |
| CR against: Release* | R2 |
| CR against: WI* | Active – WI-0009 (PRO) MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | oneM2M-TS-0004-v2.0.0 |
| Clauses/Sub Clauses* | 7.4.2, 8.1.1 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

At TP#17, PRO-2015-0758R03-CR_for_TS-0004_ShortNames was agreed which has reassigned some names of resource attributes, request parameters and of elements of complex data types in order to allow a one-to-one mapping correspondence between short and long names.

PRO-2015-0758R03 proposed to change the XML element name used for the Content primitive parameter, from ‘content’ to ‘primitiveContent’.

However, when implementing this name change in CDT-requestPrimitive-v1_2_0.xsd and CDT-responsePrimitive-v1_2_0.xsd the question came up whether or not the changes shown in PRO-2015-0758R03 really justify this name change since none of the data types given that this change is not reflected in a change of any data type shown in clause 6.3 of TS-0004.

The reason is that data types for resources and primitives are defined anonymously and therefore do not appear in clause 6.3 of TS-0004 but instead show up in tables of clauses 7.1 (primitives) and 7.3 (resource types) that specify the data types to be used for the primitive parameters and resource attributes.

However in order to clarify the relation between primitive parameters and their corresponding names in the XML  representations, especially for the Content primitive parameter,  this CR proposes some additional text changes to clauses 7.1.1 (Primitive format) and 7.4.2 (Elements contained in the primitive Content), and 8 (Representation of primitives in data transfer)

Changes in R01 relative to the initial version:

- removed proposed changes to clause 7.1.1 (i.e. change 1 in the initial version has been removed)

- in clause 8.1, only the correction of the short name “rqp” for requestPrimitive has been kept

### -----------------------Start of change 1---------------------------------------------

### Elements contained in the Content primitive  parameter

Clauses 7.1.1.1 and 7.1.1.2 enumerate the forms that the Content primitive parameter takes in various Request and Response cases. Note that the Content primitive parameter is denoted as primitiveContent in both, CDT-requestPrimitive-v1_2_0.xsd and CDT-responsePrimitive-v1_2_0.xsd.

This clause details the Objects (elements) used in some of these cases. in the tables below.

The following elements are defined for use in the content parameter of a request:

Table 7.4.2-1: Elements used for request content

| Element Name | Applicable Operations | Data Type | Defined in |
| --- | --- | --- | --- |
| m2m:notification | N | m2m:notification | CDT-notification-v1_0_0.xsd |
| m2m:aggregatedNotification | N | m2m:aggregatedNotification | CDT-notification-v1_0_0.xsd |
| m2m:attributeList | R | m2m:attributeList | CDT-requestPrimitive-v1_0_0.xsd |
| m2m:responsePrimitive | N | m2m:responsePrimitive | CDT-responsePrimitive-v1_0_0.xsd |

The following elements are defined for use in the content parameter of a response:

Table 7.4.2-2: Elements used for response content

| Element Name | Applicable Operations | Data Type | Element is Defined in |
| --- | --- | --- | --- |
| m2m:resource | C R U | m2m:resourceWrapper | CDT-responsePrimitive-v1_0_0.xsd |
| m2m:URIList | R | m2m:listOfURIs | CDT-responsePrimitive-v1_0_0.xsd |
| m2m:aggregatedResponse | C R U D | m2m:aggregatedResponse | CDT-responsePrimitive-v1_0_0.xsd |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2---------------------------------------------

### Examples

An example that shows a request primitive serialized into an XML document is shown below. This example shows the create request for an instance of a <contentInstance> resource. Only mandatory primitive parameters and resource attributes are shown.

<?xml version="1.0" encoding="UTF-8"?>
<m2m:rqp xmlns:m2m="http://www.onem2m.org/xml/protocols"
 xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance"
 xsi:schemaLocation="http://www.onem2m.org/xml/protocols CDT-requestPrimitive-v1_0_0.xsd">
    <op>1</op>
    <to>//cse1.mym2msp.org/</to>
    <fr>/cse1234/app567</fr>
    <ri>0002bf63</ri>
    <ty>4</ty>
    <pc>
        <cin rn="temp754">
            <cnf>application/xml:1</cnf>
            <con>PHRpbWU+MTc4ODkzMDk8L3RpbWU+PHRlbXA+MjA8L3RlbXA+DQo=</con>
        </cin>
    </pc>
</m2m:rqp>

The XML elements have the following meaning:

- rqp:  Root element of the Request primitive, which includes a reference to an XSD file which defines its datatype.

- op: 	Operation parameter of datatype m2m:operation:  in this example value = 1 indicates a “Create” operation.

- to: 	To parameter of type m2m:anyURI: URI of the target resource.

- fr: 	From parameter of type m2m:ID: ID of the Originator (either AE-ID or CSE-ID).

- ri: 	Request Identifier parameter of type m2m:requestID: this could e.g. represent a counter number.

- ty: 	Resource Type parameter of datatype m2m:resourceType: indicating type of the resource to be created (value = 4 indicates that a <contentInstance> resource shall be created).

- pc: 	Content parameter of datatype m2m:primitiveContent: the attributes of the resource to be provided by the Originator.

- cin:  Root element of the <contentInstance> resource of datatype m2m:contentInstance: this includes the mandatory attributes  (and optional attributes not shown in this example) supplied by the request Originator. The instance name is given in the XML name attribute, here rn="temp754". In this example, the cn parameter includes an instance of a <contentInstance> resource which consists of two attributes: contentInfo (cnf) – which specifies base64 encoding - and the content (con) itself.

### -----------------------End of change 2---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?