| CHANGE REQUEST |
| --- |
| Meeting:* | < e.g. PRO 1> |
| Source:* | FUJITSU |
| Date:* | 2015-12-06 |
| Contact:* | Shingo Fujimoto,FUJITSU,shingo_fujimoto@jp.fujitsu.com |
| Reason for Change/s:* | <exact change/s to be provided below> |
| CR against: Release* | Release-2 |
| CR against: WI* | Active WI-0030: WebSocket Binding MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | <TS/TR number> and <Version Number> |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR proposed communication channel handling procedures for WebSocket binding.

### -----------------------Start of change 1-------------------------------------------

## 5.2 Establishing communication channel with WebSocket

The AE or MN-CSE with WebSocket binding shall establish communication channel when it need to communicate with the Registrar CSE or other CSE. Establishing communication channel is achieved by performing 'opening handshake' procedures described in IETF RFC6455[1], which requests a GET request to the poA address of the targeted CSE, and upgrading the HTTP connection to the WebSocket connection. Even MN-CSE does not have to provide WebSocket Server capability, when its Registrar CSE can buffer incoming requests while the communication channel is temporary closed.

During handshake procedure, the WebSocke Sub Protocol name  ‘oneM2M-pro-1’ shall be selected and returned in ‘Sec-WebSocket-Protocol-Client’ header.

Editor:s Note: Sub protocol name should be registered to IANA registry.

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

## 5.3 Registration procedure

After WebSocket Connection is established, the Originator shall request CREATE operation (first time), or UPDATE operation of the <AE> or <remoteCSE> as the Registration procedure which is described in TS-0004. Once the first Registration procedure is successfully completed, the Registrar CSE shall provide internal buffer for incoming oneM2M primitive messages to the the AE or CSE (i.e. WebSocket Client), and the buffered shall be enabled when the Registrar detected the communication channel is temporary closed. When the <AE> or <remoteCSE> is updated by the WebSocket Client and some incoming messages destinated to the WebSocket Client are buffered, the buffered messages are forwarded to the WebSocket Client immediately.

### -----------------------End of change 2---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?