| CHANGE REQUEST |
| --- |
| Meeting:* | PRO#21 |
| Source:* | Huawei Technologies Co., Ltd. |
| Date:* | 2016-1-8 |
| Contact:* | Jiaxin Yin, yinjiaxin@huawei.com Yongjing Zhang, zhangyongjing@huawei.com |
| Reason for Change/s:* | The stage 3 procedure definition of how the Group Hosting CSE handles the group responses. |
| CR against: Release* | Release Two |
| CR against: WI* | Active WI-0031 MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 v2.3.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The CR is to define procedures for Group Hosting CSE to aggregate and respond member responses to the Originators pertaining to a request that is fanned out by the Group Hosting CSE.

### -----------------------Start of change 1-------------------------------------------

7.4.14.2.5	Aggregate member responses

The group hosting CSE shall aggregate the Responses after receiving responses from its member resources and sub-groups and aggregate the Responses into a single Response:

Depend on the Response Type parameter, the group hosting CSE shall:

blockingRequest: Before the Result Expiration Time, aggregate and respond the member responses to the Originator. And discard the remaining member responses.

nonBlockingRequestSynch: Locally create a <request> resource and respond an acknowledgement with the resource id of the created <request> resource. Before the Result Expiration Time, aggregate the member responses and put the aggregated response in the operationResult of the <request> resource. If all member responses has been aggregated, set the requestStatus of the <request> resource to COMPLETED. If only part of the member responses has been aggregated, set the requestStatus of the <request> resource to PARTIALLY_COMPLETED. Then within the time period of Result Persistence, continue aggregating the remaining member responses and updating the operationResult correspondingly.

nonBlockingRequestAsynch: Respond an acknowledgement with resource id of a <request> resource if the <request> resource type is supported by the group Hosting CSE. Before the Result Expiration Time, aggregate the member responses and notify the Originator with the aggregated response. Then within the time period of Result Persistence, continue aggregating and notify the Originator with the remaining member responses. There may be multiple notifications generated by the Group Hosting CSE according to local policies. The notifications may not include the same member response. If <request> resource type is supported by the Group Hosting CSE, the created <request> resource is updated following the procedure defined in nonBlockingRequestSynch bullet.

flexBlocking: If all member responses have been aggregated before Result Expiration Time, respond directly with the aggregated response following the blocking way. Otherwise non-blocking method shall be used. If <request> resource type is supported by the Group Hosting CSE,  locally create a <request> resource, set the requestStatus attribute of the <request> resource to PARTIALLY_COMPLETED,  set the operationResult with the currently aggregated member responses and respond an acknowledgement with the resource id the <request> resource as well as the currently aggregated member responses. Within the time period of Result Persistance, the Group Hosting CSE shall continue aggregating the remaining member responses and update the operationResult of the <request> resource. If notification targets are provided, the Group Hosting CSE shall notify the target addresses with the aggregated member responses. Within the time period of  Result Persistance, continue aggregating and notifying the notification targets with the member responses.

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

##### Create

The primitives create the content of all member resources belonging to an existing <group> resource.

Originator:

Primitive specific operation after Orig-1.0 "Compose Request primitive" and before Orig-2.0 "Send the Request to the receiver CSE": In the case the Originator wants to subscribe to all the member resources of the group and the originator wants the group hosting CSE to aggregate all the notifications come from its member hosting CSEs, the Originator shall include notificationForwardingURI attribute in the <subscription> resource.

Receiver:

Primitive specific operation after Recv-6.2 "Check existence of the addressed resource" and before Recv-6.3 "Check authorization of the Originator": The to parameter consists of the URI of the group resource plus a suffix marked by /fanOutPoint or /fanOutPoint/.....

Primitive specific operation additional to Recv-6.3 "Check authorization of the Originator": The Group Hosting CSE shall check the authorization of the Originator based on the membersAccessControlPolicyIDs of the parent <group> resource. In the case the membersAccessControlPolicyIDs is not provided, the accessControlPolicyIDs of the parent <group> resource shall be used.

Primitive specific operation to replace Recv-6.5"Create/Update/Retrieve/Delete/Notify operation is performed" and Recv-6.6"Announce/De-announce the resource" in the generic procedure:

- Validate the member types, refer to clause 7.4.14.2.1.

Sub-group creation for members residing on the same CSE, refer to clause 7.4.14.2.2.

Assign URI for aggregation of notification, refer to clause 7.4.14.2.3.

Fanout Request to each member, refer to clause 7.4.14.2.4.

Aggregate member responses, refer to clause 7.4.14.2.5.

##### Retrieve

The primitives retrieve the content of all <member> resources belonging to an existing <group> resource.

Originator:

No primitive specific operations.

Receiver:

Primitive specific operation after Recv-6.2 "Check existence of the addressed resource" and before Recv-6.3 "Check authorization of the Originator": The To parameter consists of the URI of the <group> resource plus a suffix marked by /fanOutPoint or /fanOutPoint/.....

Primitive specific operation additional to Recv-6.3 "Check authorization of the Originator": The Group Hosting CSE shall check the authorization of the Originator based on the membersAccessControlPolicyIDs of the parent group resource. In the case the membersAccessControlPolicyIDs is not provided, the accessControlPolicyIDs of the parent group resource shall be used.

Primitive specific operation to replace Recv-6.5"Create/Update/Retrieve/Delete/Notify operation is performed" and Recv-6.6 "Announce/De-announce the resource" in the generic procedure:

- Sub-group creation for members residing on the same CSE, refer to 7.4.14.2.2.

- Fanout Request to each member, refer to 7.4.14.2.4.

- Aggregate member responses, refer to clause 7.4.14.2.5.

##### Update

The primitives update the content of all member resources belonging to an existing <group> resource.

Originator:

No primitive specific operations.

Receiver:

Primitive specific operation after Recv-6.2 "Check existence of the addressed resource" and before Recv-6.3 "Check authorization of the Originator": The To parameter consists of the URI of the <group> resource plus a suffix marked by /fanOutPoint or /fanOutPoint/.....

Primitive specific operation additional to Recv-6.3 "Check authorization of the Originator": The Group Hosting CSE shall check the authorization of the Originator based on the membersAccessControlPolicyIDs of the parent group resource. In the case the membersAccessControlPolicyIDs is not provided, the accessControlPolicyIDs of the parent group resource shall be used.

Primitive specific operation to replace Recv-6.5 "Create/Update/Retrieve/Delete/Notify operation is performed" and Recv-6.6"Announce/De-announce the resource" in the generic procedure:

- Validate the member types, refer to 7.4.14.2.1.

- Sub-group creation for members residing on the same CSE , refer to 7.4.14.2.2.

- Fanout Request to each member, refer to 7.4.14.2.4

- Aggregate member responses, refer to 7.4.14.2.5..

##### Delete

The primitives delete the content of all member resources belonging to an existing <group> resource.

Originator:

No primitive specific operations.

Receiver:

Primitive specific operation after Recv-6.2 "Check existence of the addressed resource" and Recv-6.3 "Check authorization of the Originator": The To parameter consists of the URI of the group resource plus a suffix marked by /fanOutPoint or /fanOutPoint/.....

Primitive specific operation additional to Recv-6.3 "Check authorization of the Originator": The Group Hosting CSE shall check the authorization of the Originator based on the membersAccessControlPolicyIDs of the parent group resource. In the case the membersAccessControlPolicyIDs is not provided, the accessControlPolicyIDs of the parent group resource shall be used.

Primitive specific operation to replace Recv-6.5"Create/Update/Retrieve/Delete/Notify operation is performed" and Recv-6.6"Announce/De-announce the resource" in the generic procedure:

- Validate the member types , refer to 7.4.14.2.1.

- Sub-group creation for members residing on the same CSE , refer to 7.4.14.2.2

- Fanout Request to each member. See Clause 7.4.14.2.4

- Aggregate member responses, refer to clause 7.4.14.2.5.

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

##### m2m:requestStatus

Used for requestStatus attribute in <request> resource.

Table 6.3.4.2.10-1: Interpretation of requestStatus

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | COMPLETED |  |
| 2 | FAILED |  |
| 3 | PENDING |  |
| 4 | FORWARDED |  |
| 5 | PARTIALLY_COMPLETED |  |
| NOTE: See clause 7.4.12 "Resource Type request" |

### -----------------------End of change 3---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?