| CHANGE REQUEST |
| --- |
| Meeting:* | PRO#21 |
| Source:* | Huawei Technologies Co., Ltd. |
| Date:* | 2016-1-8 |
| Contact:* | Jiaxin Yin, yinjiaxin@huawei.com Yongjing Zhang, zhangyongjing@huawei.com |
| Reason for Change/s:* | The stage 3 procedure definition of how the Group Hosting CSE handles the group responses. |
| CR against: Release* | Release Two |
| CR against: WI* | Active WI-0031 MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 v2.3.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The CR is to define procedures for Group Hosting CSE to aggregate and respond member responses to the Originators pertaining to a request that is fanned out by the Group Hosting CSE.

Change in R01: some text font change to comply to the oneM2M conventions.

Change in R02: editorial.

Change in R03: rewording  for better clarity.

Change in R04: eidtorial.

Change in R05: additional subclause 7.4.14.2.6 and better clarity.

### -----------------------Start of change 1-------------------------------------------

7.4.14.2.5	Aggregate responses from members

When the group hosting CSE receives responses from its member resources and sub-groups,  it shall aggregate them into one or more Response primitives.

Depending on the Response Type parameter in the original Request, the group hosting CSE shall:

blockingRequest: aggregate any member responses received before Result Expiration Timestamp, and respond to the Originator when all member responses have been received or the Result Expiration Timestamp is reached. Discard any member responses received after Result Expiration Timestamp.

nonBlockingRequestSynch: Locally create a <request> resource, respond with an acknowledgement containing the Resource ID of the created <request> resource, and start aggregating member responses. Before the Result Expiration Timestamp time has been reached, update the <request> resource at least once according to clause 7.4.14.2.6. Continue doing this until the Result Persistence time period has elapsed.

nonBlockingRequestAsynch: Respond with an acknowledgement and start aggregating member responses. Notify the Originator or notification target(s) with the aggregated responses. These member responses may be aggregated into one or more notifications according to the local policy of the group hosting CSE, but at least one notification shall be sent before the Result Expiration Timestamp time has been reached. Continue doing this until the Result Persistence time period has elapsed. In addition if the group hosting CSE supports the <request> resource type it shall create a <request> resource locally, return its Resource ID in the initial acknowledgement. Then update the <request> resource according to clause 7.4.14.2.6 until the Result Persistence time period has elapsed.

flexBlocking: Start aggregating the member responses, and if they have all been aggregated before the Result Expiration Timestamp has been reached, respond directly with the aggregated response as defined in the blockingRequest case. Otherwise when the Result Expiration Timestamp expires, respond with an acknowledgement containing the current aggregated member responses. In addition if the group hosting CSE supports the <request> resource type it shall create a <request> resource locally, return its Resource ID in the initial acknowledgement, and update the <request> resource according to clause 7.4.14.2.6. Then until the Result Persistence time period has elapsed, proceed either as in the nonBlockingRequestAsynch case (if the Originator provided any notification targets) or as in the nonBlockingRequestSynch case (if it provided no notification targets).

##### 7.4.14.2.6	Update <request> resource according to received member responses.

In  the case that the Response Type parameter in the original Request is not blockingRequest, the group Hosting CSE shall update the created <request> resource as a Transit CSE as specified in clause 7.3.2.5 and in addition as following:

Update a value to the resource-specific attributes of <request> resource according to the following table:

Table 7.4.14.2.6-1: Resource-specific attributes settings for <request> resource

| Attribute Name | Value |
| --- | --- |
| requestStatus | If the original request has been successfully fanned out to the next hop for at least one member resource, this shall be set to "FORWARDED". If all the fanout requests have been rejected, this shall be set to "FAILED". If all member responses have been aggregated, this shall be set to ‘COMPLETED’. If only some of the member responses have been aggregated, this shall be set to ‘PARTIALLY_COMPLETED’. |
| operationResult | the aggregated group response which contains all received member responses |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

##### Create

The primitives create the content of all member resources belonging to an existing <group> resource.

Originator:

Primitive specific operation after Orig-1.0 "Compose Request primitive" and before Orig-2.0 "Send the Request to the receiver CSE": In the case the Originator wants to subscribe to all the member resources of the group and the originator wants the group hosting CSE to aggregate all the notifications come from its member hosting CSEs, the Originator shall include notificationForwardingURI attribute in the <subscription> resource.

Receiver:

Primitive specific operation after Recv-6.2 "Check existence of the addressed resource" and before Recv-6.3 "Check authorization of the Originator": The to parameter consists of the URI of the group resource plus a suffix marked by /fanOutPoint or /fanOutPoint/.....

Primitive specific operation additional to Recv-6.3 "Check authorization of the Originator": The Group Hosting CSE shall check the authorization of the Originator based on the membersAccessControlPolicyIDs of the parent <group> resource. In the case the membersAccessControlPolicyIDs is not provided, the accessControlPolicyIDs of the parent <group> resource shall be used.

Primitive specific operation to replace Recv-6.5"Create/Update/Retrieve/Delete/Notify operation is performed" and Recv-6.6"Announce/De-announce the resource" in the generic procedure:

- Validate the member types, refer to clause 7.4.14.2.1.

Sub-group creation for members residing on the same CSE, refer to clause 7.4.14.2.2.

Assign URI for aggregation of notification, refer to clause 7.4.14.2.3.

Fanout Request to each member, refer to clause 7.4.14.2.4.

Aggregate member responses, refer to clause 7.4.14.2.5.

##### Retrieve

The primitives retrieve the content of all <member> resources belonging to an existing <group> resource.

Originator:

No primitive specific operations.

Receiver:

Primitive specific operation after Recv-6.2 "Check existence of the addressed resource" and before Recv-6.3 "Check authorization of the Originator": The To parameter consists of the URI of the <group> resource plus a suffix marked by /fanOutPoint or /fanOutPoint/.....

Primitive specific operation additional to Recv-6.3 "Check authorization of the Originator": The Group Hosting CSE shall check the authorization of the Originator based on the membersAccessControlPolicyIDs of the parent group resource. In the case the membersAccessControlPolicyIDs is not provided, the accessControlPolicyIDs of the parent group resource shall be used.

Primitive specific operation to replace Recv-6.5"Create/Update/Retrieve/Delete/Notify operation is performed" and Recv-6.6 "Announce/De-announce the resource" in the generic procedure:

- Sub-group creation for members residing on the same CSE, refer to 7.4.14.2.2.

- Fanout Request to each member, refer to 7.4.14.2.4.

- Aggregate member responses, refer to clause 7.4.14.2.5.

##### Update

The primitives update the content of all member resources belonging to an existing <group> resource.

Originator:

No primitive specific operations.

Receiver:

Primitive specific operation after Recv-6.2 "Check existence of the addressed resource" and before Recv-6.3 "Check authorization of the Originator": The To parameter consists of the URI of the <group> resource plus a suffix marked by /fanOutPoint or /fanOutPoint/.....

Primitive specific operation additional to Recv-6.3 "Check authorization of the Originator": The Group Hosting CSE shall check the authorization of the Originator based on the membersAccessControlPolicyIDs of the parent group resource. In the case the membersAccessControlPolicyIDs is not provided, the accessControlPolicyIDs of the parent group resource shall be used.

Primitive specific operation to replace Recv-6.5 "Create/Update/Retrieve/Delete/Notify operation is performed" and Recv-6.6"Announce/De-announce the resource" in the generic procedure:

- Validate the member types, refer to 7.4.14.2.1.

- Sub-group creation for members residing on the same CSE , refer to 7.4.14.2.2.

- Fanout Request to each member, refer to 7.4.14.2.4

- Aggregate member responses, refer to 7.4.14.2.5..

##### Delete

The primitives delete the content of all member resources belonging to an existing <group> resource.

Originator:

No primitive specific operations.

Receiver:

Primitive specific operation after Recv-6.2 "Check existence of the addressed resource" and Recv-6.3 "Check authorization of the Originator": The To parameter consists of the URI of the group resource plus a suffix marked by /fanOutPoint or /fanOutPoint/.....

Primitive specific operation additional to Recv-6.3 "Check authorization of the Originator": The Group Hosting CSE shall check the authorization of the Originator based on the membersAccessControlPolicyIDs of the parent group resource. In the case the membersAccessControlPolicyIDs is not provided, the accessControlPolicyIDs of the parent group resource shall be used.

Primitive specific operation to replace Recv-6.5"Create/Update/Retrieve/Delete/Notify operation is performed" and Recv-6.6"Announce/De-announce the resource" in the generic procedure:

- Validate the member types , refer to 7.4.14.2.1.

- Sub-group creation for members residing on the same CSE , refer to 7.4.14.2.2

- Fanout Request to each member. See Clause 7.4.14.2.4

- Aggregate member responses, refer to clause 7.4.14.2.5.

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

##### m2m:requestStatus

Used for requestStatus attribute in <request> resource.

Table 6.3.4.2.10-1: Interpretation of requestStatus

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | COMPLETED |  |
| 2 | FAILED |  |
| 3 | PENDING |  |
| 4 | FORWARDED |  |
| 5 | PARTIALLY_COMPLETED |  |
| NOTE: See clause 7.4.12 "Resource Type request" |

### -----------------------End of change 3---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?