| CHANGE REQUEST |
| --- |
| Meeting:* | PRO#21 |
| Source:* | Qualcomm Inc. (TIA) |
| Date:* | 2016-01-11 |
| Contact:* | Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Nobu Uchida, Qualcomm, nuchida@qti.qualcomm.com |
| Reason for Change/s:* | Reorganization of sections in TS-0020 and addition of new text |
| CR against: Release* | Release-2 |
| CR against: WI* | Active WI-0040 MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0020v0.2.0 |
| Clauses/Sub Clauses* | 1, 3, 4, 5, 6, 7 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR proposes a number of changes and additions to the current draft version v0.2.0 of TS-0020.

This proposal aims to take into account previous proposals PRO-2015-0974R02 and PRO-2015-1061 presented by Fujitsu which have been already discussed but not agreed yet.

This CR also suggests a reorganization of the current structure of TS-0020. Due to this it has been felt that it is easier to write this as a separate fresh contribution rather than to suggest further updates of PRO-2015-0974R02 and PRO-2015-1061.

This first revision is still incomplete. It is planned to add text to the sections which are still empty in an update R01 of this contribution as soon as possible.

### -----------------------Start of change 1-------------------------------------------

# Scope

The present document specifies the binding of Mca and Mcc primitives onto the WebSocket protocol.

It specifies:

- Procedures  message formats for opening and closing of WebSocket connections.

- How request and response primitives are mapped into the payload of the WebSocket protocol.

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

## Definitions

oneM2M WebSocket Client: A WebSocket Client associated with an AE or a CSE capable to establish the WebSocket connection towards a CSE.

oneM2M WebSocket Server: A WebSocket Server associated with a CSE which accepts requests to establish WebSocket connections.

### Editor’s Note: Do we actually need any of the above definitions?

### -----------------------End of change 2-------------------------------------------

### -----------------------Start of change 3-------------------------------------------

# Overview on WebSocket Binding

Use of WebSocket

This binding makes use of the WebSocket protocol [RFC6455] to transport serialized representations of oneM2M request and response primitives over the Mca or Mcc reference points.

Establishment of a WebSocket connection shall be initiated by a Websocket client with sending a handshake to a Websocket server as specified in section 4 of [RFC6455]. Once the WebSocket connection is established, both oneM2M request and response primitives can be exchanged bi-directionally between the two endpoints of the connection. Serialized representations of the request and response primitives shall be mapped in the Payload Data field of the WebSocket base framing protocol as defined in section 5.2 of [RFC6455].

A WebSocket connection employs either a TCP/IP or a TLS over TCP/IP connection. The underlying TCP and TLS connections are established as the first step of the Websocket handshake.

Binding Overview

WebSocket binding may be employed for communication between any two endpoints which can be connected over the Mca, Mcc or Mcc’ interface reference points supported by the oneM2M Architecture as shown in Figure 6.1-1 of TS-0001 [x].

When using the WebSocket protocol, one communication endpoint shall act as WebSocket server. The WebSocket server listens for inbound handshake messages arriving from any Websocket client to which a WebSocket connection is not established yet. Whether a communication endpoint takes the role of the client or server shall depend on the registration relationship between the communicating entities as follows: the registree shall always use a WebSocket client, while the associated registrar shall always use a WebSocket server on the respective reference point.

This implies that ADN and ASN always take the role of a WebSocket client when WebSocket binding is employed. An MN-CSE uses a WebSocket server for communication with its registrees and a WebSocket client for communication with its own registrar (which can be another MN-CSE or an IN-CSE).

The IN-CSE uses a WebSocket server for communication with all its registrees, i.e. within a service provider’s domain.  On the Mcc’ reference points, i.e. for communication between IN-CSEs of different Service Provider domains, the IN-CSE shall provide both WebSocket client and server functionality. This enables any IN-CSE to open a WebSocket connection to any IN-CSE of another Service Provider’s domain.

Figure 4.2-1 shows some applicable example scenarios.

There exists at most one WebSocket connection between two nodes. A WebSocket connection is established for the first time when the initial registration procedure of an entity to its registrar is performed. On an established WebSocket connection, request and response primitives can be exchanged in both directions. Any connection may be closed by either the WebSocket client or the server, depending on the communication schedule of either entity. However, the connection can be reopened from the client side only.

If the connection is closed temporarily, it should be reopened when the next request primitive is sent from the client to the server side, or when the entity wants to become reachable for incoming primitives. If the next-hop entity is not reachable and the WebSocket connection cannot be established, the sending entity shall buffer any primitives until their expiration time is reached.

### Figure 4.2-2 shows an example message flow for a scenario where an ADN-AE registers to its registrar MN-CSE using an unsecured TCP connection without proxy and then continues exchanging non-registration request and response primitives.

### The ADN-AE wants to register to its registrar MN-CSE. If a WebSocket connection does not exist, it is established by means of the following steps 2) and 3). It is assumed that the ADN-AE knows the point of access (host address and port number) under which the registrar CSE can be reached with WebSocket binding.

### The WebSocket client sends a handshake to the server. The client handshake consists of an HTTP upgrade request, along with a list of required and optional header fields. If the server can be reached under the ws-URI ws://mncse1234.net:9000, the client handshake may look e.g. as follows:

### GET / HTTP/1.1

### Host: mncse1234.net:9000

### Upgrade: WebSocket

### Connection: Upgrade

### Sec-WebSocket-Key: ud63env87LQLd4uIV20/oQ==

Sec-WebSocket-Version: 13

- The WebSocket server replies with a handshake to the client. The server handshake consists of an HTTP Upgrade response, along with a list of required and optional header fields.  In the successful case, the status-line of this HTTP response may include e.g. the following information:

- Request-Version:  HTTP/1.1

- Status-Code: 101

- Response-Phrase: Switching Protocols

- Upgrade: WebSocket

- Connection: Upgrade

- Sec-WebSocket-Accept: FuSSKANnI7C/6/FrPMt70mfBY8E=

- The ADN-AE sends a registration request primitive which may e.g. look as follows as JSON-serialized representation:

- {“m2m:rqp”:{"op":"1","to":"mncse1234","ri":"A1234","pc":{"m2m:ae":{"api":“a56”, “apn”:”app1234”,“poa”:”ws://192.168.194.10”,“rr”:”true”}},"ty": 2}}

- WebSocket binding for the request primitive of step 4) is applied. When transmitting a JSON-serialized primitive in utf-8 text format, the 4-bit opcode in the WebSocket Base Framing Protocol is set to x1 (“text frame”). The binding operation then essentially is just to include the utf-8 encoded above string into the Payload Data of the frame, and to set the correct length of this field.

- The WebSocket frame is sent to the WS server

- The original request primitive us unpacket from the WebSocket frame

- The request primitive is indicated to the MN-CSE.

- The MN-CSE performs the receiver side operations of AE registration as specified in TS-0001 [y

- The response primitive is indicated to the WebSocket server

- WebSocket binding of the response primitive is performed and packed into a WebSocket frame

- The WebSocket frame which contains the response primitive in its Payload Data is returned to the client.

- The response primitive is unpacked.

- The response primitive is delivered to the ADN-AE.

- After successful completion of AE registration any other CRUDN requests and response primitives can be exchanged over the existing WebSocket connection. If the AND-AE has no other requests to send, the WebSocket connection may be closed temporarily. When the WebSocket connection is closed after registration and reopened later again, the registration procedure as outlined in steps 4 to 14 is omitted. In this case any non-registration request primitives can be sent directly.

# Protocol Binding

## Introduction

The WebSocket protocol enables two-way communication between client and server even when firewall and/or NAT are present between them. This means, once a WebSocket connection is established, request (and response) primitives can be exchanged in both direction, from the client to the server and vice versa. However, AEs may be capable to handle Notification request primitives only, or no request primitives at all.

WebSocket binding applied by oneM2M entities/nodes shall be fully compliant with RFC 6455 []. After establishment of a WebSocket connection between two nodes, at the transmitter side each individual request and response primitive is mapped into one or several WebSocket frames.

## WebSocket connection establishment

General

A WebSocket connection is opened by the client side as specified in section 4 of RFC 6455 [RFC6455] with sending of a client handshake. The server responds with a server handshake.

The client handshake consists of an HTTP upgrade request, along with a list of required and optional header fields. The server handshake consists of a HTTP status-line.

The applicable format of the request-line, status-line and the applicable header fields are specified in the following subsections

### Client handshake Format of request-line

5.2.2.1	Format of request-line

To be added

### 5.2.2.2	Host header

## To be added

5.2.2.3	Upgrade header

To be added

5.2.2.4	Connection header

To be added

5.2.2.5	Sec-WebSocket-Key header

To be added

5.2.2.6	Sec-WebSocket-Version header

To be added

5.2.2.7	Sec-WebSocket-Protocol-Client header

To be added

5.2.2.8	Selection of Payload Data formats

Selection between textual and binary Payload Data formats

To be added

Server handshake format

Status-line and headers, to be added

## Closing a WebSocket connection

A WebSocket connection shall be closed by sending a Connection Close Frame (opcode x8). Both, client and server may close an existing WebSocket connection at any time.

WebSocket connections should be kept open for as long time as possible considering any given constrains due to communication policies and power saving requirements.

## Registration procedure

Present text to be revised

Once WebSocket Connection is established, the Originator shall perform Registration procedure which is described in TS-0004. When the Registration procedure was successfully performed, the WebSocket Server (e.g. Registrar CSE for WebSocket Client) shall enable routing incoming oneM2M primitive messages to the Originator.

Editor’s Note: How to describe the point of Acess at <AE> or <CSE> is FFS.

Thus until the Registration procedure is successfully completed, all incoming oneM2M primitive messages to the WebClient shall be rejected by the Receiver (e.g. registrar CSE).

Editor’s Note: What the state of AE after it disconnected the WebSocket connection.

## Handling of Non-Registration Requests

to be added:  how to handle the various transfer modes (blocking, non-blocking synchronous, non-blocking asynchronous

# Security Aspects

Credentials to use for WSS connection, to be added

# Examples

The present clause illustrates the example call flow for WebSocket protocol binding.

(TBD)

### -----------------------End of change 3-------------------------------------------

# Text boxes

Figure 4.2-1: Example scenarios of WebSocket client and server configurations

AE

WS

Client

CSE

WS

Server

WS

Client

AE

CSE

WS

Client

AE

AE

WS

Client

CSE

WS

Client

AE

CSE

WS

Server

WS

Client

AE

CSE

WS

Server

WS

Client

ADN

ASN

ADN

MN

MN

ASN

IN

Mcc’

Mcc

Mca

Mcc

Mca

Mcc

Figure 4.2-2: Example message flow with Websocket binding

AE

WS client

c

client

CSE

WS server

c

client

ADN

MN

- AE wants to start registration procedure and triggers WebSocket connection establishment

- Client handshake

- Server handshake

- Request primitive

- WebSocket Binding

- WebSocket frame

- Unpacking request primitive

- Request primitive

- Receiver side processing of AE registration procedure

- Response primitive

- WebSocket Binding

- WebSocket frame

- Unpacking response primitive

- Response primitive

- non-registration CRUDN operations