²

| CHANGE REQUEST |
| --- |
| Meeting:* | ARC TP21 |
| Source:* | GEMALTO N.V |
| Date:* | 2016-01-11 |
| Contact:* | Thierry Garnier , GEMALTO N.V, Thierry.garnier@gemalto.com |
| Reason for Change/s:* | Alignment with TS-0001 2.5.0 regarding eventType notification This feature – eventType ‘E’ - is namely used in the (e.g. LWM2M) Interworking context . The use case is the following : a RETRIEVE request is performed in targeting a <container> resource for which the IPE has subscribed to an eventType ‘E’. With a ‘Result Content’ of the RETRIEVE request set to ‘child-resources’, if the <contentInstance> resource is obsolete, the IPE will be notified (eventType ‘E’) , and then will address the - e.g. LWM2M - Interworking context, to create and update the <latest> resource with fresh values. |
| CR against: Release* | Release 2 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 V2.3.0 |
| Clauses/Sub Clauses* | 6.3.4.2.19 m2m:eventType (refer to TS-0001 2.5 Table 9.6.8-3: eventNotificationCriteria conditions) |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

### -----------------------Start of change 1 ---------------------------------------------

##### m2m:notificationEventType

Used for eventNotificationCriteria conditions.

Table 6.3.4.2.19-1: Interpretation of notificationEventType

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | Update_of_Resource | Default |
| 2 | Delete_of_Resource |  |
| 3 | Create_of_Direct_Child_Resource |  |
| 4 | Delete_of_Direct_Child_Resource |  |
| 5 | An attempt to retrieve a direct <contentInstance> child-resource of the subscribed-to <container> resource is performed while this child is an obsolete resource or the reference used for retrieving this child resource is not assigned.This retrieval is performed by a RETRIEVE request targeting the subscribed-to resource with the Result Content parameter set to either “child-resources” or “attributes+child-resources” |  |
| NOTE: |

### -----------------------End of change 1 --------------------------------------------------

### -----------------------Start of change 2 ---------------------------------------------

#### m2m:eventNotificationCriteria

Used for eventNotificationCriteria of a <subscription> resource.

Table 6.3.5.6-1:Type Definition of m2m:eventNotificationCriteria

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| createdBefore | m2m:timestamp | 0..1 |  |
| createdAfter | m2m:timestamp | 0..1 |  |
| modifiedSince | m2m:timestamp | 0..1 |  |
| unmodifiedSince | m2m:timestamp | 0..1 |  |
| stateTagSmaller | xs:positiveInteger | 0..1 |  |
| stateTagBigger | xs:nonNegativeInteger | 0..1 |  |
| expireBefore | m2m:timestamp | 0..1 |  |
| expireAfter | m2m:timestamp | 0..1 |  |
| sizeAbove | xs:nonNegativeInteger | 0..1 |  |
| sizeBelow | xs:positiveInteger | 0..1 |  |
| operationMonitor | m2m:operation | 0..5 |  |
| attribute | m2m:attribute | 0..n |  |
| notificationEventType | m2m:notificationEventType | 0..5 |  |

### -----------------------End of change 2 --------------------------------------------------