| CHANGE REQUEST |
| --- |
| Meeting:* | PRO#21 |
| Source:* | Qualcomm Inc. (TIA) |
| Date:* | 2016-01-11 |
| Contact:* | Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Nobu Uchida, Qualcomm, nuchida@qti.qualcomm.com |
| Reason for Change/s:* | Annex A.1 of TS-0009 needs corrections |
| CR against: Release* | Release-2 |
| CR against: WI* | Active WI-0040 MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0009v2.2.0 |
| Clauses/Sub Clauses* | A.1 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: PRO-2016-0022-CR_TS0009_AnnexA1 |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

CR PRO-2015-1065 has been withdrawn but there are still some remaining errors in figure A.1-1 of Annex A.1.

These are intended to be fixed in this CR:

- The figure is not editable due to a Visio version issue and shows some subtle formatting problems due to rescaling. The figure needs to be replaced with correct format.

- The cross-referenced clause number in TS-0004 (ref [3]) is wrong.

- Value of content-size header (presently 52) is not correct for the shown XML in the FTTP body

- The XML serialized representation of the container resource has following issues:

  - CML shows unnecessary line breaks and spaces that should be removed

  - Lacks correct notation of the root element (<m2m:cnt> rather than <cnt>)

  - Value of the container”s resourceName is inconsistent with step 2 (cnt1 rather than cont1)

In order to clarify the meaning of some of the parameters, an additional sentence has been included above the figure.

### -----------------------Start of change 1-------------------------------------------

# A.1	<container> resource creation

Figure A.1-1 is HTTP mapping of procedure described in clause 7.4.7.2.1 [3]. Note the example shown in the figure applies under the following assumptions:

- “CSE1” is the name (i.e. value of the resourceName attribute) of the <CSEBase> resource of the registrar CSE

- “cont1” is the name of the created <container> resource chosen by the registrar CSE

Figure A.1-1: oneM2M HTTP Binding Example - container creation

### -----------------------End of change 1-------------------------------------------