| CHANGE REQUEST |
| --- |
| Meeting:* | PRO#21.1 |
| Source:* | Qualcomm Inc. |
| Date:* | 2016-02-08 |
| Contact:* | Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com |
| Reason for Change/s:* | Corrections to the filterCriteria primitive parameter: Wrong subelement names used in clause “7.3.3.17 Filter conditions”: “lastModifiedBefore” and “lastModifiedAfter” rather than “modifiedSince” and “unmodifiedSince”, respectively. Wrong data type used in XSD for “resourceType” subelement: XSD needs to be corrected for alignment with text in TS-0004. |
| CR against: Release* | Release-1 |
| CR against: WI* | Active <Work Item number> MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004v1.5.0 |
| Clauses/Sub Clauses* | 7.3.3.17, 7.3.3.17.2, CDT-commonTypes_v1_5_0.xsd |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

Clause “7.3.3.17	Using Filter Criteria for identification of target resources” of TS-0004 uses a wrong notation for some subelements of the Filter Criteria primitive parameter:

In Table 7.3.3.17-1 and in subclause 7.3.3.17.2, the definition of the “lastModifiedTime” filter condition is referring to subelement names denoted “lastModifiedBefore” and “lastModifiedAfter”. However, these subelements are denoted  “modifiedSince” and “unmodifiedSince” in the actual Filter Criteria definition. Changes 1 and 2 of this CR correct this notation in clauses 7.3.3.17 and 7.3.3.17.2.  This correction has no impact on the related XSD.

Further it has been noted that the XSD of the resourceType subelement of Filter Criteria is currently incorrectly implemented:  TS-0004 specifies that the resourceType subelement may be a list of resourceType identifiers including more than one list value. However the current XSD definition allows only a single resourceType entry, not a list. This correction has no impact on TS-0004 itself. It requires 2 corrections in CDT-commonTypes-v1_6_0.xsd (and CDT-commonTypes-v2_4_0 for the Release-2 mirror CR), shown in change 3 of this CR.

### -----------------------Start of change 1-------------------------------------------

#### Using Filter Criteria for identification of target resources

When the Filter Criteria primitive parameter is present in a request primitive, it shall be applied for identification of the applicable target resources of the respective operation. This may apply to Retrieve, Delete and Discovery operations as specified in clauses 7.3.3.6, 7.3.3.8 and 7.3.3.14, respectively.

The Filter Criteria primitive parameter defines conditions on resource attributes. Resources matching the conditions shall be selected as target of the operation. Table 7.3.3.17-1 summarizes the various filter criteria and conditions. Each row in the table represents a different filter condition type.

If multiple conditions of different type (i.e. different condition tags) are present in the Filter Criteria parameter, these shall be satisfied all to pass the overall combined filter condition, i.e. the combined condition shall be derived by applying Boolean AND operation across each individual condition.

If multiple conditions of the same type (i.e. same condition tag) are present in the Filter Criteria parameter, these shall be combined by applying Boolean OR operation. This applies to condition tags labels, resourceType, contentType or attribute for multiplicity n > 1.

Table 7.3.3.17-1: Summary on Filter conditions

| Condition Tag | Multiplicity | Targeted Resource Attribute | Matching Condition |
| --- | --- | --- | --- |
| createdBefore, | 0..1 | creationTime | creationTime < createdBefore, see clause 7.3.3.17.1. |
| createdAfter | 0..1 |  | createdAfter ≤ creationTime , see clause 7.3.3.17.1. |
| unmodifiedSince | 0..1 | lastModifiedTime | lastModifiedTime < unmodifiedSince, see clause 7.3.3.17.2. |
| modifiedSince | 0..1 |  | modifiedSince ≤ lastModifiedTime, see clause 7.3.3.17.2. |
| stateTagSmaller | 0..1 | stateTag | stateTagSmaller < stateTag, see clause 7.3.3.17.3. |
| stateTagBigger | 0..1 |  | stateTag ≤ stateTagBigger, see clause 7.3.3.17.3. |
| expireBefore | 0..1 | expirationTime | expirationTime < expireBefore, see clause 7.3.3.17.4. |
| expireAfter | 0..1 |  | expireAfter ≤ expirationTime , see clause 7.3.3.17.4. |
| labels | 0..n | labels | see clause 7.3.3.17.5. |
| resourceType | 0..n | resourceType | see clause 7.3.3.17.6. |
| sizeBelow | 0..1 | contentSize | contentSize < sizeBelow, see clause 7.3.3.17.7. |
| sizeAbove | 0..1 |  | sizeAbove ≤ contentSize, see clause 7.3.3.17.7. |
| typeOfContent | 0..n | contentInfo | matched with typeOfContent component in contentInfo, see clause 7.3.3.17.8. |
| attribute | 0..n | (variable) | name and value of Filter Criteria attribute matches resource attribute, see clause 7.3.3.17.9. |
| limits | 0..1 | (not applicable) | Constraint on maximum number of targeted resources, see clause 7.3.3.17.10. |
| filterUsage | 0..1 | (not applicable) | Indicator specifying the use case of Filter Criteria parameters. |

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

##### Conditions on the lastModifiedTime attribute

The Filter Criteria elements modifiedSince and unmodifiedSince define a time interval which is tested against the lastModifiedTime attribute of the applicable resources.

This filter criterion shall be satisfied if any of the following three conditions is fulfilled:

- only unmodifiedSince given in Filter Criteria: 
lastModifiedTime <  unmodifiedSince

- only modifiedSince given in Filter Criteria: 
modifiedSince ≤ lastModifiedTime

- both, modifiedSince and unmodifiedSince given in Filter Criteria: 
(modifiedSince ≤ lastModifiedTime) AND (lastModifiedTime < unmodifiedSince))

NOTE:  In case 3) the Filter Criteria will only generate a match if modifiedSince < unmodifiedSince.

### -----------------------End of change 2-------------------------------------------

### -----------------------Start of change 3-------------------------------------------

Correction of existing “filterCriteria” data type and addition of a new simple type “resourceTypeList”  in CDT-commonTypes-v1_6_0.xsd and CDT-commonTypes-v2_4_0.xsd:

<xs:complexType name="filterCriteria">
		<xs:sequence>
			<xs:element name="createdBefore" type="m2m:timestamp" minOccurs="0" />
			<xs:element name="createdAfter" type="m2m:timestamp" minOccurs="0" />
			<xs:element name="modifiedSince" type="m2m:timestamp" minOccurs="0" />
			<xs:element name="unmodifiedSince" type="m2m:timestamp" minOccurs="0" />
			<xs:element name="stateTagSmaller" type="xs:positiveInteger" minOccurs="0" />
			<xs:element name="stateTagBigger" type="xs:nonNegativeInteger" minOccurs="0" />
			<xs:element name="expireBefore" type="m2m:timestamp" minOccurs="0" />
			<xs:element name="expireAfter" type="m2m:timestamp" minOccurs="0" />
			<xs:element name="labels" type="m2m:labels" minOccurs="0" />
			<xs:element name="resourceType" type="m2m:resourceTypeList" minOccurs="0" />
			<xs:element name="sizeAbove" type="xs:nonNegativeInteger" minOccurs="0" />
			<xs:element name="sizeBelow" type="xs:positiveInteger" minOccurs="0" />
			<xs:element name="contentType" type="m2m:typeOfContent" minOccurs="0" maxOccurs="unbounded" />
			<xs:element name="attribute" type="m2m:attribute" minOccurs="0" maxOccurs="unbounded" />
			<xs:element name="filterUsage" type="m2m:filterUsage" minOccurs="0" />
			<xs:element name="limit" type="xs:nonNegativeInteger" minOccurs="0" />
		</xs:sequence>
	</xs:complexType>

<xs:simpleType name="resourceTypeList">
		<xs:restriction> 
			<xs:simpleType> 
				<xs:list itemType="m2m:resourceType" />
			</xs:simpleType> 	
			<xs:minLength value="1" /> 
		</xs:restriction> 
	</xs:simpleType>

### -----------------------End of change 3-------------------------------------------