| Input Contribution |
| --- |
| Meeting ID* | PRO22 |
| Title:* | Group_frm_Compliance |
| Source:* | Bob Flynn, InterDigital, Bob.Flynn@interdigital.com |
| Uploaded Date:* | 2016-03-06 |
| Document(s) Impacted* | TS-0004 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | The contribution proposes some CRs found during development of Test Purposes for compliance. |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution introduces CRs to address details needed for compliance test purpose development.

Issue 1: TS-0001 states that there is a check to make sure that duplicate memberIDs do not exist, it does not say what to do in the case that duplicate members are found..  I propose that TS-0004 include text that states that duplicate memberIDs are dropped, leaving only a single instance of any memberID in a group.

Issue 2: TS-0001 states that member type validation should occur and that failures should be handled according to the specified consistency strategy.  However, in the case of memberTypeValidation failing and consistencyStrategy is ABANDON_GROUP there is no <group> resource created, unlike the other failure scenarios.  In this case, the response status code is not specified.  I propose that TS-0004 use the existing Response Status Code indicating "MEMBER_TYPE_INCONSISTENT" error.

================ Start of  1st  Change ==================

##### Create

Primitive specific operation after Recv-C-6.4 "Check validity of resource representation for the given resource type" and before Recv-C-6.5 "Create/Update/Retrieve/Delete/Notify operation is performed ". See clause 7.2.2.2.

- Primitive specific operation: Validate the provided attributes. It shall also check whether the number of URIs present in the memberIDs attribute of the group resource representation does not exceed the maximum as specified by the attribute maxNrOfMembers. If the maximum is exceeded, the request shall be rejected with a Response Status Code indicating "MAX_NUMBER_OF_MEMBER_EXCEEDED" error. If any memberIDs is present more that once then the duplicate memberIDs are removed before creation of the <group> resource.
If the memberType attribute of the <group> resource is not "MIXED", the hosting CSE shall also verify that all the member URIs including sub-groups in the attribute memberIDs of the <group> resource representation provided in the request shall conform to the memberType of the group resource.

In the case that the <group> resource contains sub-group member resources, the receiver shall retrieve the memberType of the sub-group member resources to validate the memberType. If the memberType cannot be retrieved due to lack of privilege, the request shall be rejected with a Response Status Code indicating "NO_PRIVILEGE" error. If the sub-group member resources are temporarily unreachable, the receiver shall set the memberTypeValidated attribute of the <group> resource to FALSE and return the result to the originator in the response of the request. As soon as any unreachable sub-group resource becomes reachable, the receiver shall perform the memberType validation procedure. The originator may get to know the validation result by subscribe to the created resource if the memberTypeValidated attribute is FALSE.

Upon unsuccessful validation, the receiver shall delete the <group> resource if the consistencyStrategy of the <group> resource is ABANDON_GROUP then the request shall be rejected with a Response Status Code indicating "MEMBER_TYPE_INCONSISTENT" error, or remove the inconsistent members from the <group> resource if the consistencyStrategy attribute is ABANDON_MEMBER, or set the memberType attribute of the <group> resource to "MIXED" if the consistencyStrategy attribute is SET_MIXED.
The memberTypeValidated attribute shall be set to TRUE if all the members have been validated successfully.

================ End of  1st  Change ==================