| CHANGE REQUEST |
| --- |
| Meeting:* | PRO#22 |
| Source:* | Dongjoo Kim (dongjoo7.kim@lge.com) Yingjie Hong, ZTE, hong.yingjie@zte.com.cn |
| Date:* | 2016-3-14 |
| Contact:* | Dongjoo Kim (dongjoo7.kim@lge.com) |
| Reason for Change/s:* | This CR is for reducing the gap between ARC and PRO and for editorial changes |
| CR against: Release* | Rel-2 |
| CR against: WI* | Active MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 V2.4.0 |
| Clauses/Sub Clauses* | 7.3.3.10 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: PRO-2016-0097R01) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR is proposed to reduce the gap between ARC and PRO spec. While reviewing the agreed contribution ARC-2016-0023R01-resource_announcement_procedure_corrections(R2) from ZTE, it was found that the sentence in red color below is not specified in the PRO spec.

| Processing at the Originator before sending Request | Other details for the information in the Request message shall be as follows: Attributes marked with MA and attributes marked with OA that are included in the announcedAttribute attribute at the original resource shall be provided in the CREATE Request. Such attributes shall have the same value as for the original resource. resourceType which shall be set to the appropriate tag that identifies the <Annc> resource. expirationTime provided by the Originator equal to the one for the original resource. |
| --- | --- |

In addition, this input also includes a few editorial changes.

### -----------------------Start of change 1-------------------------------------------

#### Announce the resource or attribute

If a CREATE request that contains an announceTo attribute is received,

Compose the CREATE Request primitive to create announced resource as follows:

The link  attribute is set to the URI of the original resource.

If accessControlPolicyIDs attribute of the original resource is not present, accessControlPolicyIDs attribute is set to the same value with the parent resource or from the local policy of the original resource.

Attributes marked with MA and attributes marked with OA that are included in the announcedAttribute attribute. Such attributes shall be present in the original resource and set to same value as the original resource.

The resourceType attribute is set to the announced variant of the original resource (see the table 6.3.4.2.1-1)

Send the CREATE Request to the CSE(s) represented by exact URI(s) or CSE-ID(s) in the announceTo attribute of the request.

Wait for the Response primitive

Add the URI of successfully announced resource to the announceTo attribute of the resource

Include updated announceTo attribute in the Content parameter in the Response to the received CREATE Request.

### -----------------------End of change 1---------------------------------------------