| CHANGE REQUEST |
| --- |
| Meeting:* | PRO 22.0 |
| Source:* | FUJITSU |
| Date:* | 2016-03-17 |
| Contact:* | Shingo Fujimoto, FUJITSU, shingo_fujimoto@jp.fujitsu.com |
| Reason for Change/s:* | PRO-2016-0100-discussion_data_type_for_customAttribute was introduced and discussed in MAS adhoc with interested party about how <flexContainer> resource can be generic without change processing logic on the oneM2M solution. As the conclusion of the discussion, participants determined opt-2: name attribute is the way to go. This CR proposed to add new common data type to implement the idea. |
| CR against: Release* | Release-2 |
| CR against: WI* | Active WI-0017: Home network enablement MNT maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 v2.2.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

New common type named costomAttributeList is proposed.

If the customAttributes are defined as [attribute1] and [attribute2] then,The XML data should look like:

<customAttribute ID="attribute1">value1</customAttribute>

<customAttribute ID="attribute2">value2</customAttribute>

And, JSON data should look like:

"customAttribute": [

"attribute1": "value1",

"attribute2": "value2"

]

### -----------------------Start of change 1-------------------------------------------

#### 6.3.4.x	m2m:customAttribute

Used for representing customAttribute attribute name and its value pairs in <flexContainer> resource.

Table 6.3.4.x-1: Type Definition of m2m:customAttribute

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| customAttribute | xs:string | 0..n | String representation of [customAttribute] value. Actual data type shall be checked according from the definition of the specialization of <flexContainer> |
| customAttribute/@name | xs:ID | 1 | The name of [custromAttribute]. |
| NOTE: In the above table, names of XML schema attributes are prefixed with a "@" character to differentiate these from Resource attribute names. The "@" character is not part of the actual attribute name. |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

(folloing XSD definition to be added as common type)

<xs:element name="customAttribute" maxOccurs="unbounded" minOccurs="0">

<xs:complexType>

<xs:simpleContent>

<xs:extension base="xs:string">

<xs:attribute type="xs:string" name="name" use="required"/>

</xs:extension>

</xs:simpleContent>

</xs:complexType>

</xs:element>

### -----------------------End of change 2-------------------------------------------

### -----------------------Start of change 3-------------------------------------------

### Resource Type <flexContainer>

#### Introduction

This resource represents a customizable container for data instances. It is a template for the definition of flexible specializations of data containers.

The detailed description can be found in clause 9.6.35 in TS-0001 [6].

There are multiple specializations of  <flexContainer>; these are defined in TBD. Each of these specializations has its own schema file. There is no separate schema file just for <flexContainer>, however the XML schema types for the specializations all conform to the pattern described in this clause.

Table 7.4.30.1-1: Universal/Common Attributes of <flexContainer> resource

| Attribute Name | Request Optionality |
| --- | --- |
|  | Create | Update |
| @resourceName | O | NP |
| resourceType | NP | NP |
| resourceID | NP | NP |
| parentID | NP | NP |
| accessControlPolicyIDs | O | O |
| creationTime | NP | NP |
| expirationTime | O | O |
| lastModifiedTime | NP | NP |
| stateTag | NP | NP |
| labels | O | O |
| announceTo | O | O |
| announcedAttribute | O | O |
| dynamicAuthorizationConsultationIDs | O | O |

Table 7.4.30.1-2: Resource Specific Attributes of <flexContainer> resource

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | Create | Update |  |  |
| containerDefinition | M | NP | xs:anyURI | No default |
| creator | NP | NP | m2m:ID | No default |
| ontologyRef | O | O | xs:anyURI | No default |
| [customAttribute] | O | O | m2m:custromAttribute.Name of customAttribute and its data type are defined in the specification document or XSD file identified by the value of containerDefinition attribute. | No default. |

Table 7.4.30.1-3: Child resources of <flexContainer> resource

| Child Resource Type | Child Resource Name | Multiplicity | Ref. to in Resource Type Definition |
| --- | --- | --- | --- |
| <semanticDescriptor> | semanticDescriptor | 0..n | Clause 7.4.x |
| <subscription> | [variable] | 0..n | Clause 7.4.8 |
| <container> | [variable] | 0..n | Clause 7.4.6 |
| <flexContainer> | [variable] | 0..n | Clause 7.4.30 |

#### <flexContainer> resource specific procedure on CRUD operations

This clause describes <flexContainer> resource specific behaviour for CRUD operations.

##### Create

Originator:

No change from the generic procedures in clause 7.2.2.1.

Receiver:

No change from the generic procedures in clause 7.2.2.2.

##### Retrieve

Originator:

No change from the generic procedures in clause 7.2.2.1.

Receiver:

No change from the generic procedures in clause 7.2.2.2.

##### Update

Originator:

No change from the generic procedures in clause 7.2.2.1.

Receiver:

No change from the generic procedures in clause 7.2.2.2.

##### Delete

Originator:

No change from the generic procedures in clause 7.2.2.1.

Receiver:

No change from the generic procedures in clause 7.2.2.2.

### -----------------------End of change 3---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?