| CHANGE REQUEST |
| --- |
| Meeting:* | TP 23 |
| Source:* | InterDigital |
| Date:* | 2016-05-05 |
| Contact:* | Dale Seed – dale.seed@InterDigital.com Bob Flynn – bob.flynn@InterDigital.com Adarsh B L - adarshbramhavara.lakshmana@InterDigital.com |
| Reason for Change/s:* | Add clarification for RO announceable attributes. |
| CR against: Release* | Rel-2 |
| CR against: WI* | Active <Work Item number> MNT Maintenace / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004-V2.4.0 |
| Clauses/Sub Clauses* | Section 6.5.1 , 7.3.1.1, 7.3.3.3 , 7.3.3.4 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: PRO-2016-0156-CR_for_announced_RO_attributes_R1 |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution corresponds to the agreed to ARC-2015-1977R04-Mirror_CR_for_announced_RO_attributes contribution.

This CR clarifies that if an attribute is marked as RO and also marked as MA or OA, then only the attribute of the original resource shall be interpreted as RO.  The corresponding attribute of the announced resource shall be RW to the original resource hosting CSE to allow it to properly announce and de-announce the attribute and keep the attribute’s value synchronized with the original resource.

For example, the currentNrOfInstances, currentByteSize and stateTag attributes of the <container> resource are marked as RO and OA.  .

## ----------------------- Start of change 1 -----------------------

### Description

Each oneM2M Resource Data Type is defined using XML Schema (XSD), and supplied as a separate XSD document.  This XML Schema defines the attributes of the Resource in accordance with TS-0001 [6]. It represents an entire resource. In other words if and only if a requestor retrieves an entire resource in XML format, the XML that is returned shall be valid with respect to the schema for that resource. Note that the payload of a Create or Update request primitive does not necessarily have to be valid according to the schema, as this payload is not required to contain values for all the resource attributes. In particular a resource might contain mandatory read-only primitives, and these would not appear in a Create or Update request, with the exception of announce-deannounce procedures.

During announce-deannounce procedure, read-only attributes ( MA or OA ) are allowed to be present in the announced CREATE/UPDATE request issued from the original resource hosting CSE.

## ----------------------- End of change 1 -----------------------

#### Compose request primitive

The originator shall compose a Request message that shall be mapped to a specific protocol.

The Request shall include mandatory parameters which is Operation, To, From and Request Identifier.

The Request may include the time related parameters which is Originating Timestamp, Request Expiration Timestamp, Result Expiration Timestamp and Operation Execution Time.

The Request may include the other parameters as specified in Table 7.2.1.1-1: Request Primitive Parameters.

When including a resource representation in the request indication for create and update, the originator shall take into account the validation rules as specified in "Check validity for resource representation for create" and "Check validity for resource representation for update" respectively.

EXAMPLE:	Any attributes marked with NP shall not be present in the resource representation for the corresponding request indication with the exception of announce-deannounce procedures.

## ----------------------- Start of change 3 -----------------------

#### Check validity of resource representation for CREATE

The handling below shall apply to each attribute in the resource for CREATE request primitives and the handling depends on the "presence in CREATE request" column of the resource table. If the request is rejected based on the rules below, then the other attributes do not have to be checked.

If no resource representation is present in the CREATE request, then the request is rejected with a Response Status Code indicating "BAD_REQUEST" error.

If the expirationTime attribute is present in the resource representation, but its value indicates a time in the past, then the request shall be rejected with a Response Status Code indicating "BAD_REQUEST" error.

There are three cases where the hosting CSE shall configure or overrride an expirationTime value that differs from the value specified in the resource representation (if present).

- The Originator does not specify an expirationTime

The Originator requests an expirationTime that is later than expirationTime of the parent

The hosting CSE determines the expirationTime requested by the Originator doesn’t meet its requirements (E.g. based on a local policy)

In each of these cases, the hosting CSE shall configure an expirationTime into the resource that is less than or equal to  the expirationTime of the parent resource. In addition, the hosting CSE shall communicate the modified value back to the originator in the response if the Result Content parameter permits this.

M attribute

If the attribute is present in the resource representation in the CREATE request, the hosting CSE shall check if the value is acceptable according to internal policies.

If the provided value is not accepted,  the hosting CSE shall reject the request with a Response Status Code indicating "BAD_REQUEST" error.

If the attribute is not present in the resource representation in the CREATE request the hosting CSE shall reject the request with a Response Status Code indicating "BAD_REQUEST" error.

O attribute

If the attribute is present in the resource representation in the CREATE request, the hosting CSE shall check if the value is acceptable according to internal policies.

If the provided value is not accepted then the hosting CSE shall reject the request with a Response Status Code indicating "BAD_REQUEST" error.

NP attribute

If the attribute is present in the resource representation in the CREATE request, the hosting CSE shall reject the request with a Response Status Code indicating "BAD_REQUEST" error, with the exception during announce-deannounce procedures.

If the request is an announce request by a CSE hosting original resource , NP attributes with values shall be allowed so that the announced attributes remain in synchronization with original attribute values.

## ----------------------- End of change 3 -----------------------

## ----------------------- Start of change 4 -----------------------

#### Check validity of resource representation for UPDATE

The handling below shall apply to each attribute in the resource for UPDATE request primitives and the handling depends on the "presence in UPDATE request" column of the resource table. If the request is rejected based on the rules below, then the other attributes do not have to be checked.

If the expirationTime attribute is present in the resource representation, but its value indicates a time in the past, then the request shall be rejected with a Response Status Code indicating "BAD_REQUEST" error.

M attribute

If the attribute is present in the resource representation in the UPDATE request, the hosting CSE shall check if the value is acceptable according to internal policies.

If the provided value is not accepted, the hosting CSE shall reject the request with a Response Status Code indicating "BAD_REQUEST" error.

If the attribute is not present in the resource representation in the UPDATE request, the hosting CSE shall reject the request with a Response Status Code indicating "BAD_REQUEST" error.

O attribute

If the attribute is present in the resource representation in the UPDATE request, the hosting CSE shall check if the value is acceptable according to internal policies.

If the provided value is not accepted, the hosting CSE shall reject the request with a Response Status Code indicating "BAD_REQUEST " error.

NP attribute

If the attribute is present in the resource representation in the UPDATE request, the hosting CSE shall reject the request with a Response Status Code indicating "BAD_REQUEST" error, with the exception during announce-deannounce procedures.

If the request is an announce request by a CSE hosting original resource, NP attributes with values shall be allowed so that the announced attributes remain in synchronization with the original attribute values.

## ----------------------- End of change 4 -----------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?