| CHANGE REQUEST |
| --- |
| Meeting:* | PRO 23 |
| Source:* | Phil Hawkes, Qualcomm, phawkes@qti.qualcomm.com Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com Nobuyuki Uchida, Qualcomm, nuchida@qti.qualcomm.com |
| Date:* | 2016-05-15 |
| Contact:* | As above |
| Reason for Change/s:* | Stage 3 of primitive parameters added in ARC-2016-0082R04 for end-to-end security features |
| CR against: Release* | 2 |
| CR against: WI* | Active WI-0019 Dynamic Authorization MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0004 and 2.5.0 |
| Clauses/Sub Clauses* |  |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This CR defines data types needed for end-to-end security features

### Add the following row to Table 6.3.3.-1

### -----------------------Start of change 0a (clause 6.3.3)---------------

.

| m2m:e2eCompactJWS | JSON Web Signature (JWS) Compact Serialization, used in End-to-End Security Features TS-003 [7] | eyJ0eXAiOiJK. eyJpc3MiOiJqb2UiLA0KIC. dBjftJeZ4CVP (line breaks for display purposes only) | Of the form [a].[b].[c], where components [a] and [c] are non-empty, while component [b] can be either empty or not empty. When not empty, each component is base64url encoded (RFC 4648 [RFC4648]). See [i.RFC7515] |
| --- | --- | --- | --- |
| m2m:e2eCompactJWE | JSON Web Encryption (JWE) Compact Serialization, used in End-to-End Security Features TS-003 [7] | eyJ0eXAiOiJK. eyJpc3MiOiJqb2UiLA0KIC. dBjftJeZ4CVP. 5eym8TW_c8SuK. SdiwkIr3a. XFBoMYUZo (line breaks for display purposes only) | Of the form [a].[b].[c].[d].[e], where components [a] and [d] are non-empty, while components [b],[c] and [e] can be empty or not empty. When not empty, each component is base64url encoded (RFC 4648 [RFC4648]). See [i.RFC7516] |

### -----------------------End of change 0a ---------------

### -----------------------Start of change 0b ---------------

##### m2m:encodingType

Used for describing encoding type which is applied on the content attribute of the contentInstance resource.

Table 6.3.4.2.28-1: Interpretation of encodingType

| Value | Interpretation | Note |
| --- | --- | --- |
| 0 | Plain - no transfer encoding is applied |  |
| 1 | base64 encoding (see [9]) is applied on string data |  |
| 2 | base64 encoding (see [9]) is applied on binary data |  |
| 3a | JWE Compact Serialization for Encryption-Only End-to-End Security of Data (ESData) Security Class | See [i.RFC7516] |
| 3b | JWS Compact Serialization for Signature-Only ESData Security Class | See [i.RFC7515] |
| 3c | JWE Compact Serialization for Nested-Sign-then-Encrypt ESData Security Class | See [i.RFC7516] |
| 4a | Plain JWE JSON Serialization for Encryption-Only ESData Security Class- no transfer encoding is applied | See [i.RFC7516] |
| 4b | Plain Plain JWS JSON Serialization for Signature-Only ESData Security Class- no transfer encoding is applied | See [i.RFC7515] |
| 4c | JWE JSON Serialization for Nested-Sign-then-Encrypt ESData Security Class- no transfer encoding is applied | See [i.RFC7516] |
| 5a | base64 encoding (see [9]) applied on JWE JSON Serialization for Encryption-Only ESData Security Class | See [i.RFC7516] |
| 5b | base64 encoding (see [9]) applied on JWS JSON Serialization for Signature-Only ESData Security Class | See [i.RFC7515] |
| 5c | base64 encoding (see [9]) applied on JWE JSON Serialization for Nested-Sign-then-Encrypt ESData Security Class | See [i.RFC7516] |
| 6a | Plain XML Encryption v1.1 Serialization for Encryption-Only ESData Security Class - no transfer encoding is applied | See [i.XML-ENCv1.1] |
| 6b | Plain XML Encryption v1.1 Serialization for Signature-Only ESData Security Class - no transfer encoding is applied | See [i.XML-SIGv1.1] |
| 6c | Plain XML Encryption v1.1 for Nested-Sign-then-Encrypt ESData Security Class - no transfer encoding is applied | See [i.XML-ENCv1.1] |
| 7a | base64 encoding (see [9]) is applied on XML Encryption v1.1 Serialization for Encryption-Only ESData Security Class | See [i.XML-ENCv1.1] |
| 7b | base64 encoding (see [9]) applied on XML Encryption v1.1 Serialization for Signature-Only ESData Security Class | See [i.XML-SIGv1.1] |
| 7c | base64 encoding (see [9]) applied on XML Encryption v1.1 for Nested-Sign-then-Encrypt ESData Security Class | See [i.XML-ENCv1.1] |

### -----------------------End of change 0a ---------------

### -----------------------Start of change 1c  (new enumerated data type)---------------

##### 6.3.4.2.c m2m:suid

Used in m2m:e2eSecInfo and other security features in TS-0003 [7].

NOTE: This enumeration uses a structure with two identifiers separated by the ‘-‘ character. The first identifier identifies the origin of the symmetric key (such as pre-provisioning, provisioned via a RSPF, or distributed via MAF) and the intended scope within which the symmetric key is to be used (such as shared with an MEF, shared with an MAF, use in SAEF, use in ESPrim, use in authentication encryption in ESData, or use in signature only in ESData).

Table 6.3.4.2.c-1: Interpretation of suid

| Value | Interpretation | Note |
| --- | --- | --- |
| 0-0 | A pre-provisioned symmetric key intended to be shared with a MEF |  |
| 0-1 | A pre-provisioned symmetric key intended to be shared with a MAF |  |
| 0-2 | A pre-provisioned symmetric key intended for use in a Security Associated Establishment Framework (SAEF) |  |
| 0-3 | A pre-provisioned symmetric key intended for use in End-to-End Security of Primitives (ESPrim) |  |
| 0-4 | A pre-provisioned symmetric key intended for use with authenticated encryption in the Encryption-only or Nested Sign-then-Encrypt End-to-End Security of Data (ESData) Data classes |  |
| 0-5 | A pre-provisioned symmetric key intended for use in Signature-only ESData Security Class |  |
| 1-1 | A symmetric key, provisioned via a Remote Security Provisioning Framework (RSPF), and intended to be shared with a MAF |  |
| 1-2 | A symmetric key, provisioned via a RSPF, and intended for use in a SAEF |  |
| 1-3 | A symmetric key, provisioned via a RSPF, and intended for use in ESPrim |  |
| 1-4 | A symmetric key, provisioned via a RSPF, and intended for use with authenticated encryption in the Encryption-only or Nested Sign-then-Encrypt ESData) Data classes |  |
| 1-5 | A symmetric key, provisioned via a RSPF, and intended for use in Signature-only ESData Security Class |  |
| 2-2 | A MAF-distributed symmetric key intended for use in a SAEF |  |
| 2-3 | A MAF-distributed symmetric key intended for use in ESPrim |  |
| 2-4 | A MAF-distributed symmetric key intended for use with authenticated encryption in the Encryption-only or Nested Sign-then-Encrypt ESData Data classes |  |
| 2-5 | A MAF-distributed symmetric key intended for use in Signature-only ESData Security Class |  |
| NOTES: See TS-0003 [7] for further detail. |

### -----------------------End of change 1c-------------------------------------------

### -----------------------Start of change 2c (new complex data type)------------------

#### 6.3.5.y m2m:e2eSecInfo

Used for the e2eSecInfo attribute of the <CSEBase>, <AE> and <remoteSE> resources.

Table 6.3.5.y-1: Type Definition of m2m:e2eSecInfo

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| supportedE2ESecFeatures | List of m2m:suid | 1 | See clause 6.3.4.2.c |
| certificates | List of xs:base64Binary | 0..1 |  |
| sharedReceiverE2ERandObject | m2m:receiverE2ERandObject | 0..1 | See clause 6.3.5.x |

### -----------------------End of change 2d-------------------------------------------

### -----------------------Start of change 3a (clause 7.4.3.1)------------------------------

Table 7.4.3.1-2: Resource Specific Attributes of <CSEBase> resource

| Attribute Name | Data Type | Default Value and Constraints |
| --- | --- | --- |
| cseType | m2m:cseTypeID | No default |
| CSE-ID | m2m:ID | No default |
| supportedResourceType | list of m2m:resourceType | No default |
| pointOfAccess | m2m:poaList | No default |
| nodeLink | xs:anyURI | No default |
| e2eSecInfo | m2m:e2eSecInfo | No default |

### -----------------------End of change 2d-------------------------------------------

### -----------------------Start of change 3b (clause 7.4.3.1)------------------------------

Table 7.4.4.1-3: Resource Specific Attributes of <remoteCSE> resource

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | Create | Update |  |  |
| cseType | O | NP | m2m:cseTypeID | No default |
| pointOfAccess | O | O | m2m:poaList | No default |
| CSEBase | M | NP | xs:anyURI | No default |
| CSE-ID | M | NP | m2m:ID | No default |
| M2M-Ext-ID | O | O | m2m:externalID | No default |
| Trigger-Recipient-ID | O | O | m2m:triggerRecipientID | No default |
| requestReachability | M | O | xs:boolean | No default |
| nodeLink | O | O | xs:anyURI | No default |
| e2eSecInfo | O | O | m2m:e2eSecInfo | No default |

### -----------------------End of change 3b-------------------------------------------

### -----------------------Start of change 3c (clause 7.4.3.1)------------------------------

Table 7.4.5.1-3: Resource Specific Attributes of <AE> resource

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | Create | Update |  |  |
| appName | O | O | xs:string | No default |
| App-ID | M | NP | xs:string | No default |
| AE-ID | NP | NP | m2m:ID | No default |
| pointOfAccess | O | O | m2m:poaList | No default |
| ontologyRef | O | O | xs:anyURI | No default |
| nodeLink | NP | NP | xs:anyURI | No default |
| requestReachability | M | O | xs:boolean | No default |
| contentSerialization | O | O | m2m:serializations | No default |
| e2eSecInfo | O | O | m2m:e2eSecInfo | No default |

### -----------------------Start of change X TO DO-------------------------------------------

### Complex data types members

In protocol bindings complex data types member names shall be translated into short names of Table 8.2.5-1.

Table 8.2.5-1: Complex data type member short names

| Member Name | Occurs in | Short Name |
| --- | --- | --- |
| createdBefore | filterCriteria, eventNotificationCriteria | crb |
| createdAfter | filterCriteria, eventNotificationCriteria | cra |
| modifiedSince | filterCriteria, eventNotificationCriteria | ms |
| unmodifiedSince | filterCriteria, eventNotificationCriteria | us |
| stateTagSmaller | filterCriteria, eventNotificationCriteria | sts |
| stateTagBigger | filterCriteria, eventNotificationCriteria | stb |
| expireBefore | filterCriteria, eventNotificationCriteria | exb |
| expireAfter | filterCriteria, eventNotificationCriteria | exa |
| labels | filterCriteria, eventNotificationCriteria | lbl * |
| resourceType | filterCriteria | ty * |
| sizeAbove | filterCriteria, eventNotificationCriteria | sza |
| sizeBelow | filterCriteria, eventNotificationCriteriay | szb |
| contentType | filterCriteria | cty |
| limit | filterCriteria | lim |
| attribute | filterCriteria, eventNotificationCriteria | atr |
| notificationEventType | eventNotificationCriteria | net |
| operationMonitor | eventNotificationCriteria, notificationEvent | om |
| representation | notificationEvent | rep |
| filterUsage | filterCriteria | fu |
| eventCatType | eventCat | ect |
| eventCatNo | eventCat | ecn |
| number | batchNotify | num |
| duration | batchNotify | dur |
| notification | aggregatedNotification, Request Primitive Content | sgn |
| notificationEvent | notification | nev |
| verificationRequest | notification | vrq |
| subscriptionDeletion | notification | sud |
| subscriptionReference | notification | sur |
| creator | notification | cr* |
| notificationForwardingURI | notification | nfu* |
| operation | operationMonitor | op* |
| originator | operationMonitor | or* |
| accessId | externalID | aci |
| MSISDN | externalID | msd |
| action | actionStatus | acn |
| status | actionStatus | sus |
| childResource | All except execInstance, announced resource, management resources from firmware | ch |
| accessControlRule | privileges, selfPrivileges | acr |
| accessControlOriginators | accessControlRule | acor |
| accessControlOperations | accessControlRule | acop |
| accessControlContexts | accessControlRule | acco |
| accessControWindow | accessControlContexts | actw |
| accessControlIpAddresses | accessControlContexts | acip |
| ipv4Addresses | accessControlIpAddress | ipv4 |
| ipv6Addresses | accessControlIpAddress | ipv6 |
| accessControlLocationRegion | accessControlContexts | aclr |
| countryCode | accessControlLocationRegion | accc |
| circRegion | accessControlLocationRegion | accr |
| name | attribute, anyArgType, mgmtLinkRef, childResourceRef | nm* |
| value | attribute | val |
| type | anyArgType | typ |
| maxNrOfNotify | rateLimit | mnn |
| timeWindow | rateLimit | tww |
| scheduleEntry | scheduleElement | sce |
| aggregatedNotification | Request Primitive Content | agn |
| attributeList | Request Primitive Content | atrl |
| aggregatedResponse | Response Primitive Content | agr |
| resource | Response Primitive Content | rce |
| URIList | Response Primitive Content | uril |
| anyArg | resetArgsType, rebootArgsType, uploadArgsType, downloadArgsType, softwareInstallArgsType softwareUpdateArgsType, softwareUninstallArgsType, execReqArgsListType | any |
| fileType | downloadArgsType | ftyp |
| URI | resourceWrapper | uri |
| URL | downloadArgsType | url* |
| username | uploadArgsType, downloadArgsType, softwareUpdateArgsType, softwareUninstallArgsType, | unm |
| password | uploadArgsType, downloadArgsType, softwareUpdateArgsType, softwareUninstallArgsType, | pwd |
| filesize | downloadArgsType | fsi |
| targetFile | downloadArgsType | tgf |
| delaySeconds | downloadArgsType | dss |
| successURL | downloadArgsType | surl |
| startTime | downloadArgsType | stt |
| completeTime | downloadArgsType | cpt |
| UUID | softwareInstallArgsType softwareUpdateArgsType, softwareUninstallArgsType, | uuid |
| executionEnvRef | softwareInstallArgsType softawareUpdateArgsType, softwareUninstallArgsType, | eer |
| version | softwareUninstallArgsType | vr* |
| reset | execReqArgsListType | rst |
| reboot | execReqArgsListType | rbo* |
| upload | execReqArgsListType | uld |
| download | execReqArgsListType | dld |
| softwareInstall | execReqArgsListType | swin |
| softwareUpdate | execReqArgsListType | swup |
| softwareUninstall | execReqArgsListType | swun |
| tracingOption | dekiveryMetaData | tcop |
| tracingInfo | dekiveryMetaData | tcin |
| responseTypeValue | responseTypeInfo | rtv |
| notificationURI | responseTypeInfo | Nu |
| NOTE: * marked short names have been already assigned in attribute Table 8.2.3-1. |

### -----------------------End of change X -------------------------------------------

### ------------Add the following informative references to clause 2.2  -------------

[RFC4648]	IETF RFC 4648: “The Base16, Base32, and Base64 Data Encodings”, 2006

### ------------End of changes  to clause 2.2  -------------

### ------------Add the following informative references to clause 2.2  -------------

[i.XML-ENCv11]	W3C Recommendation “XML Encryption Syntax and Processing v1.1”, 2013, http://www.w3.org/TR/xmlenc-core1/

[i.XML-SIGv11]	W3C Recommendation “XML Signature Syntax and Processing v1.1”, 2013, http://www.w3.org/TR/xmlenc-core1/

[i.RFC7515]	IETF RFC 7515: “JSON Web Signature (JWS)”, 2015

[i.RFC7516]	IETF RFC 7516: “JSON Web Encryption (JWE)”, 2015

[i.RFC7518]	IETF RFC 7518: “JSON Web Algorithms (JWA)”, 2015

### ------------End of changes  to clause 2.2  -------------