| CHANGE REQUEST |
| --- |
| Meeting:* | PRO#21 |
| Source:* | Qualcomm Inc. (TIA) |
| Date:* | 2016-05-17 |
| Contact:* | Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com Nobu Uchida, Qualcomm, nuchida@qti.qualcomm.com |
| Reason for Change/s:* | Completion of WebSocket Binding specification |
| CR against: Release* | Release-2 |
| CR against: WI* | Active WI-0040 MNT Maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0020v0.4.0 |
| Clauses/Sub Clauses* | 2, 3, 4, 5, 6, 7, 8 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR is a mirror CR? YES NO if YES, please indicate the document number of the original CR: <Document Number)<CR Number of the original CR to the current Release> |
| Template Version:23 February 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR proposes following changes to the current draft version v0.4.0 of TS-0020:

- Minor editorial corrections

- Addressing open issues:  serialization formats, subprotocol negotiation.

NOTE:  the method proposed here, to select message serialization formats by means of  subprotocol-name negotiation is also applied by other WebSocket applications, see

The Web Application Messaging Protocol draft-oberstet-hybi-tavendo-wamp-02

This seems to be the most appropriate method.

- Adding text for currently empty sections “7 Security Aspects”

- Removing empty section  “8 Examples” and instead adding “Annex A (Informative) Example Procedures” with inclusion of one message flow example

- Addition of a normative Annex B on the (binary) CBOR serialization format (refer to PRO-2016-0086R01-WebSocket_OpenIssues  for a discussion on the gain of binary serialization and CBOR)

Revision R01:  Annex B and reference [8] added

### -----------------------Start of change 1-------------------------------------------

# Scope

The present document specifies the binding of Mca and Mcc primitives onto the WebSocket binding

It specifies:

- Procedures and message formats for operating and closing of WebSocket connections.

- How request and response primitives are mapped into the payload of the WebSocket protocol.

# References

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references,only the cited version applies. For non-specific references, the latest version of the referenced document (including any amendments) applies.

## Normative references

The following referenced documents are necessary for the application of the present document.

[1]	IETF RFC 6455: "The Web Socket Protocol", December 2011.

[2]	oneM2M TS-0001: "Functional Architecture".

[3]	IETF RFC 7230: "Hypertext Transport Protocol (HTTP/1.1): Message Syntax and Routing", June 2014.

[4]	oneM2M TS-0003: "Security Solutions".

[5]	oneM2M TS-0004: "Service Layer Core Protocol Specification".

[6]	IETF RFC 7692: "Compression Extensions for WebSocket", December 2015.

[7]	IETF RFC 7049: "Concise Binary Object Representation (CBOR)", October 2013.

[8]	IETF RFC 7159: "The JavaScript Object Notation (JSON) Data Interchange Format", March 2014.

## Informative references

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

- Use the EX style, add the letter "i" (for informative) before the number (which shall be in square brackets) and separate this from the title with a tab (you may use sequence fields for automatically numbering references).

[i.1]	oneM2M Drafting Rules  (http://member.onem2m.org/Static_pages/Others/Rules_Pages/oneM2M-Drafting-Rules-V1_0.doc)

# Definitions, symbols and abbreviations

Delete from the above heading the word(s) which is/are not applicable.

## Definitions

oneM2M WebSocket Client (WS Client): A WebSocket Client associated with an AE or a CSE capable of establishing the WebSocket connections.

oneM2M WebSocket Server (WS Server): A WebSocket Server associated with a CSE which accepts requests to establish WebSocket connections.

## Abbreviations

For the purposes of the present document, the following abbreviations apply:

AND	Application Dedicated Node

AE	Application Entity

ASN	Application Service Node

CBOR 	Concise Binary Object Representation

CSE	Common Services Entity

HTTP 	Hypertext Transport Protocol

IANA	Internet Assigned Numbers Authority

IETF	Internet Engineering Task Force

IN-CSE	Infrastructure Node Common Services Entity

IP	Internet Protocol

MN	Middle Node

MN-CSE	Middle Node Common Services Entity

TCP	Transmission Control Protocol

TLS	Transport Layer Security

URI	Uniform Resource Identifier

WS	WebSocket

# Conventions

The key words “Shall”, ”Shall not”, “May”, ”Need not”, “Should”, ”Should not” in this document are to be interpreted as described in the oneM2M Drafting Rules [i.1]

# Overview on WebSocket Binding

## Use of WebSocket

This binding makes use of the WebSocket protocol [RFC6455] to transport serialized representations of oneM2M request and response primitives over the Mca or Mcc reference points.

Establishment of a WebSocket connection shall be initiated by a WebSocket client by sending a handshake to a WebSocket server as specified in section 4 of IETF RFC6455[1]. Once the WebSocket connection is established, both oneM2M request and response primitives can be exchanged bi-directionally between the two endpoints of the connection. Serialized representations of the request and response primitives shall be mapped in the Payload Data field of the WebSocket base framing protocol, as defined in section 5.2 of IETF RFC6455[1].

A WebSocket connection employs either a TCP/IP or a TLS over TCP/IP connection. The underlying TCP and TLS connections are established as the first step of the WebSocket handshake.

## Binding Overview

WebSocket binding may be employed for communication between any two endpoints which can be connected over the Mca, Mcc or Mcc’ interface reference points supported by the oneM2M Architecture as shown in figure 6.1-1 of oneM2M TS-0001 [2].

When using the WebSocket protocol, one communication endpoint shall act as the WebSocket server. The WebSocket server listens for inbound handshake messages arriving from any WebSocket client to which a WebSocket connection is not yet established. Whether a communication endpoint takes the role of the client or the server shall depend on the registration relationship between the communicating entities as follows: the registree shall always use a WebSocket client, while the associated registrar shall always use a WebSocket server on the respective reference point.

This implies that ADN and ASN always take the role of a WebSocket client when WebSocket binding is employed. An MN-CSE uses a WebSocket server to communicate with its registrees and a WebSocket client to communicate with its own registrar (which can be another MN-CSE or an IN-CSE).

The IN-CSE provides a WebSocket server functionality to communicate with all its registrees, i.e. within a service provider’s domain.  On the Mcc’ reference points, i.e. for communication between IN-CSEs of different Service Provider domains, the IN-CSE shall provide both WebSocket client and server functionality. This enables any IN-CSE to open a WebSocket connection to any IN-CSE of another Service Provider’s domain.

Figure 5.2-1 shows some applicable example system configuration.

There exists a maximum of one WebSocket connection between two nodes. A WebSocket connection is established for the first time when the initial registration procedure of an entity to its registrar is performed. On an established WebSocket connection, request and response primitives can be exchanged in both directions. Any connection may be closed by either the WebSocket client or the server, depending on the communication schedule of either entity. However, the connection can be reopened from the client side only.

If the connection is closed temporarily, it  shall be reopened when the next request primitive is sent from the client to the server side, or when the time to become reachable configured at <schedule> resource. If the WebSocket connection with the next-hop entity is not opened, and the WebSocket connection cannot be established due to lack of pointOfAccess address for the entity, a sending CSE shall buffer primitives which should be sent to the entity until the connection is reopened or their expiration time is reached.

Editor’s note: buffering should be handled by the service layer (i.e. CSE) and this feature should apply independent of the binding protocol and be properly specified in oneM2M TS-0001[2]. Therefore we should consider to remove mentioning of buffering in this document.

Figure 5.2-2 shows an example message flow for a scenario where an ADN-AE registers to its registrar MN-CSE using an unsecured TCP connection without proxy and then continues exchanging non-registration request and response primitives.

- The ADN-AE wants to register to its registrar MN-CSE. If a WebSocket connection does not exist, it is established by the following steps 2) and 3). It is assumed that the ADN-AE knows the point of access (i.e. WebSocket URI specified in IETF RFC6455 [1]) under which the registrar CSE can be reached with WebSocket binding.

- The WebSocket client shall open handshake to the server with subprotocol name 'oneM2M-pro-v1.0' following IETF RFC6455 [1]. 
If the server can be reached under the WebSocket URI ws://example.net:9000/, the client handshake may look as follows:

GET / HTTP/1.1

Host: mncse1234.net:9000

Upgrade: WebSocket

Connection: Upgrade

Sec-WebSocket-Key: ud63env87LQLd4uIV20/oQ==
Sec-WebSocket-Protocol: oneM2M-pro-v1.0

Sec-WebSocket-Version: 13

- The WebSocket server shall reply with a handshake to the client. In the successful case, the status-line of this HTTP response may look as follow:

Request-Version:  HTTP/1.1

Status-Code: 101

Response-Phrase: Switching Protocols

Upgrade: WebSocket

Connection: Upgrade

Sec-WebSocket-Protocol: oneM2M-pro-v1.0

Sec-WebSocket-Accept: FuSSKANnI7C/6/FrPMt70mfBY8E=

- The ADN-AE shall issue a registration request primitive. The request primitive may e.g. look as follows as JSON-serialized representation:

{"m2m:rqp":{"op":1,"to":"//example.net/mncse1234","rqi":"A1234","pc":{"m2m:ae":{"api":"a56", "apn":"app1234"}},"ty": 2}}

NOTE: The WebSocket client associated with an ADN-AE does not need to be reachable for WebSocket Server handshake messages.

- WebSocket Binding process, which transforms a single oneM2M primitive into one or more data frames of the WebSocket Framing protocol, as specified in IETF RFC6455 [1]. When transmitting a JSON-serialized primitive in utf-8 text format, the 4-bit opcode in the WebSocket Base Framing Protocol of the first message fragment shall be set to x1 (“text frame”).

- The WebSocket message (consisting of one or more frames) shall be sent to the WS server.

- The original request primitive shall be unpacked from the WebSocket message by the WS server.

- The request primitive shall be delivered to the MN-CSE.

- The MN-CSE shall perform the receiver side operations of AE registration as specified in oneM2M TS-0001[2].

- The response primitive shall be issued to the WebSocket server.

- WebSocket binding process for the response primitive shall be performed.

- The WebSocket message (consisting of one or more frames) shall be sent to the client.

- The response primitive shall be unpacked.

- The response primitive shall be delivered to the ADN-AE.

- After successful completion of AE registration any other CRUDN requests and response primitives can be exchanged over the existing WebSocket connection in both directions. If the AND-AE has no other requests to send, the WebSocket connection may be closed temporarily. When the WebSocket connection is closed after registration and reopened later again, the registration procedure as outlined in steps 4 to 14 is omitted. In this case any non-registration request primitives can be sent directly.

# Protocol Binding

## Introduction

The WebSocket protocol enables two-way communication between client and server even when a firewall and/or NAT are present between them. This means, once a WebSocket connection is established, request (and response) primitives can be exchanged in both directions, from the client to the server and vice versa. However, AEs may be capable of handling Notification request primitives only, or no request primitives at all.

WebSocket binding applied by oneM2M entities/nodes shall be fully compliant with IETF RFC 6455 [1]. After establishment of a WebSocket connection between two nodes, at the transmitter side each individual request and response primitive is mapped into one or several WebSocket frames.

## WebSocket connection establishment

### General

A WebSocket connection is opened by the client side as specified in section 4 of  IETF RFC 6455 [1] with sending of a client handshake. The server responds with a server handshake.

The client handshake consists of an HTTP upgrade request, along with a list of required and optional header fields.

The handshake shall be a valid HTTP request as specified by IETF RFC7230 [3]. The server handshake consists of a HTTP status-line and a list of header fields.

The applicable format of the request-line, status-line and the applicable header fields are specified in the following subsections.

HTTP headers fields have case-insensitive field names.

CSEs capable to support WebSocket shall indicate the schemes ws and/or wss  together with the applicable host name and port numbers in the pointOfAccess attribute of their <CSEBase> resource, i.e. as ws://host:port1 and wss://host:port2.

### Client handshake

#### Format of request-line

The request-line of a client handshake shall begin with the method token “GET”, followed by the request target “/” and the HTTP version set to “HTTP/1.1” as follows:

GET / HTTP/1.1

If the client is configured to use a proxy when using the WebSocket Protocol, a connection to the proxy server shall be established prior to sending the above client handshake. This is described in clause 5.5.

#### Host header

The Host header shall be present in each client handshake.

The Host header indicates the FQDN or IP address of the Receiver CSE of the next hop. If the originator of the client handshake is an oneM2M field entity, the host header represents the registrar CSE of the originator.

When no proxy is used, the Host header shall be set as one of the pointOfAccess attribute values associated with the Receiver. Selection of the appropriate Receiver is described in oneM2M TS-0004 [5].

If the client is configured to use a proxy when using the WebSocket Protocol, then the client should connect to that proxy and ask it to open a TCP connection to the host and  port rather than to the next hop CSE,

Editor’s Note: request line format when using proxy needs more study

#### Upgrade header

The Upgrade header shall be present in each client handshake message with value WebSocket as follows:

Upgrade: WebSocket

#### Connection header

The Connection header shall be present in each client handshake message with value Upgrade as follows:

Connection: Upgrade

#### Sec-WebSocket-Key header

The Sec-WebSocket-Key header shall be present in each client handshake message. The header field includes a base64-encoded representation of a random 16 bytes pattern, for example:

Sec-WebSocket-Key: ud63env87LQLd4uIV20/oQ==

#### Sec-WebSocket-Version header

The Sec-WebSocket-Version header shall be present in each client handshake message with value 13 as follows:

Sec-WebSocket-Version: 13

#### Sec-WebSocket-Protocol header

The Sec-WebSocket-Protocol header shall be present in a client handshake message. It enables the client to indicate its supported application subprotocols on the server and be sure that the server agreed to support that subprotocol. It is used by the client to indicate the oneM2M Service Layer Protocol version and supported serialization formats to the server.

The value of the Sec-WebSocket-Protocol header shall be one or more of the registered names defined in clause5.2.2.9. It shall also be allowed to include multiple Sec-WebSocket-Protocol headers with a value that includes one registered name each as defined in IETF RFC6455[1], for example

Sec-WebSocket-Protocol:   oneM2M.R2.0.JSON, oneM2M.R2.0.XML

and

Sec-WebSocket-Protocol:   oneM2M.R2.0.XML

Sec-WebSocket-Protocol:   oneM2M.R2.0.JSON

are equivalent headers, expressing that the WebSocket client supports both application subprotocols, oneM2M.R2.0.XMLand oneM2M.R2.0.XML. The order of names indicated in the Sec-WebSocket-Protocol header specifies the client’s preference.

Editor’s Note:  Subprotocol names need to be registered in the IANA WebSocket Protocol registry https://www.iana.org/assignments/websocket/websocket.xhtml#subprotocol-name

#### Sec-WebSocket-Extensions header

The Sec-WebSocket-Extensions header may be used to negotiate the use of per-message compression as specified in RFC 7692 [6].

If the client handshake includes the header, e.g.

Sec-WebSocket-Extensions: permessage-deflate

it indicates to the server the client’s preference to apply the compression mechanism defined in RFC 7692 [6]. The header may include additional parameters as specified in [6].

When the server accepts use of message compression it responds with a Sec-WebSocket-Extensions header in the server handshake message as specified in clause 7.2.3.6, and in this case compression is applied in both transmission directions. If the server handshake message does not include a Sec-WebSocket-Extensions header, compression shall not be applied.

#### Subprotocol names and serialization formats

The Sec-WebSocket-Protocol header in the opening handshake is used to negotiate the application protocol layered on top of WebSocket. The application protocol addressed in this specification is the Release-2 version of the oneM2M Service Layer.

The oneM2M Service Layer Protocol consists of the exchange of serialized representations of  request and response primitives as defined in TS-0001 [2] and TS-0004 [5]. This version of the specification allows use of the serialization formats listed in Table 7.2.2.9-1. Both, protocol version and serialization format are associated with a specific subprotocol name.

Table 7.2.2.9-1 lists the serialization formats, associated subprotocols names and opcode setting of the WebSocket Frame protocol applicable for the present version of this specification.

Table 7.2.2.9-1: Applicable Subprotocol names

| Serialization Format | Subprotocol Name | WS opcode | Notes |
| --- | --- | --- | --- |
| JSON | oneM2M.R2.0.json | x1 (“text frame”) | See clause 8.4 in TS-0004 [5] |
| XML | oneM2M.R2.0.xml | x1 (“text frame”) | See clause 8.3 in TS-0004 [5] |
| CBOR | oneM2M.R2.0.cbor | x2 (“binary frame”) | See RFC7049 [7] and Annex B |

### Server handshake format

#### Format of status-line

The status-line of a server handshake shall begin with the HTTP version set to “HTTP/1.1”, followed by the status code and reason phrase as defined in IETF RFC6455[1]. When the WebSocket connection is established successfully, the status-line may look as follows:

HTTP/1.1 101 Switching Protocols

In the unsuccessful any appropriate HTTP error status code shall be returned with optional addition of a corresponding reason phrase.

#### Upgrade header

The Upgrade header shall be present in each server handshake message with value WebSocket as follows:

Upgrade: WebSocket

#### Connection header

The Connection header shall be present in each server handshake message with value Upgrade as follows:

Connection: Upgrade

#### Sec-WebSocket-Accept header

The Sec-WebSocket-Accept header shall be present in each server handshake message. The header field shall be constructed from the Sec-WebSocket-Key value and the GUID as specified in section 4.2.2 of IETF RFC6455 [1]. It may look e.g. as follows:

Sec-WebSocket-Accept: FuSSKANnI7C/6/FrPMt70mfBY8E=

#### Sec-WebSocket-Protocol header

The Sec-WebSocket-Protocol header shall be present in a server handshake message. It indicates to the client that the server accepts (one of) the subprotocol(s) indicated by the client.

The server compliant with this specification shall select one of the subprotocol names indicated in the Sec-WebSocket-Protocol header of the client handshake message and set the value of the Sec-WebSocket-Protocol header of the server handshake message accordingly.

#### Sec-WebSocket-Extensions header

If the optional Sec-WebSocket-Extensions header with value “permessage-deflate” was included in the client handshake message, the Sec-WebSocket-Extensions header with same value shall also be included into the server handshake message, if the server accepts usage of message compression, and apply message compression in the transmit direction and message decompression in the receive direction as defined in RFC7692 [6].

If the server does not accept message compression, it shall not include the Sec-WebSocket-Extensions header.

## Closing WebSocket connection

Compliant with section 7 of RFC6455[1] a WebSocket connection shall be closed by sending a Connection Close Frame (opcode x8). Both, client and server may initiate a closing handshake of an existing WebSocket connection at any time.

WebSocket connections should be kept open for as long as possible considering any given constraints due to communication policies and power saving requirements. Unless communication policies enforce the closing of network access, it is left to implementation to decide when exactly the closing of a WebSocket shall be triggered. However, the further requirements and recommendations specified in clause 7.5 apply.

## Registration procedure

A oneM2M entity (AE or CSE) not yet registered to its registrar CSE needs to be preconfigured with various parameters as specified in oneM2M TS-0001 [2] and oneM2M TS-0003 [4] in order to be able to send the registration request primitive (i.e. create <AE> or create <remoteCSE> request primitive). To establish a WebSocket connection, the WebSocket client must be configured with an applicable point of access of its registrar CSE which includes FQDN or IP address and the port number.

After the Registration procedure has been successfully completed, the WebSocket Server (e.g. Registrar CSE for WebSocket Client) shall enable routing of any incoming oneM2M primitives to this registree.

Thus until the Before the Registration procedure is successfully completed, any incoming oneM2M primitives to the WebClient shall be rejected by the Receiver (e.g. registrar CSE).

Closing of the WebSocket connection after registration does not impact the registration status of an AE or CSE to its registrar, unless an explicit de-registration procedure is performed by deletion of the respective <AE> or <remoteCSE> resource instance.

## Handling of Non-Registration Request

Registered entities (AE and CSE) are allowed to send and receive non-registration request primitives. A WebSocket connection should support any of the transfer modes defined in clause 8.2 of oneM2M TS-0001 [2], i.e. blocking requests, and non-blocking requests for both synchronous and asynchronous cases.

When sending blocking requests, the WebSocket connection shall not be closed before the response is received, or before any configured timeout period has expired.

When sending non-blocking requests, the WebSocket connection shall not be closed before the acknowledgment response is received, or before any configured timeout period has expired. If the entities’ communication policies and power saving requirements allow, the connection should be kept open at least until an ongoing procedure has fully completed, i.e. requesting of the result in synchronous mode or completion of Notify procedure in asynchronous mode.

## Use of proxy servers

The connection to a proxy shall be requested by sending a request-line with the method token “CONNECT”, followed by the request target host and port of the WebSocket server and the HTTP version set to “HTTP/1.1” as follows:

CONNECT WSserver.example.com:80 HTTP/1.1

Editor's Note: More text to be added!!

# Security Aspects

## Authentication and Transport Layer Security can be established when the oneM2M entity which hosts the WebSocket Server can be addressed with the wss URI scheme. When using the wss URI scheme, one of the Security Association Establishment Frameworks (SAEF) as defined in TS-0003 [4] shall be applied to provide mutually authenticated Transport Layer Security between the communicating entities prior to sending the WebSocket client handshake.

## The SAEF is accomplished by successful completion of a TLS handshake procedure before the client sends its opening handshake message. The details of SAEF and possibly required Remote Security Provisioning Frameworks are specified in TS-0003 [4].

## In special deployment scenarios, e.g. when the communicating oneM2M entities using WebSocket binding are located in a secure environment and/or implemented on the same device, Transport Layer Security may not be required. In such scenarios unsecured WebSocket communication addressed with the ws URI scheme may be adequate.

## Editor’s note: There might be other scenarios, i.e. where Dynamic Authorization and/or End-to-End Security is employed, where use of Transport Layer Security may not be required. We could add descriptions of such use cases.

Annex <A> (Informative): Example Procedures

# A.1	AE Registration and creation of a Container child resource

Figure A.1-1 illustrates a message flow for registration of an ADN-AE to an IN-CSE as described in clause 7.3.5.2.1 of TS-0004 [5] with WebSocket mapping and subsequent creation of a <Container> child resource.

In the considered example, the WebSocket protocol is used to send JSON serialized request and response primitives in text format.

The message flow may look as follows:

- TCP connection establishment and Security Association Establishment as defined in TS-0003 [4] based on TLS handshake procedure is accomplished.

- The WSS client sends e.g. the following opening handshake message, offering to use either JSON or XML serialization of primitives:

- GET / HTTP/1.1

- Host: mncse1234.net:9000

- Upgrade: WebSocket

- Connection: Upgrade

- Sec-WebSocket-Key: ud63env87LQLd4uIV20/oQ==
        Sec-WebSocket-Protocol: oneM2M.R2.0.json, oneM2M.R2.0.xml

Sec-WebSocket-Version: 13

- The WSS server selects use of JSON serialization and responds the following handshake message:

- Request-Version:  HTTP/1.1

- Status-Code: 101

- Response-Phrase: Switching Protocols

- Upgrade: WebSocket

- Connection: Upgrade

- Sec-WebSocket-Protocol: oneM2M.R2.0.json

- Sec-WebSocket-Accept: FuSSKANnI7C/6/FrPMt70mfBY8E=

- The AE sends the following request primitive in textual JSON serialized format

- {"m2m:rqp":{"op":1,"to":"//example.net/mncse1234","rqi":"A1000", "rcn":7,"pc":{"m2m:ae":{"rn":"SmartHomeApplication", "api":"Na56", "apn":"app1234"}},"ty":2}}

- The above JSON object is mapped by the WS client into a data frame of the WebSocket Framing protocol in utf-8 text format, the 4-bit opcode in the WebSocket Base Framing Protocol of the first message fragment is set to x1 (“text frame”).

- The IN-CSE validates the privilege of the originator to create an <AE> resource, and accepts the request to create the resource.

- The IN-CSE acknowledges the success of the request by responding the following JSON serialized response primitive. The response primitive includes all attributes of <AE> instance created in Step 5.

- {"m2m:rsp":{"rsc":2001,"rqi":"A1000","pc":{"m2m:ae":{"rn":"SmartHomeApplication","ty":2,"ri":"ae1","api":"Na56","apn":"app1234","pi":"cb1","ct":"20160506T153208", "lt":"20160506T153208","acpi":["acp1","acp2"],"et":"20180506T153208", "aei":"S_SAH25"}}}}

- The above JSON object is mapped by the WS server into a data frame of the WebSocket Framing protocol in utf-8 text format, the 4-bit opcode in the WebSocket Base Framing Protocol of the first message fragment is set to x1 (“text frame”).

- The AE sends in textual JSON serialized format the following request primitive to create a <Container> resource as child resource of the <AE> created in Step 5:

{"m2m:rqp":{"op":1,"to":"//example.net/mncse1234/SmartHomeApplication", "rqi":"A1001","rcn":7,"pc":{"m2m:cnt":{"rn":"SmartHomeContainer","mbs":100000, "mni":500}},"ty":3}}

The above JSON object is mapped by the WS client into a data frame of the WebSocket Framing protocol in utf-8 text format, the 4-bit opcode in the WebSocket Base Framing Protocol of the first message fragment is set to x1 (“text frame”).

- The IN-CSE validates the privilege of the originator to create an <Container> resource under the <AE> resource created in step 5, and accepts the request to create the resource.

- The IN-CSE acknowledges the success of the request by responding the following JSON serialized response primitive

- {"m2m:rsp":{"rsc":2001,"rqi":"A1001","pc":{"m2m:cnt":{"rn":"SmartHomeContainer", "ty":3,"ri":"cnt1","pi":"ae1","ct":"20160506T154048", "lt":"20160506T154048","acpi":["acp1"],"et":"20180506T154048","cr":" S_SAH25","st":0,"mni":500,"mbs":100000,"cni":0,"cbs":0,"mia":3600}}}}

The above JSON object is mapped by the WS server into a data frame of the WebSocket Framing protocol in utf-8 text format, the 4-bit opcode in the WebSocket Base Framing Protocol of the first message fragment is set to x1 (“text frame”).

- Primitives of further subsequent CRUDN procedures may be transferred on the existing WebSocket connection.

# Annex <B> (Normative): CBOR serialization

B.1		CBOR encoding rules

Concise Binary Object Representation (CBOR) is a binary serialization format of structured data specified in RFC7049 [7]. CBOR provides unambiguous encoding of structured data into a binary representation and reverse decoding.

This Annex defines the relationship between JSON objects as defined in clause 8.4 of TS-0004 [5] and CBOR representations.

JSON objects are data structures represented as a pair of curly brackets surrounding zero or more name/value pairs (referred to as members). A name is a string. A single colon comes after each name, separating the name from the value. A single comma separates a value from a following name, see RFC7159 [8]. Clause 8.4 of TS-0004 [5] defines how oneM2M primitives which are constrained by an underlying XML schema definition (XSD) shall be encoded as JSON objects. Note that the XSD imposes constraints onto the JSON representations which do not generally apply. One such constraint is that JSON serializations of oneM2M primitives have unique member names.

In computer programming, the abstract data type equivalent to a JSON object is referred to as Associative Array. An Associative Array (in some programming languages also called map, symbol table, hash, or dictionary) is an abstract data type composed of a collection of key/value pairs, such that each possible key appears just once in the collection.

JSON objects and Associative Arrays can be nested, i.e. any value of a JSON member or Associative Array can be itself a JSON object or Associative Array, respectively.

Furthermore, any value of a JSON member or Associative Array may represent a single individual value of a given data type (i.e. UTF-8 encoded string or number), or an array (also called list, sequence, or tuple) of values. Note that due to constraints imposed by the XSD of oneM2M primitives, all elements of an array have the same data type which is associated with the name (key) of the array.

Section 2 of RFC7049 [7] specifies the applicable CBOR encoding rules.

In particular, the following rules shall apply when using CBOR serialization for this WebSocket binding:

- Text strings (i.e. any names/keys and text string values) shall be encoded as UTF-8 strings, CBOR major type 3.

- Integer numbers shall be encoded as CBOR major types 0 or 1.

- Floating point numbers shall be encoded as CBOR major type 7 with Additional Information 26 for single precision (32-bit) and Additional Information 27 for double precision (64-bit) formats.

Note that CBOR ignores whitespace characters (including space, LF/CR) if used for formatting of JSON objects in textual representations.

Editor’s Note: It needs to be reviewed if there are any CBOR aspects which need to be further clarified in this specification to enable platform-independent encoding and decoding.

If decoding of CBOR serializations results in values not compliant with the underlying XSD, this shall be interpreted as an error by the receiver of the primitive.

# B.2  	Examples

This clause presents some examples of CBOR serialized primitives. Note that due to given encoding options, a CBOR encoder may produce somewhat different binary serializations. However, in any case the CBOR decoding shall produce an equivalent representation in JSON format as shown in the examples below.

Example 1:

JSON representation (request primitive used in step 4 of message flow in Annex A.1, length: 173 bytes):

{"m2m:rqp":{"op":1,"to":"//example.net/mncse1234","rqi":"A1000", "rcn":7,"pc":{"m2m:ae":{"rn":"SmartHomeApplication", "api":"Na56", "apn":"app1234"}},"ty":2}}

CBOR representation as sequence of hexadecimal characters (length: 117 bytes):

a1476d326d3a727170a6427063a1466d326d3a6165a342726e54536d617274486f6d654170706c69636174696f6e43617069444e6135364361706e47617070313233344274790242746f572f2f6578616d706c652e6e65742f6d6e637365313233344372636e07426f700143727169454131303030

Example 2:

JSON representation (response primitive used in step 6 of message flow in Annex A.1, length: 234 bytes):

{"m2m:rsp":{"rsc":2001,"rqi":"A1000","pc":{"m2m:ae":{"rn":"SmartHomeApplication","ty":2,"ri":"ae1","api":"Na56","apn":"app1234","pi":"cb1","ct":"20160506T153208", "lt":"20160506T153208","acpi":["acp1","acp2"],"et":"20180506T153208", "aei":"S_SAH25"}}}}

CBOR representation as sequence of hexadecimal characters (length: 187 bytes):

a1476d326d3a727370a3427063a1466d326d3a6165ab43617069444e6135364361706e47617070313233344265744f3230313830353036543135333230384263744f3230313630353036543135333230384274790242726943616531426c744f3230313630353036543135333230384361656947535f534148323542726e54536d617274486f6d654170706c69636174696f6e427069436362314461637069824461637031446163703243727169454131303030437273631907d1

Example 3:

JSON representation (request primitive used in step 7 of message flow in Annex A.1, length: 187 bytes):

{"m2m:rsp":{"rsc":2001,"rqi":"A1000","pc":{"m2m:ae":{"rn":"SmartHomeApplication","ty":2,"ri":"ae1","api":"Na56","apn":"app1234","pi":"cb1","ct":"20160506T153208", "lt":"20160506T153208","acpi":["acp1","acp2"],"et":"20180506T153208", "aei":"S_SAH25"}}}}

CBOR representation as sequence of hexadecimal characters (length: 133 bytes):

a1476d326d3a727170a6427063a1476d326d3a636e74a3436d6e691901f442726e52536d617274486f6d65436f6e7461696e6572436d62731a000186a04274790342746f582c2f2f6578616d706c652e6e65742f6d6e637365313233342f536d617274486f6d654170706c69636174696f6e4372636e07426f700143727169454131303031

Example 4:

JSON representation (response primitive used in step 9 of message flow in Annex A.1, length: 306 bytes):

{"m2m:rsp":{"rsc":2001,"rqi":"A1001","pc":{"m2m:cnt":{"rn":"SmartHomeContainer", "ty":3,"ri":"cnt1","pi":"ae1","ct":"20160506T154048", "lt":"20160506T154048","acpi":["acp1"],"et":"20180506T154048","cr":" S_SAH25","st":0,"mni":500,"mbs":100000,"cni":0,"cbs":0,"mia":3600}}}}

CBOR representation as sequence of hexadecimal characters (length: 197 bytes):

a1476d326d3a727370a3427063a1476d326d3a636e74af436362730042726944636e7431436d6e691901f442637247535f53414832354265744f3230313830353036543135343034384263744f323031363035303654313534303438436d62731a000186a042747903436d6961190e1042737400426c744f32303136303530365431353430343842726e52536d617274486f6d65436f6e7461696e657242706943616531446163706981446163703143636e690043727169454131303031437273631907d1

7Annex <y>:
Bibliography

The annex entitled "Bibliography" is optional.

It shall contain a list of standards, books, articles, or other sources on a particular subject which are not mentioned in the document itself

It shall not include references mentioned in the document.

Use the Heading 9 style for the title and B1+ or Normal for the text.

- <Publication>: "<Title>".

OR

<Publication>: "<Title>".

<PAGE BREAK>

### -----------------------End of change 1-------------------------------------------

# Text boxes

Figure 5.2-1: Example scenarios of WebSocket client and server configurations

AE

WS

Client

CSE

WS

Server

WS

Client

AE

CSE

WS

Client

AE

AE

WS

Client

CSE

WS

Client

AE

CSE

WS

Server

WS

Client

AE

CSE

WS

Server

WS

Client

ADN

ASN

ADN

MN

MN

ASN

IN

Mcc’

Mcc

Mca

Mcc

Mca

Mcc

Figure 5.2-2: Example message flow with Websocket binding

AE

WS client

c

client

CSE

WS server

c

client

ADN

MN

- AE wants to start registration procedure and triggers WebSocket connection establishment

- Client handshake

- Server handshake

- Request primitive

- WebSocket Binding

- WebSocket message

- Unpacking request primitive

- Request primitive

- Receiver side processing of AE registration procedure

- Response primitive

- WebSocket Binding

- WebSocket message

- Unpacking response primitive

- Response primitive

- non-registration CRUDN operations